## Slide 1: PowerPoint 10: Incidents and near misses
PowerPoint presentation
1. Health and safety in building services engineering
1.10 Reporting and recording of safety incidents and near misses

## Slide 2: Objectives
By the end of the session learners should be able to:
  explain the correct procedure for recording an accident in an accident book
  explain what an accident reporting policy is
  understand the requirements for reporting RIDDOR incidents.

## Slide 3: Accident reporting
All accidents on a construction site or in your place of work must be recorded in an accident book. This is a requirement of the Health and Safety at Work Act (HASAWA) 1974. Usually the site manager/foreman or your employer will be in charge of the accident book and of completing it correctly. The following details are required as a minimum:
  name, address and occupation of injured person
  dated signature, address and occupation of the person making the entry
  brief description of the accident, cause and what injury occurred
  whether the accident needs to be reported to the Health and Safety Executive (HSE).

## Slide 4: Accident Reporting
Many companies have an accident reporting policy which provides guidance and timelines on how and when to report an accident.
For example, what are the procedures for someone who suffers a minor injury, such as a small cut, as opposed to someone who suffers a major injury, such as a broken leg and has to have significant time off work?
The accident reporting policy also provides guidance on near misses and other potential hazard reporting.

## Slide 5: Accidents that must be reported to the HSE
There are some accidents that must be reported to the HSE for monitoring purposes or to aid in any investigation of the accident. The HSE will, if required by law, complete such an investigation.
You/your employer must report:
  all accidents that cause death or major injury to an employee or member of the public
  any major injury (defined as certain fractures, amputations, loss of sight or anything that requires hospital treatment for more than 24 hours).

## Slide 6: Accident investigation
All accidents that occur in the workplace, whether fatal or otherwise, must be investigated to prevent them happening again.
The following people may be involved in an investigation:
  the employer
  an investigator from an insurance company, acting on behalf of the employer or employee
  a safety representative, usually from a trade union
  a health and safety inspector from the local authority or the HSE.

## Slide 7: RIDDOR
The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR) 2013 apply to all work activities.
The regulations place a legal duty on an employer in control of work premises to report certain work-related incidents, diseases and dangerous occurrences. RIDDOR applies to all work activities, however, not all incidents are reportable.

## Slide 8: RIDDOR reportable incidents
  Death.
  Major injury.
  Where an employee or self-employed person is away from work or unable to perform their normal work activities for more than 3 consecutive days due to the injury.
  Injuries to members of the public or people not at work, where they are taken from the scene of an accident to hospital.
  Certain work-related diseases.
  Dangerous occurrences – where something happens that does not result in an injury but may have done.

## Slide 9: RIDDOR reportable incidents
  In addition:
  Gas Safe registered gas engineers must report any dangerous gas installations/fittings they encounter
  gas transporters/suppliers must report flammable gas incidents.

## Slide 10: Accidents and near misses
The definition of an ‘accident’ is:
  An incident that happens unexpectedly and unintentionally resulting in damage or injury to something or someone.
  The definition of a ‘near miss’ is.
  A near miss is an unplanned event that has the potential to cause but does not actually result in damage or injury to something or someone.
  However, both of the above occurrences should be recorded in order to bring about a learning culture.

## Slide 11: Near misses
  A near miss can be defined as an unplanned/unwanted event that did not cause harm but had the potential to cause injury, ill health or property damage. The Health and Safety Executive (HSE) includes dangerous occurrences as near misses. Near misses are discussed at safety committees in order to stop incidents becoming accidents.
  The following are examples of near misses:
  slip or a trip in the workshop
  narrow escape: something falls from above and nearly hits you
  nearly falling from a damaged ladder
  nearly tripping over a coiled extension lead on the floor.

## Slide 12
Any questions?