## Slide 1: PowerPoint 5: Safe systems of work
PowerPoint presentation
1. Health and safety in building services engineering
1.4 Development of safe systems of work

## Slide 2: Objectives
  By the end of the session, learners should be able to:
  state how safe systems of work are developed and used
  understand the implications of not having safe systems of work in place
  complete risk assessments, method statements and COSHH assessments
  understand how to apply Construction Design and Management (CDM)
  understand the requirements for site signage
  state the different levels of the Construction Skills Certification Scheme (CSCS, SMSTS, SSSTS)
  understand the safe isolation of the different systems encountered in the BSE sector.

## Slide 3: Safe systems at work
A safe system of work is a procedure to eliminate the risks that are involved in a specific operation. The priority of a safe system of work is to eliminate any risks involved with the work.
In this presentation we look at how following the risk assessment process can reduce risks on site and ensure safe systems of work.
It is vital that safe systems and practices are adhered to so that everyone is working to the same high safety standards at all times.
Without these systems in place, accidents might occur that could cause injury or death.

## Slide 4: Method statements
A method statement documents the logical process of how an operative intends to complete a task safely.
It should complement an associated risk assessment and be written to negate any risks identified when completing any task.
The method statement should provide logical steps and specific actions on how to complete the task, ensuring safety at all times.
It also documents what control measures, personal protective equipment (PPE) or other safety resources are required so that the task can be completed safely.

## Slide 5: Method statements
Method statements form part of the overall safety plan and any risk assessment.
Such statements are written after the risk assessment has been undertaken.

## Slide 6: Risk assessments
A risk assessment needs to be completed in order to:
  back up a manufacturer’s data sheet for the Control of Substances Hazardous to Health Regulations (COSHH)
  assess various activities carried out by employees.
  As an employee, you must assess the risk to yourself and others when work is being carried out. This is the essence of working safety. After a risk assessment has been completed, it will, at minimum, result in the use of PPE and the presence of a first-aid kit. However, the more risk is identified in the assessment, the more mitigation processes need be in place to protect operatives and anyone else who may be affected by the work being completed.

## Slide 7: The five steps
There are five steps to a risk assessment:
Look for hazards.
Decide who or what might be harmed.
Evaluate the risks, present precautions and act when needed.
Record your findings.
Review and revise your findings regularly.
The Management of Health and Safety at Work Regulations 1999 legally require employers to make decisions about the hazards, significant or otherwise, faced in the workplace.

## Slide 8: Risk assessment: key definitions
Accident: an unplanned, undesired occurrence which may result in harm or loss.
Hazard: anything that has the potential to cause loss or harm.
Risk: how likely is it that a hazard will actually cause harm or loss?
When a risk assessment is put together, you have to identify the work hazard and calculate the likelihood of an accident happening. In this way you identify the risk rating.

## Slide 9: Risk assessment
Risk rating
Value of likelihood X Value of consequence
No likelihood 0 No injury or loss 0
Very unlikely 1 First aid 1
Unlikely 2 Up to 3 days off work 2
Likely 3 Over 3 days off work 3
Very likely 4 Major injury 4
Certainty 5 Fatality 5
Such assessments will always be examined by safety officers when performing inspections and may also be sought by insurance companies in the event of a claim.

## Slide 10: Risk assessment documentation

## Slide 11: COSHH
COSSH stands for Control of Substances Hazardous to Health.
The 2002 Regulations were introduced to control exposure to hazardous substances. The regulations explain any safety requirements when working with the following materials:
  solids – eg soda crystals
  liquids – eg bleach
  dust – eg drilling through asbestos ceilings
  fumes – eg when soldering
  vapours – eg when solvent-cementing waste pipes
  gases – eg flammable gases.

## Slide 12: COSHH data sheet
Before using any substance always check the COSHH data sheet. You should then:
  conduct a risk assessment prior to use
  take precautions to minimise risk to health and establish if harm is caused by ingestion, inhalation or absorption
  introduce control measures to minimise risk further
  monitor levels of use and exposure to the risk on a regular basis.
  You must receive training on the use of the substance concerned and learn where it is possible to substitute a hazardous substance with a less harmful alternative.

## Slide 13: COSHH categories and symbols
TOXIC – Poisons
HARMFUL
CORROSIVE – severe burns
EXTREMELY FLAMMABLE (eg liquefied petroleum gas – LPG)

## Slide 14: Domestic products and COSHH
Remember that some domestic products can be hazardous. For example, loft insulation can be an irritant to the skin, domestic cleaning chemicals can be either acid or alkali (corrosive)and may burn the skin.
The rule is that when using any item with a COSHH symbol:
you need to wear gloves to protect your hands.

## Slide 15: CDM Regulations
The Construction (Design and Management) (CDM) Regulations 2015:
  are intended to ensure health and safety issues are properly considered to minimise the risk of harm to everyone involved in a project
  set out definitions for principal designers, principal contractors and contractors. These are explained on the next slide.

## Slide 16: CDM definitions
  The principal designer (PD) is responsible for all the pre-construction phase planning and design work.
  The principal contractor (PC) must manage and coordinate the construction side of the project.
  The contractor (C) must plan and manage the work under their control, liaise with the PC and carry out the works without compromising health and safety.
  More information on the CDM Regulations 2015 can be found here: trusted-traders-guidance-for-businesses-434474.pdf (which.co.uk)

## Slide 17: Site safety signs
Construction sites can be dangerous places, with hazards lurking around every corner. Construction site safety signs are designed to reduce the risk of accidents and injuries, protecting workers and members of the public.
As well as pointing out hazards and pointing site users in the direction of urgent medical equipment, building site signs also play a crucial role in the efficient day-to-day running of the construction site.
Employers have a legal responsibility to ensure that every site has the relevant construction signage. This is an essential step to reduce the incidence of workplace accidents and injuries and ensure that members of the public are aware of the location of prohibited sites.

## Slide 18: The four safety sign colours
What are the four colours of safety signs?
What are the categories of safety signs?
Prohibition | Warning | Mandatory | Information

## Slide 19: Prohibition signs
Do not drink
Do not touch
No naked flames
No access for pedestrians

## Slide 20: Warning signs
Corrosive material
Danger, electricity
Flammable materials
Trip hazard

## Slide 21: Mandatory signs
Safety boots must be worn
Eye protection must be worn
Pedestrians walk this way
Hard hats must be worn

## Slide 22: Emergency signs
Emergency exit route
Emergency eye wash
First aid
Emergency telephone

## Slide 23: Construction Skills Certification Scheme
A Construction Skills Certification Scheme card proves that an individual has passed a health and safety test which enables them to work on a building site.
The cards come in different colours which are in line with the level of qualifications held by the individual.
  Green – construction site operative/labourer.
  Gold – skilled worker (NVQ Level 3 qualified).
  Black – senior manager (NVQ Level 4 qualified).
  Red – trainee/apprentice.
  White – individual with a construction-related job (eg cleaning of sites).

## Slide 24: SMSTS
The Site Managers Safety Training Scheme (SMSTS) course is for project managers, site managers and supervisors, business owners and clients. The course covers:
  Health and Safety at Work Act (HASAWA)
  Construction Design and Management (CDM) Regulations
  risk assessments/method statements
  recent changes in accepted working practices
  behavioural safety
  management of occupational health

## Slide 25: SMSTS
  electricity
  excavations
  working at height
  scaffolding
  demolition
  confined spaces.

## Slide 26: SSSTS
The Site Supervisors’ Safety Training Scheme (SSSTS) is for site supervisors and covers:
  Health and Safety at Work Act
  specific site issues that challenge supervisors on a daily basis
  effective toolbox talks
  supervision of occupational health
  behavioural safety.

## Slide 27
Any questions?