## Slide 1: PowerPoint 6: Awareness and inspections
PowerPoint presentation
1. Health and safety in building services engineering
1:5 Safety conscious procedures
1.6 Safety inspection of a work environment

## Slide 2: Objectives
By the end of the session, learners should be able to:
  understand safety-consciousness
  describe to report potential hazards
  outline methods of communication
  describe the importance of good housekeeping
  outline the requirements of an HSE construction site inspection.

## Slide 3: Being safety conscious
Safe systems of work cannot always eliminate all the risks involved in a specific operation.
Therefore, priority falls to lowering the risks involved in the process to an acceptable level: in other words, being safety conscious. This can be achieved by different procedures such as introducing engineering controls, administrative controls, etc and also, of course, by your own awareness concerning issues of safety in the workplace.
‘Mechanical’ examples include introducing a local exhaust ventilation system or guarding the moving parts of machinery.

## Slide 4: Being safety conscious
There are many ways we can be safety conscious in construction, such as:
  reporting of potential hazards – it is important to report any potential hazards identified to your supervisor or site manager. Good communication is essential. Make any concerns known clearly and quickly
  site inductions – educating site operatives about the safety processes on a specific site
  training – eg use of equipment, health and safety (eg the Construction Site Certification Scheme – CSCS), fire and first aid training as required
  ‘toolbox talks’ – meetings to discuss a particular topic between trades.

## Slide 5: Construction site safety inspections
Due to the construction industry being one of the most dangerous environments to work in, construction sites are routinely inspected by the Health and Safety Executive (HSE), whose inspectors have the right to enter your site without prior notice.
So: be prepared at all times for an audit of site safety.
Inspectors work within the guidelines and regulations of the law. They will often make a photographic record of the site and will ensure that all health and safety documentation is up to date.

## Slide 6: Types of inspection
Sensory inspections: evaluate construction operatives awareness (consciousness) regarding the hearing and smelling of possible dangers in the workplace.
Visual inspections: speak for themselves – what dangers are visibly clear? Are they being managed correctly?
  General health and safety risk management: inspectors ensure any contractors to the site have formally agreed to meet the health and safety standards of that site. They will ensure any equipment is installed correctly, is regularly inspected and is properly maintained according to manufacturer’s instructions.

## Slide 7: Good housekeeping: general order
Inspectors will be also be checking how the general cleanliness and waste management of the site is managed. For example:
  Are all walkways, stairs and work areas clear and easy to access?
  Are walkways level, even and gritted if slippery in cold or wet weather?
  Are materials stored safely in their correct places?
  Is waste managed and recycled as much as possible?

## Slide 8: Good housekeeping: working at height
  Site managers must demonstrate they are following the Work at Height Regulations 2005, for example:
  workers are taking proper precautions, such as the use of edge protection on scaffolding
  there is universal awareness of ladder safety (correct type of ladder, ladder in good repair, placed on suitable ground, properly secured and always at the correct angle and length).
  relevant training has been completed for all site operatives.

## Slide 9: Good housekeeping: welfare facilities
  Inspectors will enquire into the welfare facilities on site. For example:
  Is a kitchen or canteen provided for site operatives to rest and eat? This area should be well lit and ventilated, and be at a suitable temperature for the time of year.
  Is there a changing area and a place to dry/store items of clothing and workwear?
  Are washing facilities and clean working toilets available? Clean soap and towels must be provided for site personnel to wash and dry their hands. Washbasins should have hot and cold running water.

## Slide 10: Good housekeeping: PPE
  The inspector will make sure all site operatives are wearing the appropriate personal protective equipment (PPE), correctly and at suitable times. They will:
  ensure hard hats, ear protectors, masks and gloves are available to the team and are used correctly
  stress the importance of wearing the correct safety footwear on site
  ensure PPE is well maintained and in good condition.

## Slide 11: Good housekeeping: health and safety records
The site must also record and store all health and safety information for audit by an inspector. All internal (‘in-house’) and external inspections must be recorded. These should include information on:
  equipment
  storage
  welfare facilities
  risk assessments
  method statements
  near misses
  workplace accidents and incidents
  access to equipment.

## Slide 12
Any questions?