## Slide 1: PowerPoint 7: Implications of not following health and safety legislation
1. Health and safety in building services engineering
PowerPoint presentation
1.7 Implications to those working in the BSE industry of not following health and safety legislation

## Slide 2: Objectives
By the end of the session, learners should be able to:
  understand the implications of not following health and safety legislation
  describe the penalties that can be imposed
  explain the different notices that can be issued
  describe powers of prosecution if legislation is not followed.

## Slide 3: Implications
As you learned at the beginning of this unit, there are a range of different implications for not adhering to safe systems of work and not following health and safety legislation while working in the BSE sector: these vary from penalties to prosecution and because of the importance of this topic we look briefly at this area again here.
The law sets out responsibilities for both the employer and the employee to ensure that any work completed does not pose a risk or hazard to anyone who may be affected by that work – for example, the general public or the customer.

## Slide 4: Health and Safety at Work Act (HASAWA) 1974
The duties of the employer are:
  to provide a safe and healthy place of work
  to ensure safe systems of work
  to ensure the safety of equipment, plant and machinery
  to provide adequate facilities for staff welfare at work.

## Slide 5: HASAWA 1974
The duties of the employee are:
  to take reasonable care of the health and safety of themselves and others
  to comply with the employer’s health and safety policy
  not to recklessly interfere with anything that may affect health and safety.

## Slide 6: Enforcement authorities
Health and Safety Executive (HSE)
  HSE officers can:
  inspect sites
  give guidance and advice on work or processes
  take photos and samples
  discuss situations and/or problems
  seize evidence, equipment or materials.

## Slide 7: Enforcement authorities
HSE officers can also:
  take informal action – advise
  issue improvement notices outlining specific action (ie what, why and when)
  issue prohibition notices in cases of serious risk
  prosecute in cases of failure to comply with legislation.

## Slide 8: HSE inspectors
Heath and safety inspectors have the legal right to enter a workplace without giving notice, although notice may be given where the inspector considers it appropriate.
On a normal inspection visit, an inspector will look at the place of work, assess working activities and how health and safety is managed, to check that the employer is complying with health and safety law.
The inspector may offer guidance and advice, talk to employees, take photographs (evidence) and samples (evidence), serve improvement notices or act if a risk to health and safety is perceived.

## Slide 9: Informal action
There are several ways in which an inspector may take enforcement action to deal with a breach of regulations.
Where the breach of the law is comparatively small, an inspector will advise the duty-holder on what action should be taken to conform with the requirements of the law.
If required, this information can be given in writing.

## Slide 10: Improvement notice
More severe breaches will receive a direct order from an HSE inspector to take specific action in order to comply with the law.
The inspector will discuss the improvement notice with the duty-holder and resolve points of difference before serving it.
The notice will state what must be done, why and by when.
The time period to take the corrective action will be a minimum of 21 days, to allow the duty-holder time to appeal to an industrial tribunal if they believe this is justified.

## Slide 11: Prohibition notice
Where an activity involves a risk of serious personal injury, the inspector may issue a prohibition notice, forbidding the activity either immediately or after a specified time period.
This notice will not be lifted and work will not be allowed to resume until corrective action has been taken.
There will be a formal record of the non-conformance.

## Slide 12: Prosecution
In some cases, prosecution may be deemed necessary.
Failure to comply with an improvement or prohibition notice, or a court remedy order, can carry a fine or imprisonment, or both.
Unlimited fines, and in some cases imprisonment, may be given by higher courts.

## Slide 13: Local authority: inspection and enforcement
The building control inspector (or ‘building control surveyor’ as they are more commonly known) works for the local authority and makes sure that Building Regulations are observed in the planning and construction stages of new buildings.
They have the power to reject plans that fail to meet the Regulations.
They may also have to use their professional judgement and skill to offer advice on acceptable solutions to meet statutory requirements, should any problems arise.
They will make site visits at different stages of construction to ensure that all construction work is being properly carried out.

## Slide 14
Any questions?