## Slide 1: PowerPoint 2: Digital engineering techniques
PowerPoint presentation
10: Digital technology in construction
10.2 Digital engineering techniques

## Slide 2: What is digital engineering?
Digital engineering is the fusion of advanced digital technologies with product engineering capabilities in a digital environment. ​Its progressive development in the manufacturing and automotive industry is now being rivalled in the construction industry. A prime example of its use is in building information modelling (B.I.M.).
Notes: https://www.youtube.com/watch?v=kab2WdXEUBg&feature=youtu.be
Tutors may wish to show this video (Video clip 5.30m) which shows how designers and engineers can work together on shared BIM documents.

## Slide 3: Industrial strategy: Construction 2025
Working together, industry and government have developed a clear and defined set of aspirations for UK construction:
People – An industry that is known for its talented and diverse workforce.
SMART – An industry that is efficient and technologically advanced.
Sustainable – An industry that leads the world in low-carbon and green construction exports.
Growth – An industry that drives growth across the entire economy.
Leadership – An industry with clear leadership from a Construction Leadership Council.
You can access the full document here: Construction 2025: strategy - GOV.UK (www.gov.uk).
This document highlights how digital engineering and technology are expected to play a large role in construction in the future.

## Slide 4: Industrial strategy: Construction 2025
SMART: An industry that is efficient and technologically advanced:
Invest in smart construction and digital design: The radical changes promised by the rise of the digital economy will have profound implications for UK construction. UK construction businesses must be ready to secure their share of the forecast £200 billion p.a. global market for integrated city systems by 2030.
Bring forward more research and innovation: To meet the local and global opportunities presented by green construction, smart construction and digital design, UK construction must invest in people and technology.
Building information modelling: Industry and government have made a good start through their joint commitment to the building information modelling (BIM) programme.

## Slide 5: Structural analysis simulations
Structural analysis is the determination of the effects of loads on physical structures and their components. Structural analysis is at component and building structure level.
What are the types of structural analysis?
Hand calculations and prototype testing.
Finite element analysis.
Structural analysis software such as Autodesk REVIT is a digital engineering solution, which offers BIM structural analysis software.
Notes: Tutors may wish to show the following video clip about structural analysis simulations: https://youtu.be/C17ALt0ryBg

## Slide 6: Wind load simulations
Uplift load – Wind flow pressures that create a strong lifting effect, much like the effect on airplane wings. Wind flow under a roof pushes upward; wind flow over a roof pulls upward.
Shear load – Horizontal wind pressure that could cause racking of walls, making a building tilt.
Lateral load – Horizontal pushing and pulling pressure on walls that could make a structure slide off the foundation or overturn.
Source: https://campus.extension.org/mod/book/tool/print/index.php?id=6418&chapterid=6747
Notes: To see an example of how wind is modelled in 3D BIM, go to File:Cloud-based wind simulation by SimScale 3D London model by AccuCities.png - Designing Buildings Wiki
To watch a video demonstrating digital wind load simulation software, see https://youtu.be/cW5NOLaHgO4

## Slide 7: 3D rendering of building assets
Computer generated images (CGI) is also known as 3D rendering. CGI is a very broad term that refers to processes involving the use of computer software to create images. Until relatively recently, CGI was used predominately to create photo-realistic images of buildings before they had been completed on site.
Source: https://www.designingbuildings.co.uk/wiki/Computer_generated_imagery_(CGI)
Detailed architectural drawing, or design plans only go so far in helping people to create pictures in their heads. A 3D visualisation within an environmental context, however, will lodge in the mind for several days. This kind of drawing is also known as an artist's impression.

## Slide 8: Using CGI to view proposed built assets
Step by step of the CGI production process
Site photography – in order to capture the lighting conditions and the context created by the natural environment.
3D Modelling – using CAD drawings, a 3D model of the property is created. Finishes are then added, such as the texture of the bricks, or sunlight reflecting on windows.
Rendering – the CGI model is ‘situated’ within the context captured by the onsite photography. The model information and finish is then rendered. Now the image looks like a high quality photograph.
Detail work – is done to complete the image. Masking is applied to ensure the property CGI looks ‘real’ within its surrounding environment. Contrast is applied and people may be added for scale.

## Slide 9: Augmented reality (AR) underground asset mapping
Pipes can be located to within 5cm and video capture of geospatial information can be made prior to an excavation.
The resulting footage is used to create detailed 3D point cloud models that ensure accurate visual records and ‘x-ray vision’ of the utility layout and geology for future works.
It makes working on underground systems safer and simpler, allows projects to be delivered more quickly and efficiently, and keeps disruption to the public to a minimum.
Source: https://constructionmanagement.co.uk/morrison-us-maps-underground-services-with-ar-tech/
2D and 3D augmented reality (AR) systems can be used to view and map underground services prior to excavation to plan and manage works more effectively. This can be accessed by smart phones and tablets on site or remotely.

## Slide 10: 3D modelling
3D modelling refers to the process of creating a mathematical representation of a 3-dimensional object or shape using software. The common types of 3D modelling are:
3-D primitives – simple polygon-based shapes, such as pyramids, cubes, spheres, cylinders and cones and spline curves.
Primitives are the building blocks of 3D – basic geometric forms that you can use as they are or modify.
Sources: https://www.igi-global.com/dictionary/3d-modelling/48788
https://www.techtarget.com/whatis/definition/3-D-three-dimensions-or-three-dimensional

## Slide 11: 3D modelling
NURBS (non-uniform rational basis spline) are smooth shapes defined by bezel curves. NURBS is a mathematical model that is commonly used in computer graphics for representing curves and surfaces.
Rectangular shape spline mesh
The NURB surface is a rectangular mesh of rows and columns with four hard corner points. The entire surface is continuous, except for these four points. You can stretch and distort the surface to any shape by repositioning the vertex points, but the more non-rectangular shape, the more difficult it will be.
It is the designer’s job to determine how to break down a full 3D model into a collection of rectangular-like pieces, how to deal with the four hard corner points, and how to maintain the proper continuity between surfaces.
Source: http://www.pilot3d.com/NurbSecrets.htm

## Slide 12: 3D modelling and animation
3D modelling in construction also allows for animation, giving clients a virtual walkthrough of the proposed building.
In the case of a new home, clients can walk through the entry of their future home, reach the hallway and even visualise guests having dinner at the dining area. Realistic lighting can be used and it is also possible to fill the space with appropriate furniture and decor choices.
It also becomes easy to understand a structure in the context of the surrounding space. For example. transforming a building into a dream home by virtually surrounding it with landscaping.
Source: https://www.geospatialworld.net/blogs/3d-modeling-construction-benefiting/

## Slide 13: 3D modelling
There is no doubt that use of 3D modelling in construction results in better designing and material utilisation. 3D models can be rotated for different perspectives and to gather additional views.
The advantages of 3D modelling include:
checking the errors which might occur in the drawing process
gaining better insight for surface patterns
having virtual tours through walkthroughs
getting renderings with customised interiors
achieving more at a lower cost
achieving better collaboration between teams involved in the construction process.
Source: https://www.geospatialworld.net/blogs/3d-modeling-construction-benefiting/

## Slide 14
Any questions?