## Slide 1: PowerPoint 3: 10.2 Digital engineering techniques (2)
PowerPoint presentation
10. Digital technology in construction
10.2 Digital engineering techniques

## Slide 2
Rotary laser level
Laser scanner
Video: https://share.vidyard.com/watch/2CFpwg7Anvd3hfeetZj36i
Virtual surveying using drones
Video: https://youtu.be/JMv61HpdR2c
Surveying devices

## Slide 3
Digital engineering – surveying equipment
A total station is an electronic transit theodolite integrated with electronic distance measurement (EDM) to measure both vertical and horizontal angles and the slope distance from the instrument to a particular point, and an on-board computer to collect data and perform triangulation calculations.
Notes: To demonstrate a rotary laser level, tutor may wish to show the Leica Rugby 610 Rotating laser level (Li-ion) at https://leica-geosystems.com/en-gb/products

## Slide 4
Digital engineering – surveying (photogrammetry)
Photogrammetry involves taking overlapping photographs of an object, structure or space and converting them into 2D or 3D digital models. It is often used by surveyors, architects, engineers and contractors to create topographic maps. Using ultra high-resolution images with advanced GPS and mapping software, photogrammetry can produce a fully immersive 3D visual model of the real world.
Used to survey structures or property.
Uses ultra high-resolution aerial photography.
Captures multiple images over a landscape.
Can offer differing views of a single focal point.
Produces a photographic document of on-the-ground conditions that can be used by engineers, architects and the wider construction team.

## Slide 5
Digital engineering – surveying (LiDAR)
LiDAR, or light detection and ranging, uses points of light to create a detailed map of an object’s position in space. It has been used to power everything from automated driving technology, to augmented reality, to advanced topographic surveying. When mounted from a UAV or airplane, LiDAR can be used to directly measure the height and density of land and vegetation below, including detailed data on groundcover and trees. This remote sensing method is valuable for mapping the characteristics of land from overhead.
Notes: Virtual surveying using drones: https://youtu.be/JMv61HpdR2c
Tutors may wish to explain how LiDAR works:
LiDAR uses the power of a laser directed down toward the earth surface and fired in rapid succession, a rate of many thousand pulses per second. The amount of time it takes for the light to return to the LiDAR source indicates its exact distance.
It works like echolocation in bats or submarines, but powered by the speed of light. Data generated by LiDAR sensors is collected and pinned to GPS metadata to create a detailed map of the landscape. To produce an accurate picture, data from remote sensing tech is then layered to cross-reference ground points. During the 1980s, after the introduction of GPS, it became a popular method for calculating accurate geospatial measurements.

## Slide 6: Surveying – guidance systems
In a machine control system, the cutting edge of the equipment is fully controlled by automation. The system is connected to and controls the hydraulics while the operator drives the equipment and manages the automation. Laser augmented GPS provides near exact positions of the vehicle in real time and allow a high degree of accuracy.
Advantages:
No stakes needed.
No grade checker needed.
Its recorded data can be used for quality control and volume computation.
The data can be transmitted to the engineer, inspector or surveyor for real-time checks.
Notes: To watch a video, see https://youtu.be/ImqvzKEOe6M

## Slide 7: 3D camera systems
Three dimensional (3D) camera systems can be used to create virtual tours of a space. They can capture imagery, collect measurements and process data to create, edit and share a 3D rendering of the location. This can also be integrated into BIM technology. It can be used throughout the project, for example, to allow engineers to view the site in accurate detail without needing to make repeated visits.
For example, Matterport is a three-dimensional camera system which can be used to document a building or property in 3D.
Notes: For more information, see https://matterport.com/industries/architects-engineering-construction .
A video demonstration of the software is shown here: https://youtu.be/aHuHNjdrdHs

## Slide 8: Virtual reality (VR)
        Virtual reality (VR) technologies, when used with the building information modelling, make it possible to ‘walk around’ a building.
        To improve accuracy, VR can be combined with laser scanning (also known as LiDAR or point cloud surveying).
        When you combine laser scanning technology with a drone, you can create highly detailed models for virtual reality which allows the client to ensure that his brief is understood by the designers and the contractors.
The benefits of using VR in a project:
saves time and money
improves training safety
improves collaboration
improves/shorter timescale
improves quality.
Notes: To see a video clip of VR, go to https://www.youtube.com/watch?v=R4gWpXuPAXo

## Slide 9: Augmented reality (AR)
AR is a computer simulated ‘enhancement’ of real life. It is the overlaying of digitally-created content on top of the real world. It can be offered through a headset or a screen in a 2D display.
AR is like a VR experience, the difference being you can see the real world around you. Workers can use AR to check progress and prevent mistakes by double-checking work on site. It can be used to ensure that all the components were laid down as designed and to check whether the project’s requirements have been met.
Notes: To watch a video about AR, see: https://www.youtube.com/watch?v=R4gWpXuPAXo

## Slide 10: Augmented reality (AR)
The benefits of using AR in a project:
Less rework and downtime cost.
Improved safety.
Better project management and collaboration.
Improved/shorter timescale.
Improved quality.
Accurate space and measurement projection.
The limitations of using AR in a project:
Expensive, but software is becoming cheaper, especially with the availability of mobile apps.
Not all AR headsets allow for hard hats to be worn.
The distraction factor, health and safety, risks on site (failure to see a hole or a crane).
Bad internet connections.

## Slide 11: Digital artist impressions
Photo-realistic artist impressions help clients and other parties to see what a project will look like before building starts, with accurate depictions of materials and finishes. They can even show what a building project will look like in different weather or lighting conditions.
3D artist impressions capture the look and feel of a building in a way that 2D drawings simply cannot match. Artist impressions are a proven selling tool because buyers respond faster and more positively to high detail – perspective, colour, materials and lighting.

## Slide 12: Digital artist impressions
These can be created from detailed architectural drawings or verbal/written briefs.
Photo realistic architectural visualisations can be used for a variety of purposes:
Planned or imaginary landscapes and cityscapes.
Infrastructure developments and improvement schemes.
High quality 3D technical drawings for building materials.
Artist impressions of a new home.
Street scenes.

## Slide 13
Any questions?