## Slide 1: PowerPoint 2: Maintenance plans and timeframes
PowerPoint presentation
13. Maintenance principles
13.2 Maintenance plans
13.3 Typical timeframes between maintenance tasks

## Slide 2: Objectives
At the end of the session learners should:
  understand the different types of maintenance plans for different BSE systems
  be aware of the different timeframes between maintenance activities
  describe the different tasks to be carried out during the maintenance of BSE systems.

## Slide 3: Planned preventative maintenance (PPM)
As you have already learned, larger BSE installations and systems will benefit from having PPM schedules to:
  identify any failing components
  ensure the system is working at its optimum.

## Slide 4: Plans for plumbing systems
PPM activities for plumbing systems are typically carried out every 12 months, although as with all PPM activities, heavily used systems will likely need to be checked every 3 months. The engineer will, for example:
  check and set float-operated valves
  clean out sediment
  re-washer taps if required
  test drainage systems
  check flow rates
  check safety valves and external controls.

## Slide 5: Plans for gas systems
A gas engineer will typically service a system every 12 months (3 for heavily used systems, as is the case for all areas of PPM), and carry out checks such as:
  setting gas valves and safety controls
  testing sizing and leaks
  boiler maintenance/servicing
  checking ventilation parameters
  testing flue integrity and flow
  ensuring flue products are within manufacturer’s requirements
  checking any safety valves and external controls.

## Slide 6: Plans for wiring and electrical systems
Electrical engineers typically conduct PPM on systems every 12 months. Checks include:
  checking the integrity of electrical circuits (continuity of earthing, cable insulation properties, polarity of switching)
  checking cable assemblies (prior to full testing, an inspection is carried out, using touch, sight, hearing and smell to detect signs of overheating or dissimilar metal corrosion, such as when copper and aluminium come into contact)

## Slide 7: Plans for wiring and electrical systems
  examining plug outlets for suitability (continuity of earthing, cable insulation properties, correct polarity of switching)
  testing residual circuit breakers and trip switches
  identifying any possible areas for future faults
  checking the operation of any components, appliances and safety controls.

## Slide 8: Plans for ventilation systems
As for gas and electrical systems, the engineer will typically carry out PPM every 12 months. For ventilation systems, checks will include:
  whether the system has been installed properly
  examining the integrity of ductwork
  checking the system is balanced correctly
  checking any condensate connection is installed correctly
  conducting an airflow measurement test
  checking the operation of any components, appliances and safety controls
  conducting a visual inspection to identify any future issues.

## Slide 9: Plans for air conditioning systems
Again, PPM is carried out at least every 12 months and includes:
  checking the unit’s electrical wiring to ensure it is safe to use
  cleaning vents and grilles
  cleaning and inspecting motors
  checking and cleaning any condenser coils
  inspecting and adjusting belts and pulleys
  ensuring any condensate connection is installed correctly
  using a leak detector device to test for any leaks from refrigerant
  checking any components, appliances and safety controls
  recording the temperature and pressure of the unit.
Source: Shutterstock.com/eagle_marat

## Slide 10: Plans for drainage systems
Annual PPM checks include:
  checking gutters and downpipes for sagging, blockages or leaks
  cleaning and testing water traps for blockages and trap retention
  checking water levels in WC cisterns
  inspecting waste and soil pipes for adequate support and size
  checking float-operated valves
  ensuring any condensate connections are installed correctly
  checking that any air admittance valves are working as intended.

## Slide 11: Plans for lighting systems
Annual checks include:
  checking the integrity of electrical circuits
  checking cable assemblies: these should be visually inspected and tested against Institution of Engineering and Technology (IET) BS 7671

## Slide 12: Plans for lighting systems
  examining lighting fixtures for suitability
  cleaning lighting fixtures because dirt causes reduction of illumination
  testing any residual circuit breakers, trip switches, residual current devices (RCDs), fuses and circuit breakers
  identifying any possible areas for future faults
  checking the operation of components, appliances and safety controls.

## Slide 13: Plans for communication and data systems
Annual checks include:
  visually examine cabling and connections
  testing and inspecting switches, routers, etc
  updating virus and malware software
  installing security patches
  installing application updates as appropriate
  removing dust and any obstructions from server intakes and vents
  performing routine maintenance tasks (‘checkdisk’, ‘defrag’ and security and virus scans).

## Slide 14
Any questions?