## Slide 1: PowerPoint 3: Documentation and fault action
13. Maintenance principles
PowerPoint presentation
13.4: Documentation required for maintenance and verification of maintenance activities
13.5: Actions required when faults cannot be rectified

## Slide 2: Objectives
At the end of the session learners should:
  be able to identify the various pieces of documentation necessary to complete maintenance activities
  understand the actions required when faults cannot be rectified.

## Slide 3: Maintenance documentation
There are many different pieces of documentation required when completing maintenance activities. Some offer advice and guidance to the customer about maintenance, others require completion to record your findings and inform future maintenance activities and/or timeframes.

## Slide 4: Manufacturer’s instructions
Every component or appliance to be installed in a BSE system will come with manufacturer’s instructions to assist in its:
installation
servicing
maintenance
repair.
Instructions are produced for each individual appliance/component and must be followed to ensure correct functioning.

## Slide 5: Maintenance checklist
A maintenance checklist is designed to track the maintenance of buildings, equipment and systems. Regular maintenance is needed to ensure efficiency in operation. These documents cover systems such as:
  lighting
  plumbing
  fire equipment
  heating and cooling systems
  energy systems.
The maintenance checklist details what must be checked and when.

## Slide 6: Service logbook
A service logbook details all the tests and checks that need to be, and have been, completed to ensure continued safe use of an appliance or component. For example, all gas systems and appliances in rented property must be inspected every 12 months to ensure they are safe.
However, in any environment, gas boiler manufacturers normally state that all their appliances require servicing every 12 months or any warranty is void.
The findings of the annual inspection/service are documented as proof that the appliance is working within set parameters and is safe to use.

## Slide 7: Job sheet
A job sheet or job specification is a document detailing a description of the installation that is being quoted for, complete with the types of materials and appliances the installation will contain.
Occasionally, it may specify the manufacturer and model of the appliance to be installed and how long it should take to complete the work.

## Slide 8: Condition report
A condition report is completed when a building is being sold or when the owner wants to receive a low-level report on what state of repair the building is in. A condition report records the conditions of different areas of the building and assigns each a level. These areas commonly include:
  site improvements – the surrounding land of the building
  structural systems and building ‘envelope’
  mechanical, electrical and plumbing systems
  fire safety
  accessibility.
These areas are assessed, and the report is provided to the client to carry out any remedial works required.

## Slide 9: Actions required when faults cannot be rectified
Sometimes an identified fault cannot be rectified and a new part, component or appliance will be needed. This may in turn need to be ordered, which will lead to a delay in repair.
Therefore, it is imperative that you:
inform the customer of any possible delays in the replacement of the system/component
arrange for secondary services to be available until the primary source is back in service (eg, by providing electrical heaters if the heating is broken)
make the system safe until a replacement is installed (eg, safe isolation from energy, gas, electric and water supplies).

## Slide 10: Other implications of irreparable faults
If faults cannot be rectified, the following may result:
  increased time on the job
  increased costs due to having to reattend the property
  system downtime – distressing for the customer
  loss of income – distressing for the customer
  increased hazards – possibility of further damage/breakdown: distressing for the customer
  loss of services – distressing for the customer.

## Slide 11
Any questions?