## Slide 1: 2.5 Electricity principles PowerPoint 4: Power and distribution
2. Construction science principles

## Slide 2: Generating electricity
Electricity is generated by moving a conductor through a magnetic field (electromagnetism). Different forces are used to drive the conductor, such as steam or water, as shown in the hydro scheme illustrated here.

## Slide 3: Sources of power
Fossil fuels – oil, gas and coal.
Nuclear power – a controversial fuel, especially since radioactivity remains active for hundreds of years.
Renewable energy – solar, wind, water.

## Slide 4: How power is generated from fuel
Coal – coal-fired power stations burn coal to turn water into steam which drives a turbine (electrical generator).
Oil and gas – these fossil fuels produce heat on burning which generates electricity.
Nuclear power – relies on fusion to produce heat, then steam, etc.
Renewable generation – eg wind farms producing ‘clean’ energy by turning a turbine using the power of the wind.

## Slide 5: Components of a power generation system

## Slide 6: Units of measurement for electricity
The base SI unit of amperes (A) is the unit of measurement for current. For example, lighting circuits don’t need as much energy and are 5A, whereas power circuits require 13A.
A volt (V) is the derived unit for electric potential, electric potential difference (voltage) and electromotive force.
The ohm (Ω) is the derived unit of electrical resistance.
The watt (W) is the SI unit of power, used to measure the rate of energy transfer.

## Slide 7: Electromagnetic induction
When rotated around each other, a magnet and a copper coil of wire create an electrical force.
A voltage is produced when a magnet moves into a coil of wire. This process is called electromagnetic induction. The direction of the induced voltage is reversed when the magnet is moved out of the coil again. If the coil is part of a complete circuit then a current will be induced in the circuit.
This principle is what an electrical generator consists of: a copper coil surrounded by a magnet which generates electricity.
Notes: Electricity and magnetism are symbiotic, in other words you cannot have one without the other.
Therefore, when a conductor is moved through a magnetic field it creates an electromagnetic force, and this is known as the generator principle.
For more see: Electromagnetic induction - Electromagnets and motors - GCSE Physics (Single Science) Revision - BBC Bitesize

## Slide 8: Transformers
There are various types of transformer: step-up and step-down (power transformers), which can be either three-phase or single-phase. In addition there are:
current transformers (eg clamp meters)
safety isolation transformers (eg electric shavers)
autotransformers (reduced voltage systems such as a 110V supply)
differing equipment supplies, eg 12V (battery), 230V (mains)
Industrial equipment cannot necessarily run on 12V, 110V or 230V because there is insufficient power (current) to drive heavy loads. Therefore, three-phase 400V supplies are used for larger electrical motors.

## Slide 9: Step-up and step-down transformers
Step-up and step-down transformers allow us to easily multiply or divide voltage and current in AC circuits. AC voltage can be ‘stepped up’ and current ‘stepped down’ for reduced wire resistance power losses along power lines.
Notes: Tutor notes
The power into a transformer must equal the power out. We cannot alter it.
Voltage is deliberately stepped up, in order to reduce its output current, which then permits the use of much smaller conductors. Less current also means less heat loss and volt drop and therefore makes for a far more efficient system.
Suggest you stipulate that there is no electrical link between the Primary (input) and the Secondary (output), which is why transformers are used as Safety Isolation devices. Equally that magnetic link needs to be continually pulsed, which is why transformers only work with alternating current.

## Slide 10: Three-phase transformers
Three-phase transformers are static electromagnetic devices made to transmit energy or send alternating electrical signals between circuits. This equipment is mainly used for industrial purposes to generate, transmit and distribute electrical energy.

## Slide 11: Power distribution
A star distribution system involves two different voltage systems and is able to supply:
domestic power (230V single phase)
commercial power (400V three-phase & neutral)
industrial power (400V three-phase & neutral).
To distribute power via networks to industry and domestic users, pylons are mainly used in the UK – the country has a ‘National Grid’ to distribute high voltages nationally.

## Slide 12: Power distribution system
Notes: Tutor notes if needed
Once the National Grid has delivered the electricity to areas of high consumption, electricity is then ‘taken’ from the national grid via a series of appropriately located sub-stations that sequentially transform the grid supply down. The voltage is stepped down as follows:
  33 kV for distribution to heavy industry
  11 kV for high voltage distribution to lighter industry
  415/400 V to commercial consumer supplies
  240/230 V to domestic supplies
At the 11 kV stage the supply reaches a series of local sub-stations. This is then further transformed down to 400 V and distributed via a network of underground radial circuits to customers. At this point the neutral conductor is also introduced by connecting the secondary side of a star-connected transformer to an earth spike at its star point. In rural areas the distribution is via overhead lines and will also be associated with TT earthing systems.

## Slide 13: Direct and alternating current
Unlike the mains supply, direct current (DC) is a constant value
and only travels in one direction. Batteries prefer DC supplies.
But transformers only operate with alternating current (AC).

## Slide 14: Electricity in the built environment
Domestic properties do not normally need more than 100A to supply their electrical loads and a 230V single-phase supply can provide this.
A large factory or commercial premises (eg a hotel or school) will need far more than 100A, and will therefore have a 400V, three-phase & neutral supply.
In construction, 110V is used onsite, because it is a safer voltage. This is known as a reduced voltage system.

## Slide 15: Fuses
Fuses operate on one of two principles:
heat: excess current melts a fuse wire within a fuse, or trips a bimetallic contact within a circuit breaker
magnetism: a circuit breaker also has a magnetic trip isolator, which will engage when very high fault currents occur. RCDs are purely magnetic safety devices and we will look at these now.

## Slide 16: Residual current devices
A residual current device (RCD) is one of the most important electrical safety devices in both the home and in commercial environments.
Upon detecting an earth fault (eg an electric shock to the body), it will turn off the current immediately before it can cause harm.
RCDs protect against injury and death by electric shock by detecting an imbalance between the outgoing and incoming total current of a circuit.
RCDs work on the simple principle that if there is a difference between the electricity coming in and going out, then it must have gone somewhere.
RCDs provide additional protection for earth faults only. If an RCD detects that there is no current flowing in the neutral, then it will trip instantly in the belief that the current has either gone down the earthing system or elsewhere – such as through a person!

## Slide 17: The return earth path
Notes: Tutor notes
An electrical supply that relies on a negative conductor to complete a circuit will work perfectly when the circuit is put to use ie running through a resistor. This could be a light fitting, a water heater element or motor which is adequately insulated meaning a short circuit fault cannot exist.
In cases where cable or appliance insulation is compromised there is a potential for a short circuit to occur, in other place the current will find a direct path to earth. This path will return to the generator or substation through the earth’s conductive low resistance.
If a person bridges the gap between the fault and the earth sink the short circuit current will flow them to the power source possibly resulting in death (in excess of 50 mA flowing through a human body will result in death).
This emphasises why circuit protection devices are so important an integral part of electrical circuits.

## Slide 18: Earth loop impedance
The path a fault current takes is referred to as the earth loop impedance and, like resistance, it is measured in ohms (Ω).
The total sum of loop impedance can either be calculated or measured. If this value is less than what is registered in the wiring regulations, for a given type and rating of a protective device, it will isolate the supply within the expected time, such as 0.4 seconds.

## Slide 19
Any questions?