## Slide 1: 2.8 Light principles 2.9 Acoustic principles PowerPoint 8: Principles of light and sound
2. Construction science principles

## Slide 2: The principles of light
Artificial and natural light must both be incorporated into the design of a building, taking into consideration energy use and the creation of a pleasant environment for the occupants (the aesthetics of a building). Two key principles come into play here.
Refraction is the scientific principle that light can be bent when it passes through a translucent medium such as glass or water. This distorts the path of the light and shifts or skews it.
Reflection is the term applied to light as it bounces off internal surfaces of our built environment.

## Slide 3: Refraction
Both refraction and reflection can be used to positive effect in buildings, and both have drawbacks that should be avoided, such as unwanted distortion and glare.

## Slide 4: Light and building design
Artificial light is light created using electricity and a filament (or increasingly, a light emitting diode – an LED). LEDs are favoured because they are energy efficient. Lamps that utilise a filament are called incandescent lamps. Incandescence means ‘white hot’. Discharge lights, on the other hand, create illumination by sending an electric discharge through an ionised gas.
Natural light is provided by the sun. The intensity of sunlight varies across the seasons in relation to the height of the sun above the horizon.
Good design incorporates a blend of each so that uniform lighting is balanced across a whole floor. Buildings should ideally be orientated to maximise daylight within.

## Slide 5: Natural light used to positive effect

## Slide 6: Directed light and glare
Directed light: we can direct light using reflectance (the proportion of light striking a surface which is reflected off it), and put it to good use. For example, light tunnels can be installed over staircases using a polished stainless steel tube and a lens. Light is directed down the tube and through a diffuser at ceiling level.
Glare is light that is directly reflected back into the eye causing discomfort and irritation. Window blinds can prevent this along with sunshades and window tints.

## Slide 7: Glare
Unpleasant glare caused by direct sunlight

## Slide 8: The daylight factor
The daylight factor is a design element that is applied to calculations in lighting design. The height of the sun above the horizon, the reflectance around a window and the internal finishes are all taken into account when striving to create a pleasant and healthy indoor environment.
Notes: Tutor notes:
Inverse square law Law and Cosine law (at an angle) both relate to the amount of illuminance of a surface.

## Slide 9: Colour rendering
Colours take on different shades or hues when viewed in different types of light (natural, artificial, bright or dim light). Colour rendering ‘scores’ can assist in determining how colours (of walls, floors, paintwork etc) will look when illuminated by a particular type of light. The Colour Rendering Index (CRI) is the tool used to measure how a colour will look under artificial light compared with natural light.
All good colour schemes, including any inherent in a building’s fabric, should take colour rendering into account as it may make the difference between a calm and pleasant space and one in which many people will feel uncomfortable.

## Slide 10: Principles of acoustics
Sound is created when air particles vibrate and collide with each other, causing the vibrations to pass between the air particles. The vibrating particles enter a person’s ear and vibrate the ear drum.
Acoustics refers to the qualities of a room or building that determine how sound is transmitted through or within it. The acoustic design of a concert hall would have very different requirements to an office or private home.
The Elbphilharmonie in Hamburg has a unique design. Coral reef-like structures of over 10,000 acoustic panels with uneven surfaces line the ceiling, walls and balustrades to shape the sound. When sound hits a panel, it either absorbs or scatters it, creating a balanced reverberation across the hall.

## Slide 11: Reducing unwanted sound
Unwanted sound from a neighbour can be a nuisance that isn’t welcome and must be reduced.
Part E of the approved documents provides measures that have to be incorporated into a building during construction to reduce the transference of sound. For example:
use of dense materials between party walls
use of sound insulation quilts
use of carpets and soft furnishings.

## Slide 12: Acoustic principles in the construction industry
Insulation – this is a sound-deadening ‘quilt’ placed in party walls of the timber stud type, and in cavities between such walls to reduce the transfer of noise across the cavity.
Sound absorption – soft, pliable or porous materials make good acoustic insulators, meaning that they absorb the most sound, whereas dense, hard materials (eg metals) reflect sound, making an internal space noisier. Rooms absorb sound in relation to the effective absorption area of the walls. This is also known as the total absorption area.

## Slide 13: Acoustic principles in the construction industry
Use of specific acoustic materials. This relates directly to the principles of absorption – soft furnishings such as carpets and curtains help to prevent sound reflecting around a room, thus reducing sound transfer. In the same way, choice of building materials will have an effect on the level of sound transfer and absorption.
Specific soundproofing is also important, especially in apartment blocks or terraced/semi-detached housing: anywhere in fact where people are living close to one another. Concrete blocks provide good soundproofing, and soundproofed plasterboard is also available.
Notes: https://www.nps.gov/subjects/sound/understandingsound.htm

## Slide 14: Acoustic principles in the construction industry
Reverberation is the prologation of sound, also called its resonance. The reverberation time is the time it takes for the initial sound to decay before silence resumes.
Reverberation is an important factor to take into account when designing and constructing buildings. For example, in buildings such as schools, high reverberation can reduce the clear transmission of sound and speech, making it more difficult to understand.

## Slide 15: Acoustic principles in the construction industry
Focusing is the ability to use a curved surface to focus a sound into a central point, for example a parabolic dish.
Resonance is the ability of a set of frequencies to make a second object vibrate synchonously.
Echo is a sound or sounds caused by the reflection of sound waves from a surface back to the listener.

## Slide 16: The volume (intensity) of sound
Sound levels are measured using decibels (dB). A decibel is a unit used to measure the intensity of a sound by comparing it with a given level on a logarithmic scale.
Noise levels above 70dB may damage people’s hearing over time, and noise above 120dB, such as a jet plane taking off, can cause immediate damage.
A normal conversation takes place at around 60dB, and the Health and Safety Executive (HSE) suggests that background noise is too high if employees need to raise their voices to be heard clearly when standing about 2m apart.

## Slide 17: Noise pollution
Noise can be termed ‘pollution’ when it interferes with adjacent activities. For example, loud music played in a garden will annoy the adjacent neighbour. Traffic noise may disturb people living in nearby housing.
The perception of ‘How loud is too loud?’ varies from person to person. There are points at which high noise levels start to affect wellbeing, inducing stress. Unwanted noise can also disturb sleep and prevent relaxation, adding to stress and damaging long-term health.
Notes: For more information see: How loud is too loud? – Hear the World Foundation (hear-the-world.com)

## Slide 18: Noise in construction
Construction work creates noise pollution but this can be controlled by:
limited working hours
using sound barriers around work sites.
It is important to protect operatives from noise pollution and hearing loss, including conditions such as tinnitus.
The Control of Noise at Work Regulations 2005 aim to ensure that workers’ hearing is protected from excessive noise at their place of work and must be adhered to.

## Slide 19: Approved document E
Compliance is required with approved document E (‘Resistance to the passage of sound’) in construction projects.
This document is part of the the building regulations and covers all requirements for buildings regarding resistance to sound, such as protection against sound from adjoining buildings, within dwelling-houses, reverberation inside residential buildings and acoustic conditions in schools.
You can find approved document E here: https://www.gov.uk/government/publications/resistance-to-sound-approved-document-e

## Slide 20
Any questions?