## Slide 1: PowerPoint 9: Earth science principles
PowerPoint presentation
2. Construction science principles
2.10 Earth science principles

## Slide 2: Physical geography and site investigation
Land use, water levels, ground contamination and the use of soil samples all form part of a site investigation report which reviews and evaluates each feature. A designer and structural engineer will need such information for the sub- and superstructure building design.
Soil samples are taken so they can be tested in a laboratory to see how much load they can bear before settlement occurs. Ground water levels are needed so that measures can be taken to ensure the foundations are not subject to any movement.

## Slide 3: Physical geography and topography
The geography and topography of a construction site are important because:
features in the natural environment have to be protected
watercourses and sources must remain pollution-free
drainage should be sustainable
excavation should be kept to a minimum.

## Slide 4: Hydrology
The water cycle consists of evaporation/transpiration, condensation and precipitation. Rain falls (precipitation), water evaporates, clouds form (condensation), rain falls, and so on.
It is important to prevent onsite pollutants entering the water cycle.
Construction projects always have to take into account the proximity of rivers, lakes, reservoirs and other watercourses, as well as any water below ground, such as underground streams.
Notes: https://www.sciencedirect.com/topics/earth-and-planetary-sciences/hydrological-cycle

## Slide 5: Geology
The geology of the Earth includes the rocks and strata that make up the layers we build on and materials we use for our built environment. For example, within the UK we find:
granite rocks from Scotland for hardcore fill
slate from Wales for roof tiles
clays from Leicestershire for brickmaking.

## Slide 6: Natural phenomena
Earth forces and natural phenomena include landslides and tidal influences.
Landslides – excessive rainfall penetrates the side of a slope and can cause the particles of soil to ‘slide’ over each other. The result is that slip occurs under the force of gravity. For example, a slope gives way and damages anything in its path.
Tides – some high tides must be controlled using flood defences to prevent coastal flooding during the high spring tides when the moon has the maximum gravitational influence on the Earth.

## Slide 7: Natural phenomena
Small earthquakes do occur the UK, but rarely measure more than 5 on the Richter Scale, and usually last less than a minute. Damage to buildings is very minimal and earthquakes do not have a major impact on the landscape.
Areas of the world on fault lines can experience severe earthquakes, and 81% occur in the Pacific Ring of Fire.
Earthquakes occur where tectonic plates join on the Earth’s crust. Movement in the plates causes the ground to shake as one plate moves over another. Earthquakes are measured on the Richter Scale.

## Slide 8: Natural phenomena
Weather can have a dramatic effect on our built environment – from high winds that can lift and damage roofing materials through to excessive rainfall.
The latter causes localised flooding because surface water drainage cannot cope with the increased demand and ‘backs up’.
Long periods of sunshine dry out clay soils, which leads to foundation settlement (subsidence).
Climate change is believed to be having a detrimental affect on all types of weather patterns around the world.

## Slide 9: Natural phenomena
Subsidence occurs when soils beneath a foundation are unable to support the weight of the structure. The structure settles, or subsides, as the voids between soil particles are squashed together.
Subsidence causes foundations to shift and can cause masonry to crack, becoming unsafe.

## Slide 10: Natural phenomena
Sinkholes are a form of subsidence where cavities in the ground form when water erodes an underlying rock layer.
Either:
the roof of an underground cave collapses or
water dissolves the rock beneath the soil – without rock to support it, the soil layer collapses and creates a hole.
Sinkholes can occur naturally or can result from urban development which compromises the integrity of the underlying rock structure, which is then washed away by erosion.

## Slide 11: Natural phenomena
Since 1910 in the UK, there have been 17 record-breaking months of rainfall. Nine of these have been since the year 2000, which shows that we are experiencing higher levels of rainfall, increasing the risk of flooding.
In the UK, the Environment Agency is responsible for managing flood risk and damage. New houses can be built on flood plains, but flood risk from rivers, seas, reservoirs or other bodies of water will be factored into design and planning decisions so that the risk is managed.
Notes: What causes a flood? - BBC Bitesize

## Slide 12: Minimising impact by design
We can incorporate design features into buildings and infrastructure projects to reduce the impact of Earth science events. For example:
straps from the walls to the floor slabs of a building prevent uplift in high winds such as hurricanes
overhangs on roof eaves throw off water from the face of a building
water retention measures such as soakaways reduce flood risk
schemes such as tidal defences alleviate floods
piled foundations reduce settlement.
Notes: https://www.thebalancesmb.com/types-of-concrete-joints-845022

## Slide 13: Soakaways
A soakaway is a ‘sustainable drainage solution’ – in essence it is a hole dug in the ground, often on the perimeter of a property. The hole is filled with a plastic crate, coarse stone and rubble, allowing water from a drainage pipe to filter slowly through and pass into the ground.
Soakaways are used to manage surface water from heavy rain and can help to prevent localised flooding overwhelming the main drainage system.

## Slide 14
Any questions?