## Slide 1: 6.3 Measurement standards, guidance and practice PowerPoint 7: BS1192
PowerPoint
6. Construction measurement principles

## Slide 2: BS1192: information naming and suitability codes
The BS1192 naming convention provides a ‘best practice’ guide, setting out how we’re supposed name everything – documents, drawings, models and data files.
It is part of the building information modelling (BIM) process.
It provides a template for common naming conventions for use in architecture, engineering and construction.
Using BS1192 means everyone will understand what something is and who has done it, from job to job to job.

## Slide 3: BS1192: understanding the codes
The codes used by the BS1192 system may look complex when strung together as shown in the example on the next slide. But, once you ‘translate’ them using the table, all should become clear.
The different code categories are then explained in detail in the slides that follow:
project
originator
volume or system
level and location
file type, role, classification, number, revision.

## Slide 4: Translating the codes …
Field | Project | Originator | Volume or System | Levels and Locations | Type | Role | Classification | Number | Revision
Example | ABCTRA | MB | AE | GF | DR | A | SL_18_57_26 | 0001 | 
Required or optional | Required | Required | Required | Required | Required | Required | Optional | Required | Optional
Characters | 2-6 | 3-6 | 1-2 | 2 | 2 | 1 character | To match the selected classification library | 4 integer numeric digits | 3 – with additional decimals for WIP
ABCTRA-MB-AE-GF-DR-A-SL_18_57_26-0001

## Slide 5: BS1192: project
Field | Project
Example | ABCTRA
Required or optional | Required
Characters | 2-6
This is an individual code for the project that will be used consistently throughout the project. Ideally the project code should be confirmed at the early stages of the project by all parties.
Some large jobs may consist of multiple projects.
The project code can be set up to have a main project number with sub-projects identified with an additional reference, eg
Main project code 101
Sub-project code 101a

## Slide 6: BS1192: originator
A unique code for each organisation, so that the originator of the file can be identified from the file name.
Field | Originator
Example | MB
Required or optional | Required
Characters | 3-6

## Slide 7: BS1192: volume or system
A project may have multiple buildings (such as a factory).
Buildings may be coded alphabetically and codes attached for services or the detail being described, eg
AE – Building A, electrical services
BS – Building B, steel structure
Field | Volume or System
Example | AE
Required or optional | Required
Characters | 1-2

## Slide 8: BS1192: levels and locations
Standard codes for levels
ZZ Multiple levels
XX No level
GF Ground floor
00 Base level
01 Level 1
M1 Mezzanine 1
M2 Mezzanine 2
B1 Basement 1
B2 Basement 2
Field | Levels and Locations
Example | GF
Required or optional | Required
Characters | 2

## Slide 9: BS1192: file type (for drawings and models)
AF Animation file
CM Combined model
DR 2D drawing
M2 2D model file
M3 3D model file
MR Model rendition file
VS Visualisation file
BQ Bill of quantities
CA Calculations
CO Correspondence
CP Cost plan
Field | Type
Example | DR
Required or optional | Required
Characters | 2

## Slide 10: BS1192: file type (for drawings and models)
DB Database
FN File note
HS Health & safety
IE Information exchange
MI Minutes or action notes
PP Presentation
PR Programme
RD Room data sheet
RI Request for information
RP Report
SA Schedule of accommodation
SH Schedule
SL Snagging list
Field | Type
Example | DR
Required or optional | Required
Characters | 2

## Slide 11: BS1192: role
.
A Architect
B Building surveyor
C Civil engineer
D Drainage, highways engineer
E Electrical engineer
F Facilities manager
G Geographical and land surveyor
H Heating and ventilation designer
I Interior designer
K Client
Field | Role
Example | A
Required or optional | Required
Characters | 1 character

## Slide 12: BS1192: role
L Landscape architect
M Mechanical engineer
P Public health engineer
Q Quantity surveyor
S Structural engineer
T Town and country planner
W Contractor
Y Specialist designer
Z General (non-disciplinary)
Field | Role
Example | A
Required or optional | Required
Characters | 1 character

## Slide 13: BS1192: classification
UNICLASS 2015 is a unified classification for the UK industry covering all construction sectors:
https://toolkit.thenbs.com/articles/classification/
Field | Classification
Example | SL_18_57_26
Required or optional | Optional
Characters | To match the selected classification library

## Slide 14: BS1192: number
Used if multiple files apply to the same project and link together (such as heating systems and lighting), eg
XYZ123-MSB-01-GF-DR-E-0001_GFHeating.pd
XYZ123-MSB-01-GF-DR-E-0002_GFLighting.pdf
Field | Number
Example | 0001
Required or optional | Required
Characters | 4 integer numeric digits

## Slide 15: BS1192: revision
The version of the file if revisions have been made.
Field | Revision
Example | 
Required or optional | Optional
Characters | 3 – with additional decimals for WIP

## Slide 16
Any questions?