## Slide 1: PowerPoint 3: Maintenance and post-occupancy data
8. Construction information and data principles
8.1 Data
8.2 Sources of information

## Slide 2: Data sources
There are a variety of data sources which are used in construction and building services engineering. Data from these sources can be used to understand behaviour, assess performance, improve market competitiveness, allocate resources and manage costs. In this presentation we look at:
maintenance and replacement systems
post-occupancy evaluation.

## Slide 3: Maintenance principles
Maintenance is carried out to:
  maintain structural stability and safety and prevent decay and degradation
  ensure availability of important assets
  prevent loss of core business due to failure of service systems.
  It can also prevent undesirable outcomes, such as:
        non-compliance with legal requirements
        customer dissatisfaction
        health and safety breaches
        inefficient and wasteful energy consumption
        environmental loss
        the excessive cost of catastrophic plant failures.

## Slide 4: Maintenance principles
Maintenance can also help to:
determine the causes of defects and help prevent reoccurrence or repetition
prevent unnecessary damage from the weather or from general usage
inform plans for renovation, refurbishment, retrofitting or new buildings
optimise performance of the building for its occupants.

## Slide 5: Maintenance types
Planned maintenance on a regular basis.
Preventive maintenance to maintain working order or extend life.
Corrective maintenance, eg repairs.
Front-line maintenance, eg repainting and decorating an occupied building.
Proactive maintenance undertaken to avoid failures or identify defects that could lead to failure.
Reliability-centred maintenance, combining maintenance strategies to ensure a physical asset continues to function correctly.
Scheduled maintenance, which is preventive maintenance carried out in accordance with predetermined intervals, number of operations, hours run, and so on.

## Slide 6: Computerised managed maintenance system (CMMS)
A CMMS is a computer-based software information source for maintenance management.
It evolved in the late 1980s and early 1990s as building professionals began to use computer-aided design and facilities management (CAFM) tools.
CMMS helps organise and automate the record-keeping process. As a type of work order management system, CMMS uses data collected from equipment located throughout a facility to monitor inventory, track work orders, generate reports and initiate preventive maintenance actions.

## Slide 7: Work order management systems and CMMS
Work order management systems use a dashboard to track and manage relevant maintenance projects and processes for facilities managers.
Such systems are suitable for multi-site organisations and can be integrated with enterprise asset management software (EAM) or CMMS.
CMMS can also help maintenance planners, engineers and supervisors to schedule, monitor and execute maintenance tasks in compliance with regulations and health and safety requirements.

## Slide 8: Replacement systems
In some circumstances there will be a requirement to carry out the full replacement of a system. This could be for a number of reasons such as:
non-availability of spare parts during maintenance
investment in buildings
upgrades to meet current energy efficiency legislation
building grants.
A full redesign of the replacement system should be undertaken to ensure it is fit for purpose, meets current British Standards (BS) and building regulations and takes into consideration any existing data collected on the building during its use.

## Slide 9: Handover and maintenance of built assets
It is usually only after handover and with the building in operation that the building services engineering systems are truly tested against client expectations. Often, operational issues arise when people use and occupy the building after handover.
It is important that buildings are not handed over in a poor state of operational readiness. This can be a risk when programme delays have led to short testing and pre-handover periods.

## Slide 10: Handover and maintenance
Handover should involve building services engineers, other members of the design team, the construction team, operators and commissioning and control specialists, in order to strengthen the operational readiness of the building. This includes verifying that all handover documentation is completed to a satisfactory standard and is adequate.

## Slide 11: Post-occupancy evaluation (POE)
Post-occupancy evaluation is a useful source of data about building performance. To gain meaningful insights, it is essential to measure variables before changes are made to establish a baseline and make comparisons after a project has been completed. During a POE two main types of data are collected:
Quantitative (numerical) data collected directly, or information transformed into numerical data, such as measures of energy and water consumption. This stage also includes questionnaire ratings or yes/no tick box responses.
Qualitative (non-numerical) data: text-based data used to provide deeper insight, meaning and context. It may include feedback from interviews, observations, focus groups, case studies and comments provided in questionnaires. Taken alongside quantitative data, the human voice in qualitative data can provide rich information and explain the reasons behind the numbers.

## Slide 12: POE
Continuing to undertake reviews at agreed intervals allows data to be captured on how ways of living or working in a building change, and to identify new issues that may arise.

## Slide 13: Pros and cons of POE
Method | Advantage | Disadvantage
Observations, eg space use audits, energy walkabouts | Requires few staff resources Reveals problems not noticed Can be carried out over a specific period | Comparison can be difficult Viewpoint can be biased
Occupant consultation questionnaires | Obtains detailed data Enables large-scale participation Obtains broad-based opinion | Requires expertise in statistics Requires staff time to complete
Occupant consultation interviews | Allows a range of aspects to be considered Can be restricted to key personnel | Viewpoint can be biased Can be time consuming

## Slide 14: Pros and Cons of POE
Method | Advantage | Disadvantage
Audits | Collection of data from meters Can refer to EPC for information | Not always easy to locate Calibration can cause gaps in data
Workshops/ discussions | Takes minimal management time Issues can be explored by the group Can involve fewer staff | Requires expertise in facilitation Can be time consuming Removes anonymity
Organisational performance measures | Data is already collated Measures can be identified from building | High-level data required Documentation Can be time consuming

## Slide 15
Any questions?