## Slide 1: PowerPoint 6: Certification, commissioning data, test data and condition reports
8. Construction information and data principles
8.2 Sources of information

## Slide 2: Local Authority Building Control (LABC) certification
The system of Local Authority Building Control (LABC) issues completion certificates and/or inspection letters which confirm reasonable steps have been taken that work complies with building regulations.
If the building control inspection was carried out by the local authority, there will be an inspection letter, a completion certificate (if applicable) or a ‘full plans approval notice’.
If the building control inspection is carried out by an approved inspector, they will provide copies of initial notices, plans or final certificates directly.

## Slide 3: Self-certified work
Where works have been carried out by a member of a competent person scheme (eg electrical, plumbing or gas-related works), the certification is via the relevant scheme operator. For example, double glazing is certified by FENSA: Welcome to FENSA | Find Local Double Glazing Installers; cavity wall insulation is certified by CIGA CIGA | Cavity Insulation Guarantee Agency; and plumbing and heating contractors by APHC Support for Plumbing Contractors | APHC | Support for Heating Contractors.
A full list can be found here:
https://www.gov.uk/guidance/competent-person-scheme-current-schemes-and-how-schemes-are-authorised#current-schemes

## Slide 4: Construction contract certification
Once a building project has met all the requirements of the construction contract and the defects liability period is over, the contract administrator issues a final payment certificate to the contractor.
The value of this certificate is based on the agreed final account. All defects must have been remedied and all claims settled for this certificate to be issued.
In construction management contracts, where there are a number of trade contracts, final statements are issued for each contract. Once final statements have been issued, the construction manager coordinates preparation of the final report and issues the final certificate for the whole project.

## Slide 5: Final payment certificate

## Slide 6: Energy Performance of Buildings Regulations 2012
The Energy Performance of Buildings (Certificates and Inspections) (England and Wales) (Amendment) Regulations 2012 (SI 2012/809) consolidate and revoke all previous regulations, and lay down the requirements for the production of:
domestic energy performance certificates (EPCs)
commercial/non-domestic energy performance certificates (also EPCs)
display energy certificates (DECs)
air-conditioning inspection reports (ACIRs).
All the underlying data is lodged on a central register once the EPC has been completed by an accredited domestic energy assessor. The EPC register also contains a database of all accredited domestic energy assessors.

## Slide 7: EPCs
  An EPC is a prediction of how energy efficient a property can be.
  A is the highest rating that can be achieved (most efficient).
  The EPC register is managed by the Landmark Trust on behalf of the government. The Trust also holds a register of domestic energy assessors.
  Registered EPCs are available to view or download free of charge. You can search by property address or by the Register’s RRN reference number.
  Some buildings are exempt, such as places of worship, temporary buildings or listed buildings.

## Slide 8: Domestic EPCs
EPCs are needed whenever a property is built, sold or rented. An EPC gives a property an energy efficiency rating from A (most efficient) to G (least efficient).
An EPC contains:
information about a property’s energy use
typical energy costs
recommendations about how to reduce energy use and save money.
Notes: See: https://www.ricsfirms.com/glossary/energy-performance-certificates-epcs

## Slide 9: Commercial EPCs
A commercial EPC rates how energy efficient the building is, using grades from A to G (with ‘A’ the most efficient grade). A commercial EPC is needed if:
premises are rented out or sold
a building under construction is completed.
A commercial EPC shows the energy rating of the building, indicating the energy efficiency of the fabric and the heating, ventilation, cooling and lighting systems. The rating is compared with two benchmarks: one appropriate for new buildings and one for a similar existing building. Also shown is a unique report reference number assigned to the EPC when it is lodged on the non-domestic EPC register. Those who don’t make an EPC available to any prospective buyer or tenant will be fined between £500 and £5,000 based on the rateable value of the building.

## Slide 10: Display energy certificate (DEC)
A DEC provides a building with a rating from A–G that is benchmarked against all other buildings of that type within the UK. This rating is based on operational performance and uses actual energy consumption data over a 12-month period.
DECs were introduced in 2008 and form part of the implementation of two European Directives. Post-Brexit a new UK register has been created by the government to achieve the same ends. DECs are a legal requirement for all public buildings with a usable floor space over 250m2. In the private sector, DECs are voluntary.

## Slide 11: Commissioning
Commissioning is the process of bringing installed building control systems, such as heating, ventilation and air conditioning into operation and ensuring their purpose is met efficiently. Contract documents should define who is responsible for each aspect of commissioning and:
whether it will be witnessed
the methods that should be used
the standards that should be adopted
required documentation.
A comprehensive guide (BG 8/2009) is available from the Building Services Research and Information Association (BSRIA).

## Slide 12: Commissioning
The following systems need to be commissioned and tested:
HVAC
plumbing
electrical and control
specialist (eg lifts, escalators, medical gas systems, etc).

## Slide 13: Information and data phases
Building services engineers are involved throughout the commissioning process, overseeing installation, carrying out tests and managing the many sources of information and data required by the commissioning team.
Preparation phase: developing an outline scope and budget for the commissioning of systems.
Design phase: input into creation of schematics, detailed drawings, installation wiring diagrams and method statements.
Pre-construction phase: ensuring the commissioning information is clear, complete and fully coordinated; attending tender meetings to communicate all information relating to the commissioning process.

## Slide 14: Information and data phases
Construction phase: verifying technical submittal and installation drawings for compliance with the commissioning specifications, preparing equipment and systems tracking forms, preparing verification checklists, logging and reporting construction issues on issue tracking forms.
Commissioning of engineering services phase: carrying out pre-performance tests, performance tests and review.
Pre-handover phase: checking warranty documents, as-built documents, control layouts and schedules, training documents and technical manuals ready for handover. Submitting an interim commissioning report.

## Slide 15: Information and data phases
Initial occupation phase: carrying out a survey logging the occupants’ feedback, helping occupants to fine-tune the building systems as required.
Post-occupancy phase: seasonal system tests and review, submission of final commissioning report, signing off the project.

## Slide 16: Condition reports
A condition report is a detailed report based on a close examination of the structure and condition of a building and a visual examination of the services.
It provides advice on the nature of the construction, the current condition and any defects, along with a diagnostic assessment with recommendations for repairs needed and likely future maintenance issues.

## Slide 17: Condition reports
A landlord may have invested in bringing a property into good tenantable condition prior to letting. If a tenant has not maintained the building, the commission of a condition report will help justify and resolve a claim for dilapidations at the end of the lease. This can save time and money in resolving alleged disrepair and associated legal fees.
Below is an example of the headings that can be used in a condition report.
Element | Material | Location | Comment on defect | Remedial work | Condition rating | Priority rating | Cost | Photo ref.
Door | Wooden | Lounge | Hole in wooden door panel | Replace door | Poor | High | £1,000 | 

## Slide 18
Any questions?