## Slide 1
1. Health and safety in construction
1.1 Construction legislation and regulations
PowerPoint 1: Construction legislation and regulations

## Slide 2: Objectives
By the end of the session, learners should be able to:
  identify health and safety legislation for protecting the workforce and members of the public while working in the construction industry
  define the responsibilities of members of the construction team
  describe the legal status of health and safety guidance materials and the penalties for non-compliance
  identify the role of health and safety enforcing authorities
  understand the role of health and safety inspectors.

## Slide 3: Health and Safety at Work Act 1974
The Health and Safety at Work Act (HASAWA) 1974 embodies the requirements for the management of health and safety at work, and covers:
  all people at work (i.e. employers/employees)
  the self-employed
  the general public
  all people and activities.

## Slide 4: HASAWA 1974
The main objectives of HASAWA 1974 are:
  health and safety of all people at work
  the protection of others from risks at work
  the control of dangerous substances
  the control of dangerous emissions.

## Slide 5: HASAWA 1974
  The Act makes health, safety and welfare everyone’s responsibility.
  Employers have a responsibility to provide personal protective equipment (PPE), eg hard hats, gloves, eye protection, safety footwear etc.
  A health and safety policy must be produced if a company employs five or more employees.

## Slide 6: Responsibilities of the construction team
HASAWA relates to all people at work whether they are employers, employees or the self-employed.
It is specifically aimed at people and their activities at work rather than premises or processes.
It includes provisions for both the protection of people at work and members of the general public who may be at risk as a consequence of workplace activities.
The main objectives of HASAWA state that everyone has duties and responsibilities regarding health and safety: the worker, each contractor, the architect, the client, the main contractors, the subcontractors, employees, the self-employed (labour only) and the owner of the building being built.

## Slide 7: Responsibilities of the construction team
Employers
For example, HASAWA deals specifically with the general duties of the employer towards their employees, stating that the employer must, as far as possible, ensure the health, safety and welfare of those in their employment.
This legislation also states that employers must have a health and safety policy and that, if the company has more than five employees, that policy must be written down.
The policy must be revised as necessary at regular intervals and all employees must have access to and be informed of any changes made to the policy.

## Slide 8: Responsibilities of the construction team
Employers
In addition, HASAWA tells us that all employers must:
  carry out risk assessments of all the company’s work activities
  identify and implement adequate control measures
  inform all employees of the risk assessments and associated control measures
  review the risk assessments at regular intervals
  make a record of the risk assessments if five or more operatives are employed.

## Slide 9: Responsibilities of the construction team
Every employer and self-employed person must give information to those people who are not in their employment about the way in which aspects of their work might affect the health and safety of others.
Every employer must consult with health and safety representatives. These people are appointed by the employees of an organisation to act on their behalf.
Their role is to make and maintain arrangements that will enable the employer and employees to promote and develop health and safety measures, as well as checking their effectiveness.

## Slide 10: Health and safety publications
Health and safety publications can be divided into two distinct groups: mandatory (must be followed by law) and advisory (guidance which is recommended but not legally enforceable).
Mandatory publications include:
  Acts of Parliament – also known as statutory legislation. Such Acts create a new law or change an existing one. Their implementation is the responsibility of a specific government department. In the case of health and safety Acts, this is the Health and Safety Committee. Acts are legally enforceable and must be followed to avoid prosecution.
  Regulations or non-statutory legislation. Rules, procedures and administrative codes set by authorities or government agencies to achieve a particular objective.

## Slide 11: HSE guidance notes
These are produced by the Health and Safety Executive (HSE) to help people interpret and understand what is required by law, and to comply with it.
They also give technical advice.
The course of action set out in guidance notes is not compulsory, but if the guidance is followed it is usually enough to comply with the law.

## Slide 12: Approved Codes of Practice (ACOPs)
These documents offer practical guidance on complying with regulations.
ACOPs are supplementary to regulations and give examples of how to comply with the law. Employers who have not followed an ACOP and who are prosecuted for a breach of health and safety law are likely to be found at fault by the courts.
Following an ACOP is considered good practice.

## Slide 13: HASAWA 1974
Employees
The duties of the employee are:
  to take reasonable care of the health and safety of themselves and others
  to comply with the employer’s health and safety policy
  not to recklessly interfere with anything that may affect health and safety.

## Slide 14: Enforcing authorities
Health and Safety Executive (HSE)
HSE inspectors can:
  inspect sites
  give guidance and advice on work or processes
  take photos and samples
  talk about and discuss situations and/or problems
  seize evidence, equipment or materials.

## Slide 15: Rreporting of Injuies, Diseases and Dangerous Occurrences Regulations (RIDDOR)
RIDDOR is a piece of health and safety legislation that was updated in 2013. It introduced significant changes to the previous reporting requirements in order to simplify them.
RIDDOR applies to every workplace and puts duties on employers, the self-employed and people in control of work premises (the ‘responsible person’) to report and keep records of:
  work-related accidents which cause death or serious injuries (reportable injuries)
  certain ‘dangerous occurrences’ (incidents with the potential to cause harm)
  diagnosed cases of certain industrial diseases.

## Slide 16: Control of Substances Hazardous to Health (COSHH) Regulations
COSHH is a set of regulations put in place to protect workers from ill health when working with specific substances and materials.
A breach of COSHH regulations by an employer or employee is a crime, punishable by an unlimited fine. The regulations:
  protect against illness caused by hazardous substances
  help to prevent, control and monitor exposure to hazardous substances
  stipulate the risk assessment of working practices
  describe precautions
  Training is provided where necessary.

## Slide 17: Control of Asbestos Regulations
The Control of Asbestos Regulations 2012 set minimum standards for the protection of employees from risks related to exposure to asbestos. Employers should also take account of people not directly employed by them but who could be affected by the work being done on asbestos (including employees of other employers, people occupying buildings, members of the public etc). Awareness training can be provided as required.
  Use of asbestos is prohibited.
  Asbestos may be left in place if in good condition and labelled. The risk still needs to be managed by the building’s custodian, such as employing stickers and signs to indicate where asbestos may be present.
  Asbestos must be removed by a licensed contractor.

## Slide 18: Construction (Design and Management) (CDM) Regulations 2015
CDM Regulations are designed to improve health and safety in the industry by helping employers to:
  ensure that fixed and portable electrical equipment is tested and maintained
  sensibly plan the work so that risks are managed from start to finish
  have the right people for the right job at the right time
  cooperate and coordinate work with others
  have the right information about the risks and how they are being managed
  communicate this information effectively to those who need to know
  consult and engage with workers about the risks and how they are being managed
  appoint a CDM coordinator.

## Slide 19: Provision and Use of Work Equipment Regulations (PUWER) 1998
The PUWER Regulations 1998 place duties on people and companies who own, operate or have control over work equipment (eg hand and power tools).
PUWER also places responsibilities on businesses and organisations whose employees use work equipment – whether owned by them or not – such as ensuring competency of persons operating tools, effective guards and protection to the user.

## Slide 20: PUWER
PUWER requires that equipment provided for use at work is:
  suitable for the intended use
  safe for use, maintained in a safe condition and inspected to ensure it is correctly installed and does not subsequently deteriorate
  used only by people who have received adequate information, instruction and training
  accompanied by suitable health and safety measures, such as protective devices and controls – these will normally include guarding, emergency stop devices, adequate means of isolation from sources of energy, clearly visible markings and warning devices
  used in accordance with specific requirements, for mobile work equipment and power presses.

## Slide 21: Manual Handling Operations Regulations (MHOR) 1992, amended 2002
These cover the following activities:
  lifting, lowering, pushing, pulling, moving or carrying a load
  Individuals should conduct a risk assessment first. Lifting operations should be planned in advance. Employees have a responsibility to use mechanical aids as required in order to avoid injury.
Source:

## Slide 22: Personal Protective Equipment (PPE) Regulations 1992
Wherever there are risks to health and safety that cannot be adequately controlled in other ways, the PPE at Work Regulations require PPE to be supplied by the employer to the employee.
The Regulations also require that PPE is:
  properly assessed before use to make sure it is fit for purpose
  maintained and stored properly
  provided with instructions on how to use it safely
  used correctly by employees.

## Slide 23: Work at Height Regulations 2005
Working at height means working in any place where, if there were no precautions in place, a person could fall a distance liable to cause personal injury.
The following will mitigate against falling from height:
guards and fall arresters
harnesses
planning of work
risk assessment
equipment inspections.

## Slide 24: Control of Noise at Work Regulations 2005
The aim is to ensure that workers’ hearing is protected from excessive noise at their place of work, which could cause them to lose their hearing and/or to suffer from tinnitus (permanent ringing in the ears).
The level at which employers must provide hearing protection and hearing protection zones is 85 decibels (daily or weekly average exposure).

## Slide 25: Environmental regulations
There are numerous environmental laws in the UK that cover everything from flytipping, littering and pollution to wildlife, conservation, climate change, noise and planning. However, knowing or understanding which law pertains to what aspect of the environment can be difficult.
Splitting regulations into different categories can help.
Pollution/environment
  Control of Pollution Act
  Environmental Protection Act

## Slide 26: Environmental regulations
Conservation
  Planning (Listed Buildings and Conservation Areas) Act
  Countryside and Rights of Way Act
  Climate change
  Climate Change Act 2008
  Planning and Energy Act 2008
  Energy Act 2020

## Slide 27: Environmental Protection Act
Waste management in construction
Any waste generated on site will normally need to be stored for a period of time before collection. Employers have a legal responsibility to ensure waste is stored safely. Regulations require the following actions.
  Pre-treatment – ie sorting recyclable and non-recyclable material. This can be on-site or completed by a registered waste collector at a sorting facility.
  Safe on-site storage for all waste.
  Waste must be collected by a registered waste carrier.
  Disposal of waste must take place at a licensed waste disposal facility.
  Waste must be covered by a waste transfer note.

## Slide 28: Construction (Health, Safety and Welfare) (CHSW) Regulations
These are directly related to the provision of welfare facilities during construction work. For example:
  toilets
  washing facilities
  drinking water
  heating
  changing rooms
  lockers
  rest facilities
  eating facilities.

## Slide 29
Any questions?