## Slide 1: PowerPoint 1: Internet of things
PowerPoint
10. Digital technology in construction
10.1 Internet of things

## Slide 2: The internet of things (IoT)
The internet of things describes the concept of connecting everything to everything else using the internet.
Research suggests there will be 75 billion internet connected devices, such as televisions, cameras, home assistants, sensors and their associated services, in homes around the world by the end of 2025.
These devices record the data that is so important for processing information and are like the ‘eyes and ears’ of the IoT.
John Moor, Managing Director, IoT (Internet of Things) Security Foundation said:
‘Over the past five years, there has been a great deal of concern expressed toward vulnerable consumers and inadequate cybersecurity protection. Understanding the complex nature of IoT security and determining the minimum requirements has been a challenge, yet, after a thorough and robust consultation, those baseline requirements have now been universally agreed.’
.
Notes: Source:
Published 27 January 2020
Department for Digital, Culture, Media & Sport, National Cyber Security Centre, and Matt Warman MP

## Slide 3: The internet of things (IoT)
Plans for a new law, drawn up by the Department for Digital, Culture, Media and Sport (DCMS), will ensure all consumer smart devices sold in the UK adhere to the three rigorous security requirements for the internet of things (IoT). These are:
All consumer internet-connected device passwords must be unique and not resettable to any universal factory setting.
Manufacturers of consumer IoT devices must explicitly state the minimum length of time for which the device will receive security updates at the point of sale, either in store or online.
Manufacturers of consumer IoT devices must provide a public point of contact.
Notes: https://www.gov.uk/government/news/government-to-strengthen-security-of-internet-connected-products

## Slide 4: The internet of things (IoT). Examples from the code
Monitor system telemetry data: If telemetry data is collected from IoT devices and services, such as usage and measurement data, it should be monitored for security anomalies.
Securely store credentials and security-sensitive data: Any credentials shall be stored securely within services and on devices. Hard-coded credentials in device software are not acceptable.
Ensure software integrity: Software on IoT devices should be verified using secure boot mechanisms. If an unauthorised change is detected, the device should alert the consumer/administrator to an issue and should not connect to wider networks than those necessary to perform the alerting function.
No default passwords: All IoT device passwords shall be unique and not resettable to any universal factory default value.
Notes: https://www.gov.uk/government/news/government-to-strengthen-security-of-internet-connected-products

## Slide 5: Smart cities
S.M.A.R.T. is defined as ‘Self-Monitoring, Analysis and Reporting Technology’. The catalyst for smart cities is population growth, with the majority of the population becoming more urbanised.
Cities as well as buildings need to deploy electronic and internet services. This may be smartphone apps for finding your way in a building or a city, for example, as well as interacting with a city official or a building manager electronically, basically providing convenience.
Cities need adequate energy supplies. Energy also affects the environment of a city and the cost of living. The city’s utility grid needs to communicate with the city’s buildings and the power grid.
Cities need to deploy intelligent traffic systems such as traffic signal control systems, license plate recognition, and real-time data from other systems to utilise predictive analytics in reducing travel times.

## Slide 6: Smart building
By connecting all building service systems to a smart software platform via a secured LAN or WAN network, every single one of them can be controlled and monitored from one central location (control room). Sometimes, an operator is needed to make decisions, but often the technology and software behind the systems is smart enough to operate autonomously.
Many processes and critical situations are handled in the control room. Different sectors are characterised by different types of processes and critical events. Most organisations will have the main processes such as fire detection, HVAC, access control and CCTV, with many including systems such as rainwater harvesting, exterior shading, water reclamation, electric switchable glass, sun tracking systems, etc.
The physical facilities may be spread out over many sites, cities, countries or even worldwide. In some cases, the control can be part of a larger command centre, e.g. Ministry of Defence.

## Slide 7: Management dashboards
The Direct Digital Control (DDC) of an HVAC system is a method of monitoring and controlling the HVAC system performance by collecting, processing, and sending information using sensors, actuators, and microprocessors. These centralised BAS controls (dashboards) transform data into useful information. A point is any input or output device used to control the overall or specific performance of equipment related to the equipment.
Building automation systems (BAS) centralised controls show:
change scheduling for multiple HVAC units at the same time
monitor ‘health’ of equipment
internet accessible
alarm or fault notification can be via text message or email
they can collect trend data
they can integrate to lighting control or security system.

## Slide 8: Types of points
Analog input – a sensor that monitors physical data, such as temperature, flow, pressure, humidity, voltage, current, CO2.
Discrete input – a sensor that monitors status, e.g. momentary and maintained switches, on/off equipment status, and digital pulses from flow and electric power meters.
Analog output – a physical action of a proportional device in the controlled equipment, e.g. actuator opens air damper from 20%–40%, other dampers, valves, inlet guide vanes, etc.
Discrete output – changes or maintains device status. Performs momentary or maintained switching for start/stop of pumps, fans, two-position dampers, solenoid valves, relays, alarm signal and on/off control.

## Slide 9: Building automation systems (BAS)
The building automation industry has a long history of global communication protocols in the market.
Facility managers already have the tools to take their buildings to a higher and more valuable level of building automation.
Leading manufacturers are now working towards developing IP-based communication standards that can work alongside the existing communication standards.
Wireless technologies, such as 5G and Wi-Fi-6 are likely to have a greater impact on the connectivity of building technologies and are likely to accelerate the growth of IoT devices and applications in the building automation space.

## Slide 10: Building automation systems (BAS) and AI
The application of artificial intelligence (AI) or machine learning (ML) could also be used in building automation.
A smart device executes tasks automatically without user inputs. An intelligent device extracts knowledge from data and past usage in order to improve its behaviour using artificial intelligence (AI). This means an intelligent device is usually smart too, but a smart device is not necessary intelligent.
AI can bring intelligence to the unstructured data from connected devices.
IoT and AI may connect together in building automation space to bring about improved operations, efficiency, and lower costs across building platforms in a wide range of application areas such as facility management, security, and safety management.
Notes: For more information see: https://www.prnewswire.com/news-releases/global-analysis-of-building-automation-systems-open-communication-protocols-role-of-emerging-technologies-in-the-bas-space-301166308.html

## Slide 11: Smart maintenance
Smart maintenance is predictive, which means faults can be identified and repaired before they occur in a seamless process. It is arguably one of the biggest advantages of intelligent buildings’ use of measuring and monitoring tools. By gathering all this accurate, real-time data, building service engineers can also get important information about the status and functionality of things like HVAC systems, lighting, computer systems and so on.
The first step is to start gathering data using sensors that provide real-time measurements of electricity, water, sound, vibration, temperature and more to monitor the condition of your equipment.
You can use this data to make intelligent decisions about your existing maintenance strategy, determining whether changes in the condition of equipment can be used to discover why faults occur, and introduce predictive maintenance to fix problems before they occur.

## Slide 12: Smart maintenance
Smart maintenance is made possible by the internet of things (IoT). This enables an unparalleled level of connectivity, giving building managers the ability to gather data on things like vibration, temperature, fuel levels and acoustics from thousands of devices in real-time, via both wired and wireless networks.
This IoT-connected equipment can be linked to a ‘computerised maintenance management system’ (CMMS), which uses data analytics to predict and identify faults using the data gathered by the equipment and communicate that information to staff. Building managers can use a CMMS to manage upgrades and maintenance quickly and efficiently and share that data easily to colleagues and technicians. In turn, technicians can use cloud systems to access that information on their mobile devices in the field.

## Slide 13: The benefits of smart maintenance
Smart maintenance offers several benefits:
Increased productivity – technicians work more efficiently because the data and information they receive is more accurate and they can respond to faults more quickly.
Reduced maintenance costs – downtime is expensive. Smart maintenance systems reduce or eliminate it, meaning less money is spent on costly repairs and replacements, as well as labour.
Extended equipment lifetime – by keeping it maintained and avoiding serious breakages, equipment can last for much longer without replacement.
4. Remaining compliant – smart maintenance ensures your firm remains compliant with various international and national standards for maintaining equipment, particularly the ISO 55000 standard for asset management.
Improved maintenance and management of assets can reduce energy consumption and environmental impact.
Notes: For more information, see https://www.intelligentbuildingeurope.com

## Slide 14: Just-in-time (JIT)
What is just-in-time (JIT)?
The right materials are supplied in the right order, in the right amount at the right time. The deliveries tend to be regular and in small amounts. The process is also known as ‘just-in-time production’. In recent years, the term has been used synonymously with lean manufacturing.
The JIT concept is a manufacturing workflow methodology aimed at reducing flow times and costs within production systems and the distribution of materials.
.

## Slide 15: Just-in-time (JIT)
The concept was popularised by the productivity of Japanese industry in the early 1970s within the Toyota manufacturing plants that would meet consumer demands with minimum delays using an approach focused on people, plants and systems.
The prime goal of JIT is for zero inventories across the organisation and its supply chain. This completely utilises the organisational capabilities and maximizes ROI. The system was so successful in Japan it was copied by many US companies, most notably Hewlett-Packard.
.

## Slide 16: Advantages and disadvantages of JIT
What are the advantages of JIT?
Elimination of waste in production.
The JIT approach can reduce the cost of inventories and inventory requirements and reduces the requirement for storage space.
JIT can create a stabilised work schedule.
JIT can establish long-term supplier-customer relationships.
What are the disadvantages of JIT?
Does not cope well with sudden changes to demand and supply.
You must develop a purchasing philosophy on supporting frequent small purchases.
Implementing the system can be challenging and time-consuming.
Must encourage and ensure employee discipline.
Purchasers may not get the benefit of discount for bulk purchases.

## Slide 17: Smart building asset management
On average, 50% of the available space in a typical office building is unoccupied over the course of a business day. Smart asset management uses
energy-harvesting wireless room sensors to supply information on how building areas and rooms are being used.
These sensors supply detailed information on usage patterns during normal operation as well as events, and they also consider differences in times of day and seasonal effects.
The smart and intelligent building asset management information is then used to establish the requirements for the optimum management of resources in terms of:
          space,
          personnel and
          objects.

## Slide 18: Asset management
The use of smart asset management can drive down operating costs, fixed and working capital and push up revenue and output.

## Slide 19: Smart concrete
Smart concrete is infused with potassium ions, allowing it to store electricity which can be released at times of peak demand.
When energy production levels drop, the concrete powers a house using the reserve stock of energy it has saved up.
Capacitors hold less energy by volume than batteries, but there is far more volume available if smart concrete is widely used as a building material.
The KGP capacitors can store power up to 0.33 kW/m2, enough to power systems such as health monitoring sensors, LED light poles and internet of things devices.

## Slide 20: Artificial intelligence in construction
There are artificial intelligence (AI) and machine learning (ML) solutions that contractors can use to monitor and prioritise risk on the job site, so the project team can focus time and resources on the biggest risk factors.
AI can develop safety systems that track the real-time interactions of workers, machinery, and objects on site, alerting supervisors to potential safety issues. AI is used to automatically assign priority to issues.
Self-driving construction machinery can perform repetitive tasks more efficiently than their human counterparts, such as pouring concrete, bricklaying, welding, and demolition.
Excavation and prep work is being performed by autonomous or semi-autonomous bulldozers, which can prepare a job site to exact specifications with the help of a human programmer, freeing up workers for the construction work itself and reducing the overall time required to complete the project.

## Slide 21: Artificial intelligence in construction
Labour shortage and a desire to boost the industry’s low productivity are compelling construction firms to invest in AI and data science. A 2017 McKinsey report says that construction firms could boost productivity by as much as 50% through real-time analysis of data.
AI can be used on projects to predict cost overruns based on factors such as project size, contract type and the competence level of project managers.
Historical data such as planned start and end dates are used by predictive models to envision realistic timelines for future projects.

## Slide 22: Artificial intelligence and BIM
3D BIM models need to take into consideration the architecture, engineering, mechanical, electrical, and plumbing (MEP) plans and the sequence of activities of the respective teams.
The challenge is to ensure that the different models from the sub-teams do not clash with each other.
Machine learning can be used in the future to identify and mitigate clashes between the different models generated by the different teams. This could prevent costly and time-consuming rework.

## Slide 23: Artificial intelligence in offsite manufacturing
Construction companies are increasingly relying on offsite factories staffed by autonomous robots that piece together components of a building, which are then pieced together by human workers onsite.
Structures like walls can be completed assembly-line style by autonomous machinery more efficiently than their human counterparts, leaving human workers to finish the detail work like plumbing, HVAC and electrical systems when the structure is fitted together.
Notes: For an interesting insight into robots in construction see: How Robotics Will Change the Construction Industry (automate.org)

## Slide 24
Any questions?