## Slide 1: PowerPoint 2: Sustainable solutions
PowerPoint presentation
5.2 Types of sustainable solutions

## Slide 2: Three pillars of sustainability
Sustainability is most often defined as meeting the needs of the present without compromising the ability of future generations to meet theirs.
Sustainability has three main pillars:
Economic
Environmental
Social

## Slide 3: Environmental factors
Protection of habitats and species
Use of fewer finite resources
Clean air and water
Reduced pollution
Minimisation of waste

## Slide 4: Social factors
Improved quality of life
Improved equality
Ending wars and conflicts
Ending poverty
Building communities

## Slide 5: Economic factors
Economic equality
Improved economic growth
Whole life costing
Reduced poverty

## Slide 6: Sustainable cities – social, economic and environmental
Social development | Economic development | Environmental development
Education and health | Green productive growth | Forest & soil management
Food and nutrition | Creation of decent employment | Waste & recycling management
Green housing & buildings | Production/distribution of renewable energy | Energy efficiency
Water & sanitation | Technology & innovation | Water management
Green public transport |  | Air quality conservation
Green energy access |  | Adaptation to & mitigation of climate change
Recreation spaces & community support |  | 

## Slide 7: Sustainable solutions

## Slide 8: Sustainable solutions

## Slide 9: Prefabricated construction
Prefabricated buildings consume less energy and water and produce fewer emissions during the construction phase of a project than traditional labour-intensive construction methods.
Examples of prefabrication:
Roof trusses
SIPs (structural insulated panels)
Smart panels
Modular building construction
Moveable buildings

## Slide 10: Self-healing concrete
Concrete is one of the most widely used building materials. Self-healing concrete has the ability to repair cracks autonomously. Self-activating bacteria are incorporated into the concrete to make it self-healing.
The use of self-healing concrete means that buildings are more durable and have longer life-spans, which makes it a sustainable option. It reduces the amount of new concrete produced and reduces maintenance and repair costs that traditionally can be costly.

## Slide 11: Sustainable materials
Sustainability is now a key consideration in all construction projects. The materials we use in modern buildings and refurbishments should make a sustainable contribution to the environment and minimise negative impacts. Materials should be replenished, recyclable and reusable at the end of the life span of a building.
Benefits of using sustainable materials:
Reduced reliance on finite resources
Can be replenished and reused
Reduced energy costs
Reduced carbon footprint

## Slide 12: Sourcing materials
By specifying and sourcing materials locally, the environmental costs and carbon emissions will be reduced. This will reduce congestion on the UK road systems and reduce the amount of CO2 emitted while transporting goods to the site. Sourcing locally will also help to boost local economic growth.

## Slide 13: Recyclable building materials
There are a range of building materials that can be recycled including:
Plasterboard
Aggregates
Bricks and blocks
Insulation
Glass
Tiles and slate

## Slide 14: Green roofs
Green roofs are covered with plants and vegetation. These are laid over a drainage layer. There are additional layers that provide protection, waterproofing and insulation.
Benefits:
Reduced rainwater runoff
Provision of habitats
Improved air quality
Regulated indoor temperatures

## Slide 15: Smart glass
Smart glass is an innovative building material that is made from electrochromic glass.
When an electric current is applied, the properties of the glass and the aesthetics change. Smart glass adjusts to changes in sunlight throughout the day and can switch between being transparent and being opaque.
Smart glass helps to insulate buildings and regulate inside temperatures, which creates savings in energy costs.

## Slide 16: Insulation
Insulation is a key component of the design of a sustainable building. A well-insulated building reduces energy bills and heat loss. Roofs, walls and floors are areas that require insulation and there are many different products available.
Traditional forms of insulation such as fibre glass and mineral wool contain chemicals and have high embodied energy values. Natural insulation products such as sheep's wool, flax and hemp are more sustainable alternatives.

## Slide 17: Hardwood vs softwood
Hardwoods are often more expensive and sometimes more challenging to work with.
Hardwoods will last longer than softwoods.
Hardwoods are more likely to be found in high-quality furniture, decking, flooring, and construction that needs to last.
Hardwoods are generally far more resistant to decay than softwoods when used for exterior work.
Softwoods are cheaper and easier to work with than hardwoods.
Softwoods make up the bulk of all wood used in the world, with about 80% of all timber being a softwood.
Softwoods have a lighter colour.

## Slide 18: Sustainable timber
Sustainably sourced timber is one of the most environmentally friendly building materials. Timber is a versatile renewable material that has a low embodied energy.
Cedar boarding and cladding
Cedar is a softwood that is light in weight and has a relatively low density. It is one of the most suitable timbers to use for exterior cladding as it is stable and not prone to weathering. This lightweight species lasts a long time and is easy to maintain.

## Slide 19: FSC timber
FSC (Forest Stewardship Council) check and certify forests worldwide.
To be FSC certified, a forest must be managed according to high environmental and sustainable standards.
Timber from FSC certified forests is marked with the FSC logo.
The FSC also manage a chain of custody tracking of FSC timber from forest through manufacture to end user, to ensure that the FSC label is correctly applied to products.

## Slide 20: Timber products
Engineered and eco joists
Chipboard, plywood etc
Structural insulated panels

## Slide 21: Grey water harvesting systems
Grey water is waste water from baths, showers, washing machines and dishwashers.
Water used to flush toilets is ‘blackwater’ and is much harder to treat.
Greywater can be recycled in the home for use in watering gardens, flushing toilets or washing clothes – but NOT for drinking water as it would not be safe.
Different systems can use the water directly (e.g. for watering plants) or can partially treat it so that it can be used for other tasks such as flushing toilets.

## Slide 22: Grey water harvesting (cont.)
Direct use systems – These systems can either syphon water directly from the bath or sink or you can fit a valve to the external waste pipe that allows you to direct the water to a water butt. The water can be used for watering plants but is not recommended for fruit or vegetables in case bacteria exist in the water.
Biological systems – These use gravity to filter water through a sand filter and soil box consisting of four layers of material (topsoil, fine building sand, coarse sand, pea shingle).
Mechanical systems – A greywater pump takes water away from greywater sources (washing machines, showers and utility sinks). The pump can feed the water to be treated into a storage tank (where normally it is treated chemically by adding chlorine) before it is sent to the cistern of a toilet or to the washing machine.
Notes: For more info see: https://www.thegreenage.co.uk/tech/greywater-recycling/

## Slide 23: Sustainable urban drainage systems (SUDS)
SUDS prevent water pollution and flooding in urban areas. SUDS also create green spaces and habitats for wildlife.
SUDS are systems designed to efficiently manage the drainage of surface water in the urban environment.

## Slide 24: Sustainable urban drainage systems

## Slide 25: Sustainable urban drainage systems
Potential benefits of SUDS include:
Reduced flooding
Reduced demand on traditional drainage systems
Enhanced water quality
Reduced pollution
Provision of habitats for wildlife

## Slide 26: Reducing water usage

## Slide 27
Any questions?