## Slide 1: PowerPoint 6: Waste management
5.8 Waste management

## Slide 2: Site waste management plan (SWMP)
A site waste management plan (SWMP) is an effective way to monitor and control the waste produced on a construction project. A client should work in conjunction with the principal contractor to produce a SWMP and may appoint them to do so on their behalf.
The SWMP should identify how materials will be managed and disposed of during the construction phase. It should also identify how reuse and recycling of materials will be implemented. It involves accurately estimating how much of each type of waste is likely to be produced and the percentage that can be reused or recycled.

## Slide 3: Site waste management plan
It is a joint responsibility of both the client and principal contractor to ensure that an SWMP is in place prior to construction works commencing. Although, since 2014, an SWMP is no longer a legal requirement, it is still best practice have one and it reflects positively on a company.
Hold suitable site inductions, information and training for all workers to ensure that the plan is implemented.
Update the plan as works progress to identify handling of waste.
Take all reasonable steps to prevent inappropriate and unauthorised disposal of waste.
Reflect on the effectiveness of the plan and set targets to provide information if differences occur.

## Slide 4: Waste management hierarchy
As a construction contractor, you are legally required to properly manage waste production and confirm that you are following the waste management hierarchy. This helps you to reduce, reuse, and recycle your waste before disposing of it.
This is crucial in order to help the UK to minimise its environmental impact and reduce the demand placed on landfill sites.

## Slide 5: Benefits of waste management
Compliance – Under waste management regulations, it is a legal requirement to control waste and follow the waste management hierarchy. This applies to those who produce, import or export, carry or transport, keep or store, treat, or dispose of waste.
Health and safety – Efficient waste management and segregation will help to reduce accidents. This will also prevent trip hazards associated with inappropriate storage of materials and products.
Reduced costs – Costs can be reduced by reusing materials and by not wasting materials and then paying for them to be removed.

## Slide 6: Benefits of waste management
Corporate social responsibility – Effectively managing waste to monitor and control how much you produce will help to protect our environment.
Improved reputation – Having a reputation for good waste management can have a positive impact on a company's reputation within the industry and with clients, which may lead to more work.
Promoting a circular economy – A circular economy designs out waste and pollution (uses less in the first place), keeps products and material in use (through recycling) and aims to regenerate natural systems (protecting the environment). Managing waste with care can contribute to these goals.

## Slide 7: Common types of construction waste
Concrete, bricks, tiles, cement
Wood, glass, plastic
Soil and stones
Paints and varnishes
Adhesives and sealants
Certain forms of waste must be kept separate from the general waste streams for various safety reasons. As a waste producer, it is your responsibility to prevent this waste from entering the general waste stream by using specialist waste disposal services.
Specialist waste management companies can be contracted to dispose of waste safely (Special Waste Regulations 1996). Waste carriers who transport waste and dealers or brokers who sell waste for disposal must be registered with the government and hold a waste carrier’s licence.

## Slide 8: Recycling

## Slide 9: Waste classification and transfer notes
For each load of non-hazardous waste, you must have a waste transfer note. The purpose of a waste transfer note is to outline information about the waste and how it will be disposed of.
Before you can send off waste for recycling or disposal, you must create a classification description for it. This helps you to decide how to handle the waste and provide the necessary paperwork for waste contractors.

## Slide 10: Skips
Identify the skip location on the site layout plan.
Do not overload a skip or the carrier may refuse to remove or unload it.
If it is on a highway, a skip should be lit at night and be guarded by a row of cones.
Skips must not cover drains or manholes.

## Slide 11: Segregating waste
Loads should be segregated to dispose of them correctly. This may mean have designated skips for specific materials and products. Skips may also be colour coded. This is becoming increasingly popular in industry. Categories of waste might be:
Brick, rubble, cement and plasterboard
Wood, cardboard, paper, carpet
Empty paint tins, adhesive tins or drums
Scrap metal, pipes, wire
Various chemicals, oil, grease
Asbestos
PVC window mouldings, gutters, and downpipes

## Slide 12: Waste classification and codes
Material | Waste status | Waste code
Concrete | Non-hazardous | 17-01-01
Bricks | Non-hazardous | 17-01-02
Tiles and ceramics | Non-hazardous | 17-01-03
Concrete, bricks, tiles and ceramics (alone or in mixtures) containing hazardous substances | Hazardous | 17-01-06
Concrete, bricks, tiles and ceramics in mixtures containing no hazardous substances | Non-hazardous | 17-01-07
Waste is given a classification code according to its content. Here are some examples of codes for common materials. These codes do not include asbestos (refer to asbestos and insulation codes).

## Slide 13
Any questions?