## Slide 1: 6.2 Standard units of measurement and measurement techniques PowerPoint 3: Site measurement
6. Construction measurement principles

## Slide 2: Measurement techniques In pairs, discuss the types of measurements that may need to be taken during construction projects and the tools used.

## Slide 3: Measuring tools past and present
Accurate measuring tools are becoming increasingly advanced, each and every year, although traditional tools are still as valid today as they were many years ago.
Equipment can vary from cutting edge digital equipment to water levels and plumb bobs that work very simply, using gravity.

## Slide 4: Tools for measuring on site
A laser distance measure makes the measurement task faster and easier. This tool sends out a focused pulse of light to a target and upon detecting the reflection, calculates the distance to this target with an accuracy of around +/- 1.5mm in a range of 50m.
Theodolites, in their modern form, consist of a telescope mounted to swivel both horizontally and vertically. Levelling is accomplished with the aid of a spirit level. Mounted on a tripod with adjustable legs, the theodolite is used in the field to obtain precise angular measurements.

## Slide 5: Measuring tools
A zip level is an electronic device that allows measurement of elevation, saving time on making measurements and calculations.
Zip Level – YouTube
A measuring wheel is ideally suited to estimating projects or relatively low-accuracy surveys. This is reflected in their units of measurement: generally using metres and centimetres. Measuring wheels are frequently used for estimating, marking out or verifying measurements taken with more precise measurement equipment.

## Slide 6: Measuring tools
Calipers and micrometers are used by engineers to accurately measure the distance between two sides of something. They are simple measuring tools that are very important when you need accurate data about an object. These tools are very common and have been in use for many years. Newer variants have digital displays to aid accurate readings.

## Slide 7: Measuring tools
Laser levels and measures are similar to the levels used by surveyors. Often ‘self levelling’, these tools are used by construction workers/tradespeople to give accurate horizontal and vertical lines to aid accurate installation of materials and equipment, and are generally more accurate than spirit levels.

## Slide 8: Measuring tools
A spirit level is used to indicate whether a surface is level on the horizontal or vertical planes. The most important feature on any spirit level is the glass or plastic vial. This vial contains a coloured liquid that has a bubble of air that moves along the vial. The vials feature two graduation marks that are spaced to allow positioning of the bubble between these two graduations, which then indicates horizontal or vertical level.

## Slide 9: Measuring tools
Using the principle that water will always find its own level, water levels are very accurate instruments, used widely throughout the construction and building industries.
They are designed for single-handed use when simultaneously measuring equal heights at two distant points.
A water level is the ideal tool for accurate unsighted room-to-room measurement or distant levelling, when using a spirit level would be ineffective.

## Slide 10: Measuring tools
Used to measure and draw straight lines, a rule is one of the most basic measurement devices. Available in assorted lengths, a tape measure is a portable tool that can measure to an accuracy of around 1mm if used correctly.

## Slide 11: Planning tools
A scale rule is a planning tool used by architects, engineers and designers to draw their designs at an appropriate scale that fits on a piece of paper. Typically the rule has the following scales: 1:1, 1:100, 1:20, 1:200, 1:5, 1:500, 1:1250, 1:2500.
When taking measurements, select the appropriate scale and read the measurement directly from the rule.

## Slide 12
Any questions?