## Slide 1: 6.3 Measurement standards, guidance and practice PowerPoint 5: Scales
PowerPoint presentation
6. Construction measurement principles

## Slide 2: Scales

## Slide 3: Why do we use scale?
Scale drawings are used in BSE and construction as a means of passing on and sharing complex information. Scale is generally used to show dimensions and positions.
Scale drawings remove the need for written dimensions. Calculations are used to scale up, or down, from pictures.
A scale drawing is a graphical representation of the real world, made to fit onto a piece of paper. Without scale, drawings would need to be the same size as the actual site or item described.

## Slide 4: What scale should you use?
1:1, 1:20, 1:50 or 1:100 …??
The scale that we decide to use depends on the task/site and the size of the area, component or item that we are representing.
Generally, in construction, the larger the area being pictured, the larger the scale is that we use.

## Slide 5: Typical scales
The following are typical scales used in construction.
1:1 – shows the item actual size. Usually used in engineering or for components, rather than construction.
1:2 – the drawing is half the size of the item/component represented.
1:5 – typically used for a component/detail drawing.
1:10 – used where detail is required to show the actual layout of components in a particular area.

## Slide 6: Typical scales
1:20 – used mainly for individual room layouts to show, for example, the electrical layout for a kitchen or workshop.
1:50 – used for floor plans, elevations and sectional drawings.
1:100 – similar to the 1:50 scale but used for larger areas.

## Slide 7: Typical Scales
1:500 – location drawings.
1:1250, 1:2500 – both are often requested by planners to show a location relevant to other property. The Land Registry will use these scales for urban and rural areas.

## Slide 8: Comparisons
A tattoo is drawn at a scale of 1:1
as it will be transferred directly to the skin
This cross-section of a window is drawn at a scale of 1:2

## Slide 9: Comparisons
Lathe tailstock drawing at a scale of 1:5
This wall cross section is at a scale of 1:10

## Slide 10: Comparisons
A floor plan is usually drawn at a scale of 1:50

## Slide 11: Comparisons
A road plan is shown at a scale of 1:500

## Slide 12: Comparisons
Detail from a Land Registry plan at a scale of 1:1250
Detail from a Land Registry plan at a scale of 1:2500

## Slide 13: Working out scale
Scale can be used to obtain measurements calculated up or down.
Depending on the scale, the calculation is proportionately bigger or smaller.
As an example, a scale of 1:20 means that you either multiply your measurement (up) from the drawing by the second number, in this case 20, to obtain the full-size measurement or divide (down) to make a scale drawing.

## Slide 14
÷ 20

## Slide 15
x 20

## Slide 16: Paper sizes
x 20
When scales are used, it is important to ensure drawings are produced on the correct size paper.
If the wrong size is used, measurements will not be as the designer intended and the final size will be incorrect.

## Slide 17: Scale calculations
Depending on the scale in use, scale up calculations always involve the second number of the scale ratio 1:10, 1:50, 1:1250 etc.
This is the multiplier used to carry out the calculation.
Measurements taken in the real world are divided by the scale ratio and measurements taken from drawings are multiplied.

## Slide 18
Any questions?