## Slide 1: PowerPoint 5: BIM, CDE and client specifications
8. Information and data principles
8.2 Sources of information

## Slide 2: Building information modelling (BIM)
      As you learned in Presentation 1, BIM is an intelligent 3D model-based process that gives insight and tools to more efficiently plan, design, construct and manage buildings and infrastructure projects. Different projects use different ‘levels of maturity’. Each level has its own criteria.
Level 0 BIM: no collaboration, using 2D CAD working with drawings.
Level 1 BIM: 2D CAD for drafting production information.
Level 2 BIM: all parties use 3D CAD models and share information through a common file format.
Level 3D BIM: all parties use one shared 3D model. This ‘open BIM’ approach exists in a central environment, making it easily accessible and editable by everyone.

## Slide 3: Why use BIM?
In April 2016, it was made a mandatory requirement for all publicly tendered projects in the UK to operate a level 2 BIM minimum.
For more information see:
https://www.theb1m.com/video/does-bim-take-more-time

## Slide 4: Planning and design stages (pre-construction)
    Planning: capture real-world data on environments
    Small portable imaging scanners and devices (or drones) give access to difficult locations and capture aerial imagery and generate 3D data.
    Mobile mapping includes mounting 3D laser scanners on people and vehicles.
    Static reality captures solutions.
    Terrestrial scanning allows long-range data capture.
        Design: use the 3D captured data to inform design
        Use augmented reality headsets onsite to visualise proposals.
        View overlays of proposals on 3D CAD models in common data environments (CDEs).

## Slide 5: Construction and post-completion
      The BIM specification and logistic data is shared with trades and contractors using centralised product data that is attached to the graphics, and for operation and maintenance of finished assets. Data is taken from the building in formation model and used to produce an asset information model (AIM).

## Slide 6: Asset information model (AIM)
      AIM can provide graphical and non-graphical data and information as well as metadata and documents describing procedures for the operational phase of the built asset.
      It may have been created from the existing project information model (PIM) or from new information.
      It may link to information regarding ownership, surveys or rights and restrictions.
      It should include operation and performance information.
      It may describe the original design intent of the asset.
      It may include 3D models.
      AIM is managed within the common data environment (CDE).

## Slide 7: Common data environment (CDE)
  This is the single source used to collect and manage information, documentation, the graphical model and non-graphical data gathered by the whole project team.
  CDE is a collaborative environment where all project team members can communicate. This helps to avoid mistakes and duplication.
  Within a project timeline, it is key to have regular exchange of data at strategic points using a CDE.
  For more information see: https://www.theb1m.com/video/what-is-a-common-data-environment
Notes: See PAS 1192-2 (British Standards Institute) for an illustration of the common data environment.: PAS 1192-2: PAS 1192-2 Delivery Phase of Construction Project - Operam

## Slide 8: Client specification checklist
It is important to understand the client specifications, have access to them and interpret and understand the information. Ask whether:
The client is to be the building user – if not, is the building user known?
The client wishes to operate on a total facilities management basis. If so, what are the responsibilities of each design discipline within the overall strategy?
The client has a maintenance policy?
The client will employ a maintenance engineer/premises manager/facilities manager?
The maintenance engineer/workforce will be in-house or engaged under contract?
The client has a maintenance budget in mind?

## Slide 9: Client specification checklist
Also consider:
Whether the engineering services will be operated: (a) continuously; (b) intermittently for a five-day week multi-shift operation; (c) intermittently for a five-day week single-shift operation; (d) using other operational patterns.
What the feasible/preferred timing will be for routine servicing or monitoring.
What will be the most demanding response time for emergency servicing in the event of breakdown? To what parts of the building or services installation would this apply?
Whether the total contract maintenance is to be applied to any plant items or parts of the building engineering services installations (ie where a contractor takes responsibility for the operation, maintenance and programmed replacement of plant or systems for a projected period of time)?

## Slide 10: Client specification checklist
It is also important to establish whether the client has any preconceived views about the economic life of plant and equipment. Is there an investment programme for eventual plant replacement?
Finally, ascertain:
any preferred (or not preferred) manufacturers or suppliers
if an asset register will be in place for plant and equipment items
whether there are any in-house policies or requirements in relation to health and safety; carbon emissions, energy use and efficiency; use of refrigerants; water hygiene; and any other aspects.

## Slide 11
Any questions?