## Slide 1
PowerPoint presentation
1.1 Key principles and methodologies in engineering and manufacturing design
PowerPoint 1: Manufacturing processes
1. Working within the engineering and manufacturing sectors

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain what constitutes a manufacturing process
describe the key types of manufacturing process.

## Slide 3: What is a manufacturing process?
The fundamental goal of a manufacturing process is to produce a product that has a useful form. The manufacturing process is an important step in the production process.
There are three stages in the manufacturing process:
to change the physical properties of the raw material
to change the shape and size of the workpiece
to achieve the required dimensional accuracy (tolerances) and surface finish.
An engineer must have a good understanding of the range of manufacturing processes, and the advantages and limitations of each.

## Slide 4: Types of manufacturing process
Forming A mechanical process used in manufacturing industries.
Shaping Used to change the size and shape of a workpiece.
Finishing Alters the surface of a manufactured part.
Casting Molten material (eg metal) is poured into a mould that contains a hollow cavity of the exact required shape.

## Slide 5: Types of manufacturing process
Additive Creating an object by building it one layer at a time.
Joining Fusing or joining two or more components to create a different object.
Wasting Material is either cut away or drilled out/removed.

## Slide 6: Forming
Bulk forming | Sheet metal forming | Powder metal forming
Rolling process | Bending | Powder forging
Extrusion process | Deep drawing | Powder injection
Forging process | Shearing | Powder extrusion moulding
Wire drawing |  | 
Squeezing |  | 
The forming process is a large part of the manufacturing process where a raw material is converted into a product. In this process, stresses like tension, compression and shear are applied. Forming processes can be broadly categorised into three types.

## Slide 7: Forming examples and applications
Sheet metal forming and copper wire drawing on large rollers.

## Slide 8: Shaping
Materials must be processed into a wide variety of shapes in order to make component parts of every type.
The shapes required vary enormously, both in size and complexity, ranging from micro-electronic components to large castings and forgings of several hundred tons.
The properties of the material in the finished component are also influenced to a considerable extent by the type of shaping process employed.

## Slide 9: Shaping processes
The range of shaping processes can be broadly classified into four categories:
Casting: the pouring of liquid into prepared moulds.
Manipulative processes: involving plastic deformation of the material.
Powder techniques: a shape is produced by compacting a powder.
Cutting and grinding: cutting to shape and size and grinding surfaces down to a precise finish.

## Slide 10: Shaping examples and applications
Compacting powder being used to produce small components.
A metal component being pressed into shape.

## Slide 11: Finishing
Finishing processes alter the surface of manufactured parts in order to achieve a particular characteristic.
Commonly desired characteristics include:
In some cases, these techniques may be applied to restore original dimensions or to salvage/repair a part. There are two main categories of finishing process.
improved aesthetics
adhesion
solderability
chemical, corrosion, tarnish or wear-resistance
hardness
electrical conductivity
flaw removal
surface friction control.

## Slide 12: Two categories of finishing
Removing and reshaping | Adding and altering
Abrasive and sand blasting | Anodising
Laser ablation | Dyeing
Engraving | Electroplating
Polishing | Electroless plating
Superfinishing | Plating
 | Powder coating
 | Spraying

## Slide 13: Finishing examples and applications
A laser is being used to engrave a design into wood.
Automated powder coating in a manufacturing process.

## Slide 14: Casting
The casting process involves the use of molten liquid, which is poured into a mould that takes the form of the finished part.
The liquid then cools, with heat generally being extracted via the mould, until it solidifies into the desired shape.
Although this describes a relatively simple process, casting is generally quite complex and highly skilled, in particular in metal casting, due to the complex metallurgy involved.

## Slide 15: Categories of casting
Casting processes can be broken down into two broad categories.
Expendable mould processes: the moulds are destroyed in order to remove the casting (eg, sand moulds, pictured top).
Permanent mould processes: the mould is reused and must therefore be designed to allow the easy removal of the casting (eg, metal moulds, pictured bottom).

## Slide 16: Casting patterns
Cast objects are highly dependent on pattern.
A pattern is a replica of the object to be cast, made from wood, metal, plastic or another material, which is used to prepare the cavity into which molten material will be poured during the casting process.
Types of pattern include single piece, loose piece, match plate, split, skeleton, multi-piece, sweep and follow board.

## Slide 17: Additive manufacturing
Additive manufacturing is a form of industrial 3D printing. It uses a computer-controlled process to generate 3D objects by adding materials layer by layer.
Multiple materials can be used during this process, which makes it easy to create new products with minimal waste and lower material costs.

## Slide 18: Types of additive manufacturing
1. Powder bed fusion: uses either a laser or electron beam to melt and fuse powder together to form products.
2. Vat photopolymerisation: uses liquid photopolymer resin applied layer by layer and hardened using UV light to create the final part or object.
3. Sheet lamination: binds sheets of material to form a part.
4. Directed energy deposition (DED): powder or metal wire is used with an energy source to add material or fuse a material onto an existing part or to create a new one.

## Slide 19
Types of additive manufacturing
5. Binder jetting: uses an inkjet print head to print a binder onto powder which binds the metal particles together into a ‘green state’. The parts are removed from the powder bed for de-binding and sintering (in an oven) to make them dense and hard. Sintering is the process of compacting and forming material by heat or pressure. Parts typically shrink by 20–25% during sintering.
6. Material jetting: new materials are available that have metal filler inside plastic rods that are extruded. The parts then go through the de-binding and sintering steps.
7. Material extrusion: a filament or thermoplastic material is used to create parts. The filament (or thermoplastic) is heated and then continuously layered through a nozzle to create the final component.

## Slide 20: Additive manufacturing examples and applications
DED process used to create parts.
Filament loaded into a device for material extrusion process.

## Slide 21: Joining
Joining comprises many processes used to assemble individual parts into a larger, more complex component or assembly. The individual parts of a component meet at the joints. The joints transmit or distribute forces generated during use from one part to the other parts of the assembly. A joint can be either permanent or temporary. The five joint types that are predominately used in joining are: butt, tee, corner, lap and edge.

## Slide 22: Wasting
The process of cutting away material with tools and equipment – wasting, or wastage, produces waste (as the name suggests), but good design can minimise the amount produced. Cutting processes are achieved using the following tools and methods.
Guillotining: uses a sharp blade to chop through sheet material.
Drilling: holes can be drilled through a material – a common manufacturing process.
Laser cutting: suitable materials include wood and plastic – intricate shapes can be created.
Computer numerical controlled (CNC) routing: for cutting, engraving and drilling. The cutting blade spins and moves along a pre-programmed route quickly and accurately.

## Slide 23: Wasting examples and applications
Drilling during car component manufacture using a CNC machine.
Guillotine used to cut sheet metal to size.

## Slide 24
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.