## Slide 1: 1.1 Key principles and methodologies in engineering and manufacturing design
PowerPoint presentation
1. Working within the engineering and manufacturing sectors
PowerPoint 3: Approaches to design

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the different approaches to design – linear, iterative, inclusive, user-centred, ergonomic, design for manufacturing (DFM), design for assembly (DFA)
outline sustainable design principles, including the six Rs
understand the principles behind different research and testing methodologies in design
understand different methods used to communicate with technical and non-technical audiences.

## Slide 3: The design process
To design anything – a tiny motoring component, a software package, or a huge skyscraper – requires the design team to work through several steps in a design process. The first of these is to discover and define an idea, which can then lead to a stage where the design is prototyped and tested out.

## Slide 4: Linear design
These design steps may continue from the design concept to delivery – from discovering and defining user needs, to designing and developing the solution, to delivering the end product.
A design process which follows a path such as this is called a linear design process.
Discover: understand the problem/need
Define: zero in on the need
Design: create a product/process to meet the need
Develop: build the product or process
Deliver: get the product or process into use

## Slide 5: Iterative design
The iterative design process is an approach that designers use to continually improve and refine a design or product.
A prototype is created and tested, the design is then developed, tested and evaluated, and so on. This cycle can be repeated until a satisfactory solution is reached that meets the initial design criteria and user needs.
The process can be used to continuously improve a concept, design, software system or product.

## Slide 6: Iterative design process

## Slide 7: User-centered design (UCD)
User-centered design (UCD) is a form of iterative design. Designers focus on users and their needs in each phase of the design process.
In UCD, design teams involve users throughout the design process via a variety of research and design techniques, to create highly usable and accessible products.
Notes: Image used with permission of Atiyeh Vaezipour (https://www.researchgate.net/figure/The-User-Centred-Design-Approach-adapted-from-ISO-2010_fig3_316680273)

## Slide 8: Inclusive design
Inclusive design is a process in which a product, service or environment is designed to be usable by as many people as possible. Inclusive design is a methodology that considers many aspects of human diversity that could affect a person’s ability to use a product, service or environment. For example, ability, language, culture, gender, accessibility and age.

## Slide 9: Inclusive design
Inclusive design (also called universal design) seeks to create products and places that are usable by everyone, regardless of age, ability and circumstance.
It is based on the simple principle that designing for the widest range of people creates better designs and benefits more people.
The picture shows a museum in Helsinki where inclusive design principles connect different rooms via shallow ramps.

## Slide 10: Ergonomic design
As you have already learned, anthropometric data is collected from the study of the human body and its movement.
Anthropometric data can be used to improve designs so that they better suit the way our bodies work, and are therefore easier and safer to use.
Design which factors in anthropometric data is called ergonomic design.

## Slide 11: Factors in ergonomic design
The following human factors are considered in ergonomic design.
Posture: the product should encourage good posture (eg, desk chairs should be adjustable to different heights).
Clearance: adequate headroom, elbow-room and leg-room in car interiors; door heights in buildings; manhole diameters; airline seats etc all require adequate clearance and should be designed to accommodate users with larger than average dimensions.
Strength: refers to the required application of force when operating controls and performing other physical tasks. Strength is described as a ‘one way’ constraint in that it is limited to how much force a person from the lower half of the strength spectrum can impart. A weak user must be able to use the design without considerable effort.

## Slide 12: Design for manufacturing (DFM)
Design for manufacturing (DFM) is the general engineering practice of designing products that are easy to manufacture.
DFM is the process of designing or engineering a product to ‘fit’ the most efficient manufacturing process.
It allows potential problems to be fixed in the design phase, which is the least expensive point at which to address them.
It can also reduce manufacturing costs as the design has been optimised, in advance, to reduce waste.
Factors that may affect manufacturability include the form and type of raw material, dimensional tolerances and secondary processing, such as finishing.

## Slide 13: DFM principles
Process: the manufacturing process must produce a quality item at the lowest cost and in an efficient way. DFM should consider the number of times that a part must be set up – whether in one machine or multiple machines.
Design: drawings should conform to accepted manufacturing principles. The design should include notations for all the specifications that are relevant to the manufacturing process.
Materials: the materials must be easy to source, and straightforward to use in the manufacturing process with minimal waste.
Environment: the product needs to be designed so that the materials can perform under its likely conditions of use.
Compliance: every product has to pass a certain amount of testing, such as general safety, quality or industry standards.

## Slide 14: Design for assembly (DFA)
Design for assembly (DFA) is a process which focuses on ease of assembly. The key principles of DFA are:
fewer parts take less time to assemble, thereby reducing assembly costs
fewer parts in an assembly (component elimination) has the added benefit of reducing the total cost of parts, with major cost benefits
if the parts are provided with features which make them easier to grasp, move, orient and insert them, this will also reduce assembly time and costs.

## Slide 15: Component elimination
Notes: Image source: https://www.eastekinternational.com/wp-content/uploads/2020/07/DFM.jpg (image)

## Slide 16: Sustainable design
Sustainable design (sometimes referred to as eco design) is about designing physical objects, the built environment and services to comply with the principles of ecological sustainability (protecting the environment).

## Slide 17: Sustainable design principles
The key objectives of sustainable design are to:
reduce the consumption of non-renewable resources and switch to renewable materials with low environmental impact
reduce carbon (fossil fuels) spent manufacturing a product
minimise waste in the production process
create healthy, productive environments
consider the entire product life cycle, from the mining of raw materials to disposal.

## Slide 18: The six Rs
The six Rs (often represented in various orders but all equally important) can help designers focus on sustainable goals.
Reduce: can the amount of material, energy or water needed to manufacture the product be reduced?
Refuse: can you refuse to design a single-use plastic product?
Rethink: can you rethink your design to make it easier to recycle?
Repair: if your product breaks, are there spare parts to repair it?
Reuse: can the product or its parts be reused in a new way?
Recycle: is the product easy to recycle?

## Slide 19: The six Rs

## Slide 20: Research methodologies in design
A research methodology is an outline of how a given piece of research is carried out. It defines the techniques or procedures that are used to identify and analyse information regarding a specific research topic. The research methodology, therefore, has to do with how a researcher designs their study in a way that allows them to obtain valid and reliable results and meet their research objectives. There are three key types of research methodology.
Qualitative methodology: involves research that is conducted using words and textual data.
Quantitative methodology: relies on the measurement and testing of numerical data.
Mixed-methods methodology: a methodology using both methods.

## Slide 21: Testing methodologies in design
Testing methodologies are the strategies and approaches used to test a particular product to ensure it is fit for purpose.
It is important to ensure the product works in accordance with its specification, has no undesirable side effects when used in ways outside of its design parameters and, in the worst case, that it will fail safely (eg a nuclear reactor will shut down on failure).
Testing is of particular importance in software design and implementation, where it encompasses the integration of a system with other systems, along with performance, security, usability and compatibility testing.
The results of product tests are fed back into the design process, where undesirable features can be removed or redesigned.

## Slide 22: Testing methods
In engineering the following types of testing can ensure a product will not fail.
Temperature and pressure testing: how the design withstands high or low temperatures.
Fatigue testing: how a product performs under fluctuating loads.
Fastener stress testing: how bolts/connectors perform under stress.
Testing is a crucial design stage which allows designers to remove any design flaws that could prevent the design successfully meeting its requirements. Testing contributes towards ensuring a design is suitable, effective and safe.

## Slide 23: Know your audience
It is important to know your audience if you are to successfully communicate (often complex) ideas, concepts and design requirements. Broadly speaking, audiences (be they single people or groups) are either technical or non-technical.
A technical audience with existing knowledge of the subject will appreciate your using technical language and engineering drawings, schematics and diagrams to illustrate your points.
A non-technical audience with little or no specialist knowledge will appreciate simple analogies to communicate your technical concepts, along with real-life examples and minimum use of technical language. Jargon should always be avoided.

## Slide 24: Your turn
Consider the design and manufacture of a plastic toothbrush versus a bamboo toothbrush.
Why is a bamboo toothbrush a more sustainable design?

## Slide 25
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.