## Slide 1: 1.2 The role of maintenance, repair and installation in engineering PowerPoint 4: Maintenance activities
PowerPoint presentation
1. Working within the engineering and manufacturing sectors

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the role and purpose of maintenance, repair and installation
outline the advantages and disadvantages of different approaches to maintenance.

## Slide 3: What is maintenance?
Maintenance can be considered as the ‘healthcare’ of machines and equipment. It is the process by which machines and equipment receive the appropriate care to keep them in good working order.
The importance of an effective maintenance programme cannot be overstated. It is required to effectively reduce waste and run an efficient, continuous manufacturing operation, business or service (such as a railway).
The cost of regular maintenance is very small when compared to the cost of a major breakdown which my result in a process coming to a standstill.

## Slide 4: The purpose of maintenance
The main purpose of regular maintenance is to ensure that all equipment is operating at 100% efficiency at all times.
For example, in a manufacturing context, many machines are required to be operating for production to run smoothly. Through short regular inspections, cleaning, lubricating and making adjustments, minor problems can be detected and corrected before they become major problems that can shut down a production line.
A good maintenance programme requires company-wide participation and support from everyone, ranging from the top executive to shop floor personnel.

## Slide 5: Planned maintenance
Planned maintenance refers to any maintenance activity that is planned, documented and scheduled. The aim of planned maintenance is to reduce downtime by having all the necessary resources to hand, such as labour and parts, and a strategy to use these resources.
There are two main types of planned maintenance.
Planned preventive maintenance (PM): scheduled maintenance aimed at repairing assets before they fail. An example would be conducting maintenance on a forklift after every 150 hours of operation.
Planned unscheduled maintenance: having a strategy in place to repair or replace an asset as quickly as possible when it fails. An example would be planning to have a sufficient number of easily accessible power drills on hand so that replacing a broken one is quick and easy.

## Slide 6: Advantages and disadvantages of planned maintenance
Advantages | Disadvantages
Reduces maintenance costs | Potential for over-maintenance
Improves overall equipment performance | Upfront costs – keeping equipment well maintained requires investment
Decreases downtime | Labour intensive
Improves workplace culture | 
Extends asset life | 
Improves overall equipment performance | 
Increases workplace safety | 

## Slide 7: Reactive maintenance
Reactive maintenance addresses problems when they arise. Maintenance activities are triggered by equipment malfunctions and failures. Broken-down machines are either repaired or replaced.
For example, rather than changing a light bulb before it fails, you wait for it to fail, and then replace it. The run-to-failure approach is best suited for non-critical and low-cost pieces of equipment that don’t have a major impact on production or safety.

## Slide 8: Advantages and disadvantages of reactive maintenance
Advantages | Disadvantages
Fewer staff members needed | Difficult to control budgets
No planning time necessary | Shorter life expectancies of assets
Lower upfront costs | Safety issues
 | Time consuming
 | Sporadic equipment downtime
 | Inefficient use of resources
 | Collateral damage
 | Indirect costs
 | Repeat issues
 | Higher energy costs

## Slide 9: PM
PM (preventive maintenance) is the regular and routine maintenance of equipment and assets in order to keep them running and prevent any costly unplanned downtime from unexpected equipment failure.
A successful maintenance strategy requires planning and scheduling maintenance of equipment before a problem occurs. A good preventive maintenance plan also involves keeping records of past inspections and the servicing of equipment.
Because of the complexity of maintaining a preventive maintenance schedule for a large amount of equipment, many companies use preventive maintenance software to organise the required tasks.

## Slide 10: Advantages and disadvantages of PM
Advantages | Disadvantages
Less equipment downtime | Upfront costs
Longer asset life | Labour intensive
Fewer interruptions to critical operations | Potential for over-maintenance
Increases workplace safety | 
Improves efficiency (assets in good condition perform better) | 

## Slide 11: Your turn
Summarise why it is preferable for companies to carry out preventive maintenance rather than reactive maintenance.
Discuss with your peers and report back to the group.

## Slide 12: Condition-based monitoring (CBM)
Condition-based monitoring (CBM) is the process of monitoring the parameters of conditions in machinery such as vibration, temperature or noise during operation, in order to identify a significant change. Changes in the data collected can give early warning of problems (eg degrading components), which may indicate that the machine is developing a fault.
The use of CBM allows maintenance to be scheduled, or other actions to be taken to prevent damage and avoid its consequences.
CBM has a unique benefit in that conditions that would shorten normal lifespan can be addressed before they develop into a major failure.
CBM techniques are normally used on rotating equipment, auxiliary systems and other machinery (compressors, pumps, electric motors, internal combustion engines, presses).

## Slide 13: Advantages and disadvantages of CBM
Advantages
Improves worker safety
Optimises maintenance intervals
Minimises requirement for emergency spare parts
Minimises overtime costs by scheduling maintenance activities
Improves equipment reliability
Reduces the cost of asset failures
Minimises unscheduled downtime due to catastrophic failure
Disadvantages
Unpredictable maintenance periods
Cost to train staff – a knowledgeable professional is needed to analyse the data and perform the work
Fatigue or general wear failures are not easily detected with CBM measurements
Short-term investment is required
Equipment for CBM is expensive

## Slide 14: Maintenance, repair and operations (MRO)
Maintenance, repair and operations/overhaul (MRO) is concerned with the equipment, tools and activities associated with the daily operations of a business.
It does not include materials, products and services that are directly used in production, but rather the ‘glue that holds everything together’. MRO can be:
routine, planned maintenance activities (preventive MRO)
predictive, when data indicates machinery is deteriorating and needs maintenance
corrective, after an incident occurs.

## Slide 15: Examples of MRO
MRO applies to all of the following.
Heating, ventilation and air conditioning (HVAC) maintenance
Facility lighting
Cleaning services
Jacks
Forklifts
Personal protective equipment (PPE)
CNC (computer numerical control) machinery
Powered and manual hand tools
Furniture

## Slide 16: Operations monitoring
Operations monitoring involves observing the performance of a machine or equipment over time by collecting key system performance metrics at planned intervals. This provides critical data to refine a machine’s configuration and improve efficiency. Data can be collected through a machine monitoring system. Some of the types of data collected are shown below.
Machine status – on/off, run rate, speed
Downtime and utilisation – planned/ unplanned stops
Quality – right part first time (RPFT), scrap rate
Operator effectiveness – labour productivity and efficiency
Environmental data – humidity, vibration, temperature
Energy – electricity use over time

## Slide 17: Repair
Repair means responding to the breakdown of equipment and undertaking work to correct the problem in order to return the equipment to a working condition.
Simple repairs can be done by in-house or external maintenance and repair teams. If the equipment is repaired where it is used, it is important that the team is trained to work safely and that they don’t create hazards. More complex repairs may be carried out by specialised maintenance personnel who may come to you, or you may have to send the equipment to them for repairs.

## Slide 18: When repair is not possible
Some items of equipment will be found to be damaged beyond repair. For others, spare parts may no longer be available as the equipment has become outdated.
Such equipment must be taken out of service (decommissioned or retired) and be replaced if the service they provide is to continue.
Equipment that is being decommissioned should be disposed of safely and according to proper disposal procedures.

## Slide 19: Shutdown
Shutdown maintenance can only be performed while equipment is not in use.
Shutting down machinery can be costly, but sometimes, due to the nature of the defective part/machine, shutdown maintenance is the only viable option.
Technicians will do all they can to avoid a complete shutdown. In some industrial applications (power generation for example), a shutdown can mean enormous financial losses. Companies will take the option to shut down during holiday periods to minimise disruption.

## Slide 20: Servicing
Servicing should be included in a maintenance schedule, either biannually or annually.
In the same way as servicing your car, servicing machinery ensures it is operating as productively as possible.
Servicing is also about protecting those who use the machinery and others surrounding them, as it ensures machines are running safely (eg, there are no dangerous emissions or parts that could fail and cause injury).

## Slide 21: Installation and commissioning
Commissioning is the process of assuring that all systems and components of a building or industrial plant are designed, installed, tested, operated and maintained according to the operational requirements of the owner or final client.
A commissioning process may be applied not only to new projects but also to existing units and systems subject to expansion, renovation or revamping.
In practice, the commissioning process is the integrated application of a set of engineering techniques and procedures to check, inspect and test every operational component of the project, from individual functions (such as instruments and equipment) to complex amalgamations (such as modules, subsystems and systems).

## Slide 22: Decommissioning
Decommissioning is the term used for a process to remove something from active service.
It may be a precursor to putting facilities/equipment into storage, repurposing or demolition/disposal.
There are many factors and requirements to consider in this process, including documentation, environmental and health and safety compliance, maintenance, supporting contracts, and interfaces with other facilities and site utilities, not to mention cost.
Decommissioning an oil rig such as this is a long, complex and costly operation.

## Slide 23
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.