## Slide 1: 1.3 Approaches to manufacturing, processing and control PowerPoint 7: Scale and infrastructure
1. Working within the engineering and manufacturing sectors

## Slide 2: Objectives
By the end of this session, learners should be able to:
understand the concept of manufacturing scale (prototype, one-off, batch, mass and continuous production)
understand the meaning of infrastructure in manufacturing.

## Slide 3: Scales of production
Depending on the quantity of products to be manufactured, the methods used will change. There are four main scales of production, each suited to a range of different product applications.
One-off /prototype
Batch production
Mass production
Continuous production

## Slide 4: Prototype and one-off production
When only one product is made at a particular time it may be a prototype or a one-off, perhaps handmade, object.
Prototype: a prototype is a draft version of a product that allows the exploration of ideas. The intention behind a feature or the overall design concept can be shown to users before investing time and money in development.
One-off: one-offs can be very small or very large: bridges, ships, stadia, specialist jewellery, made-to-measure clothing, bespoke furniture. One-off production is sometimes referred to as job production.

## Slide 5: Prototype and one-off examples
Prototype
One-off

## Slide 6: Batch production
Batch production is a method whereby a group (batch) of identical products is produced simultaneously (rather than one at a time), before moving along to make another group of products. It is up to the manufacturer to decide how big the batch will be, and how often these batches will be made.
Each batch goes through the separate stages of the manufacturing process at the same time. This mean that another batch can’t begin a stage if the previous batch is still going through that part of the cycle.
Each batch can be different, as manufacturers can decide to change the specifications from one group of products to the next. Perhaps it is necessary to change the colour or size of that particular group (depending on the preferences specified in a particular order).

## Slide 7: Batch production examples
Baked goods
Clothing
Computer chips
Computer software
Die- or mould-making
Electrical goods
Flat-pack furniture​
Jet engine production​
Jig and fixture production​
Machine tool manufacturing​
Material coating​
Newspapers/magazines

## Slide 8: Mass production
Mass production creates standardised goods in large quantities. The term can also be used to describe continuous production or flow production, due to products usually being manufactured on sizeable conveyor systems.
Mass production ensures that the whole process of manufacturing remains at the lowest cost possible while turning out the highest volumes possible.
Mass-produced items are made on a large scale, usually in a factory or plant. Cars, computers and sports shoes are all mass-produced. Mass-produced items are standardised, ie almost identical.

## Slide 9: Mass production
Mass production allows products to be produced very quickly, using assembly line techniques.
Workers (or automated stations) work on an individual step, rather than a whole product from start to finish. The product travels along an assembly line where each process is carried out, resulting in a completed product at the end of the line.
Mass production is capital intensive (requires high investment in machinery) and uses a lot of energy. It relies of economies of scale to be profitable. It is not a flexible approach – changing product lines is expensive and difficult.
Companies reduce costs in mass production by setting up facilities to make the same standardised product lines for a prolonged period of time.

## Slide 10: Continuous production
Continuous production is a flow production method used to manufacture, produce or process materials without interruption.
In continuous production (continuous process or continuous flow process) the materials (eg dry bulk or fluids) being processed are continuously in motion, undergoing chemical reactions or subject to mechanical or heat treatment.
‘Continuous’ usually means operating 24 hours a day, seven days a week, with infrequent maintenance shutdowns (biannual or annual).

## Slide 11: Batch vs continuous production
The diagrams show how the two processes differ.

## Slide 12: Continuous production examples
Oil refineries
Food and beverage manufacturers
Paper manufacturers
Cement manufacturers
Electronics manufacturers
Glass manufacturers
Steel manufacturers
Chemical manufacturers

## Slide 13: Combining manufacturing methods
Let’s use vehicle production as an example.
Prototype – new vehicles and designs.
Batch – models.
Mass – types (hybrid, plug-in, full electric).
Continuous – the line continues to meet manufacturing targets by running 24/7.
Automated – production is both fully- (predominately) and semi-automated.
Quality control is semi-automated and the final inspections are signed off by a human.

## Slide 14: Production matrix
 | Low volume (unique product) | Low volume (multiple products) | Higher volume (standardised products) | Very high volume (commodity products)
Jumbled flow | Job shop |  |  | 
Disconnected line flow |  | Batch |  | 
Connected line flow |  |  | Assembly line | 
Continuous flow |  |  |  | Continuous

## Slide 15: Infrastructure
Infrastructure in manufacturing refers to:
advanced manufacturing systems
engineering tools for design and manufacturing
advanced manufacturing product and process layouts and equipment
manufacturing training and education
manufacturing deployment
business practices.

## Slide 16: Product and process layouts
In manufacturing, layout is an important consideration. The systematic organisation and group of facilities and services used to manufacture goods can have a big impact on the time, cost and efficiency of production.
A product layout is one in which equipment or work processes are arranged according to the progressive steps by which the product is made. The resources needed to produce the product are arranged in one line, as per the sequence of operations (eg an assembly line).
A process layout is when similar equipment or functions are grouped together (eg in a machine shop all the lathes are in one area). The resources having the same processes or functions are grouped together. A part being worked on travels from one area to the next.

## Slide 17: Production lines
A production line is a traditional method associated with manufacturing. The production line is arranged so that the product is moved sequentially along the line and stops at various work centres where an operation is performed.
Production line in food manufacturing.

## Slide 18: Cellular manufacturing
In cellular manufacturing, production workstations and equipment are arranged in a sequence (similar to a production line) that supports a smooth flow of materials and components through the production process, with minimal transport or delay. This lean method enables increased production speed and flexibility.
Cellular manufacturing involves the use of multiple ‘cells’ in an assembly line. Each cell is composed of one or multiple machines which accomplish a certain task.
The product moves from one cell to the next, each station completing part of the manufacturing process.
Often the cells are arranged in a U-shape because this allows the overseer to move less and watch over the entire process from one place.

## Slide 19: Cellular manufacturing set-up

## Slide 20: Automation
Automation is the technology by which a process or procedure is accomplished without human assistance. There are different levels of automation in manufacturing. Some items are made with the help of automation, and some manufacturing is now fully robotic.
Automation is implemented using a computer program of instructions combined with a control system that executes the instructions.
The basic elements of an automated system are:
power: operates the automated system
program of instructions: directs the process
control system: actuates the instructions.

## Slide 21: Manual production
Manual production is still sometimes the most efficient form of manufacturing. This may be because the task is too technologically difficult to be automated. An example of this is fitting airbags in the automotive industry (in the image an airbag is fitted by hand).
Customised products are often finished by hand as humans have the adaptability to add unique features.
Human labour can also be altered up and down quickly to adapt to surges in demand, or to manage short-term production.

## Slide 22: Fully automated production
Conveyor systems and robotics are required to make a system in manufacturing fully automated. These are programmed by humans and the final processes are completed by machinery controlled by robotics. Humans tend to be used to monitor these systems.

## Slide 23: Robotics
Robotic manufacturing helps with consistent, precise manufacturing and increases production.
Robots have long been used to support humans during production processes.

## Slide 24: Types of robots
Robot type | Features | Uses
Cartesian | Moves in straight lines on three-axis, flexible configurations. | CNC machines and 3D printing.
SCARA (selective compliance assembly robot arm) | Has rotary motion, excels in lateral movements. | Assembly, palletising and bio-med applications.
Articulated | Resembles a human arm mounted on a base with two to ten rotary joints. | Assembly, arc welding, material handling, machine tending, packaging.
Delta | Three arms connected to a base, mounted above the workspace. Quick, delicate and precise. | Food, pharmaceutical and electronics applications.
Collaborative | Also called “cobots”; intended to assist human workers. | Pick and place, quality inspection, machine testing.

## Slide 25: Computer-aided manufacturing (CAM)
Computer-aided manufacturing (CAM) is the use of software and computer-controlled machinery to automate a manufacturing process. Three components are needed for a CAM system to function:
software that tells a machine how to make a product by generating tool paths
post-processing converts tool paths into a language machines can understand
machines can turn raw materials into finished products.
Human labour and skill are still required to make CAM systems successful.

## Slide 26
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.