## Slide 1: PowerPoint 2: Engineering drawings (1)
PowerPoint presentation
3. Engineering representations
3.1 Drawings and information conveyed by drawings

## Slide 2: Objectives
PowerPoint presentation
By the end of this session and the next, learners should be able to describe the following types of engineering drawing and their use:
freehand sketch
orthographic and isometric
first (1st) and third (3rd) angle
section and cross-sectional
detail
assembly.

## Slide 3: Freehand sketches
A freehand sketch is drawn without measuring instruments, with a pencil and eraser only.
Freehand sketches are often used to present an idea quickly.
An engineering drawing can then be prepared once a concept is accepted.
Notes: Sketch of car used with permission of Arvind Ramkrishna (https://www.carbodydesign.com).

## Slide 4: Benefits of a freehand sketch
Can be produced anywhere.
Minimal equipment needed.
Quickly illustrates information.
Improves communication between technical and non-technical people.
Scale and ruler are not necessarily used in a freehand sketch, yet ratio and proportion of different parts of an object are considered.
After completing the drawing, a rough scale can be added.
Notes: Image source: https://www.tudelft.nl/en/3me/education/check-out-our-education/transformative-experiences-freehand-sketching.

## Slide 5: Orthographic projection
Orthographic projection describes the projection of a single view of a 3D object (such as a view of the front, top or side) onto a drawing surface.
Rarely will a single view of an engineering component show detail of every important feature.
A complete drawing will quite often appear with two, three or more individual drawings on the same sheet.
Each of these individual drawings depicts how the same component will look when viewed from a different angle.
These drawings give the craftsperson enough information to be able to repair, install or create the item.

## Slide 6: Elements of an orthographic projection

## Slide 7: Creating an orthographic projection

## Slide 8: First and third angle
First (1st) and third (3rd) angle are different schemes to show orthographic projection, denoted by the symbols shown here.
1st angle (left)
3rd angle (right) (shows views in different positions)

## Slide 9: First angle projection

## Slide 10: Third angle projection

## Slide 11: Orthographic projection: first angle
First angle – the model view is drawn opposite the face being viewed.
BS 8888 first angle projection symbol.

## Slide 12: Orthographic projection: third angle
Third angle – the model view is drawn adjacent to the face being viewed.
BS8888 third angle projection symbol

## Slide 13: Orthographic projection: glass box approach
Orthographic Projection - The Glass Box - 3rd Angle Projection - YouTube
One way to visualise orthographic projection is to imagine a glass box around an object on which the object’s outlines are traced.
(https://www.youtube.com/watch?v=94wTgI-xS2o)

## Slide 14: Isometric drawings
An isometric drawing or projection allows the designer to draw an object in three dimensions.
Isometric drawings are a 2D drawing showing a 3D view.
Width and depth perceptions are angled back at 30 degrees.
Isometric drawings are generally used to illustrate what an end product will look like. Although they are useful for conveying a good image of the completed article, they are of little use to the craftsperson who has to produce it, other than as a visual aid.

## Slide 15: Examples of isometric projections
Isometric projections usually accompany orthographic projections.
Can be used in assembly, exploded and installation diagrams.

## Slide 16: Examples of isometric projections

## Slide 17: Isometric vs orthographic
It is possible to pack a great deal of information into an isometric projection, but look at the object shown below, and imagine that it has a hole on the side facing away from you. This would not be visible using a single isometric projection but could be seen in an orthographic projection.

## Slide 18: Isometric vs orthographic
In order to get a more complete view of an object that includes detail of the kind that would allow the item to be made using only the drawings as a guide, an orthographic projection will be needed.

## Slide 19: Section views
Orthographic and isometric projections allow us to see the external features of an object, but it is often necessary to be able to see internal features as well.
This is accomplished by ‘slicing through’ to produce a sectional or section view.

## Slide 20: Section views
All the solid internal surfaces of the section view will be cross-hatched, as shown here.

## Slide 21: Cross-sectional views
A cross-sectional view portrays a cutaway portion of the object and is another way to show hidden components in a device. Imagine a plane that cuts vertically through the centre of the pillow block as shown. Then imagine removing the material from the front of this plane.
This is how the remaining rear section would look. Diagonal lines (cross-hatches) show regions where materials have been cut by the cutting plane.
Notes: Image sources: http://www.design-technology.info/IndProd/page7.htm.

## Slide 22: Detail views
When there is a great disparity between feature size, or views are overcrowded with dimensions, a detail view can be used to capture the feature(s) of interest and display them in a removed view of greater scale.

## Slide 23: Detail views

## Slide 24: Detail drawings
Detail drawings contain enough information for the manufacturer to produce the component, including:
  geometry
  material
  heat treatment requirements
  surface texture
  size tolerances
  geometric tolerances etc.

## Slide 25: Example of a detail drawing
Notes: Image source: https://sites.google.com/site/kuhlengineering2/home/unit-d---dimensioning-conventional-tolerancing/detail-drawings.

## Slide 26: Detail drawings
A detail drawing should include all the necessary information, including relevant codes and standards to enable procurement and manufacture.
Depending on the level of detail, a detail drawing can comprise one drawing on a sheet, or a number of separate drawings.
It is sometimes possible to combine detail drawings onto an assembly drawing.

## Slide 27: Assembly drawings
Assembly drawings are illustrations used to explain how multiple components fit together.
Assembly drawings are used in many contexts, such as showing how to assemble furniture, buildings or machinery.

## Slide 28: Features of an assembly drawing
Detailed dimensions are excluded. The overall dimensions of the assembled product are used.
Maximum and minimum tolerances are usually included.
Internal assemblies are displayed in sectional views.
Multiple drawings may be used in sequence to give the reader instruction on how a product is assembled in stages.
Leader lines with arrows indicate external parts, leader lines with circles indicate internal parts.
A parts list or table may be included, with all the parts numbered. Headings include item number, description, quantity, material, remarks etc.

## Slide 29: Your turn
Have you ever used an assembly drawing? What did you assemble? A kit? Flat-packed furniture?
How good was the drawing at achieving its intended purpose?

## Slide 30
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.