## Slide 1: PowerPoint 4: Key drawing features
PowerPoint presentation
3. Engineering representations
3.1 Drawings and information conveyed by drawings

## Slide 2
Objectives
By the end of this session, learners should be able to:
understand the significance of BS 8888 in relation to engineering drawings
understand the key features of engineering drawings
identify engineering drawing symbols.
PowerPoint presentation

## Slide 3
BS 8888
British Standard (BS) 8888 is a national standard for engineering drawings and geometrical tolerancing. BS 8888 covers all the requirements for the technical specification of products and their parts. The use of engineering drawing symbols is an important part of conveying this information.
All geometric tolerancing standards are also reflected in ISO 1101: 2017, ‘Geometrical product specifications’. Find out more here:
https://www.iso.org/standard/66777.html

## Slide 4: Title block
All engineering drawings should feature a title block. Here is an example.

## Slide 5: Title block information
The title block should include:
title: the title of the drawing
name: the person who produced the drawing
checked: a signature of approval for the drawing
version: many drawings are amended, so each revision must be recorded
date: when the drawing was produced or last amended
notes: in the example, the note relates to measurements
scale: the scale of the drawing
company name
projection: the projection used to create the drawing, shown as symbol(s).

## Slide 6: Line types on engineering drawings
Drawing line
Hidden line
Centre line and centre mark
Phantom line
Break line
Dimension line and leader
line

## Slide 7: Drawing lines: purposes and conventions
It is important that hidden features are represented, so that the reader of the drawing can clearly understand the object.
Centre lines are required to understand how the features defined in the 2D views translate into 3D.
Hidden lines and centre lines are used only on orthographic projection drawings, never on isometric drawings.
If two lines fall on top of each other, there are conventions for which lines to show. Otherwise, more important features (eg visible lines) would be overridden by less important features (eg hidden lines) and the resulting drawing would be interpreted inaccurately.

## Slide 8: Common symbols
Slope: the slope symbol is placed at the left end of the slope specification.
Straightness: a straight line is used to indicate a straightness requirement.
Flatness: the flatness symbol appears as an oblique view of a square surface.

## Slide 9: Common symbols
Circularity: indicated by a circle.
Cylindricity: a circle with two parallel lines drawn tangent to the circle.
Parallelism: indicated by two parallel straight lines.

## Slide 10: Common symbols
Perpendicularity: indicated by two lines as shown.
Angularity: indicated by two lines forming a 30 degree angle.
Concentricity: indicated by two concentric circles.

## Slide 11: Common symbols
Level of surface finish.
Ground finish (using grinding tool).
Removal of material NOT permitted.
Tapped hole (a tolerance is usually allowed).
Reamed hole (very exacting, with tolerances).

## Slide 12: Datum symbols
A datum line is a standard position or level from which measurements are taken.
Datum feature triangle: this symbol always has a leader extending from it to the point of application. The leader includes a triangle at the end. It may be filled or left open. The triangle is sometimes referred to as a suction cup, but it is correctly identified as a datum feature triangle.
Datum feature symbol: a rectangle with two short dashes.

## Slide 13: Runout symbols
Circular runout: single arrow pointing in an upward direction indicates circular runout.
Total runout: two parallel arrows pointing upward and connected by a horizontal line at the bottom of the arrows indicates a total runout requirement.

## Slide 14: Letters: X and R
The letter x is used to indicate a number of times or places a feature or item is repeated.
If the x is to indicate the number of times or places, no space is shown between the number of occurrences and the letter x.
The letter x can also be used in place of the word BY. A space is placed on each side of the letter x for this usage. For example:
.125 by .750 would be shown as .125 x .750
The letter R is placed in front of any value that indicates a radius dimension.

## Slide 15: PCD
Pitch circle diameter (PCD) is the diameter of a circular component that is to be manufactured, which usually has holes drilled into it. For example, the circle drawn through the centre of the bolt holes of a wheel.
PCD is measured in millimetres, and often indicates the number of bolts a wheel will have.

## Slide 16: Other common abbreviations
You will come across all these common abbreviations on engineering drawings.
across flats AF
centre line CL
centres CRS
chamfer CHAM
counterbore CBORE
countersink CSK
external EXT
internal INT
not to scale NTS
revision Rev
specification SPEC
spot face SFACE
thickness THK
standard STD

## Slide 17: Other common abbreviations
Hexagon head (HEX)
Undercut (UCUT)
Thread (THD)
Notes: Image sources: Undercut- John Hackney (https://forums.autodesk.com/t5/fusion-360-support/drawings-can-t-dimension-to-undercut/td-p/9843823).
Thread- S.Bachar (https://community.sw.siemens.com/s/contentdocument/0694O000007DS6BQAW).

## Slide 18
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.