## Slide 1: PowerPoint 5: Examples of standard features
3. Engineering representations
3.1 Drawings and information conveyed by drawings

## Slide 2
Objectives
By the end of this session, learners should be able to:
describe and identify examples of standard engineering drawing features.
PowerPoint presentation

## Slide 3: Screw threads
Screw threads may be either left or right hand, as shown below. Notice the slope of the thread and the position of the index finger on each hand. The right-hand thread is the most commonly used. The left-hand thread is used for special applications.

## Slide 4: Thread gender
Every matched pair of threads (external and internal), such as those on nuts and bolts, can be described as male and female. For example, a bolt has male threads, while its matching hole (whether in nut or substrate) has female threads. This property is called gender.

## Slide 5: Lead and pitch
Lead and pitch are closely related concepts. They can be confused because they are the same for most screws:
lead is the distance along the screw’s axis that is covered by one complete rotation of the screw – 360 degrees
pitch is the distance from the crest of one thread to the next.

## Slide 6: How threads are illustrated
Threaded fasteners are drawn with detailed, schematic or simplified representations.

## Slide 7: How threads are illustrated
Notes: Image source: https://www.mcgill.ca/engineeringdesign/step-step-design-process/basics-graphics-communication/dimensioning-threaded-fasteners.

## Slide 8: ISO thread standards
A metric ISO screw thread is designated by the letter M followed by the value of the nominal diameter D and the pitch P, both expressed in millimetres and separated by the multiplication sign, x (eg M8×1). If the pitch is the most frequently used ‘coarse’ pitch it can be omitted (eg M8).
The coarse pitch is the commonly used default pitch for a given diameter. One or two smaller ‘fine’ pitches can also be defined, for use in applications where the height of the normal coarse pitch would be unsuitable (eg threads in thin-walled pipes).

## Slide 9: Hole features
The drawing shows how counterbore (CBORE) and countersink (CSK) holes are represented, along with other common hole types.
Notes: Jensen, Cecil and Raymond Hines “Interpreting Engineering drawings” 5th Edition, Delmar Publishers, 1994. Cengage Learning Inc. Reproduced by permission. www.cengage.com/permissions.

## Slide 10: Standard nut, bolt and washer representation

## Slide 11
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.