## Slide 1: PowerPoint 7: Dimensions and tolerances
PowerPoint presentation
3. Engineering representations
3.2 Dimensions and tolerancing on engineering drawings

## Slide 2
Objectives
By the end of this session, learners should be able to:
understand dimension types
identify/interpret dimensions
apply dimensions to a drawing.
PowerPoint presentation

## Slide 3: Dimensioning
A dimensioned drawing should provide all the measurements necessary for a finished product or part to be manufactured. An example dimension is shown below.

## Slide 4: Some rules for dimensions
Dimensions are always drawn using continuous thin lines.
Two projection lines indicate where the dimension starts and finishes (see the drawing on the previous slide).
Projection lines do not touch the object and are drawn at right angles to the element you are dimensioning.
All dimensions less than 1 should have a leading zero, so for example .35 should be written as 0.35.

## Slide 5: Parallel dimensioning
Parallel dimensioning consists of several dimensions originating from one projection line.
Projection line

## Slide 6
Superimposed running dimensioning simplifies parallel dimensions in order to reduce the space used on a drawing.
The common origin for the dimension lines is indicated by a small circle at the intersection of the first dimension and the projection line (see below left).
Superimposed running dimensioning

## Slide 7
A combined dimension uses both chain and parallel dimensioning.
Chain and combined dimensioning
Chain dimensioning

## Slide 8: Dimensioning circles
Approach (a) shows two common methods of dimensioning a circle. One method dimensions the circle between two lines projected from two diametrically opposite points. The second method dimensions the circle internally.
Approach (b) is used when the circle is too small for the dimension to be easily read if it was placed inside the circle.

## Slide 9: Dimensioning radii
All radial dimensions are preceded by the capital R.
shows a radius dimensioned with the centre of the radius located on the drawing.
(b) shows how to dimension radii which do not need their centres locating.

## Slide 10: Tolerancing
It is not possible in practice to manufacture products to the exact figures displayed on an engineering drawing. The accuracy depends largely on the manufacturing process. A tolerance value shows the manufacturer the maximum permissible variation from the dimension.
Each dimension on a drawing must include a tolerance value. This can appear as a general tolerance value applicable to several dimensions (eg a note specifying that the general tolerance is +/- 0.5 mm), or a tolerance specific to that dimension (in the example below, the item must be between 45.25 and 44.80).

## Slide 11: Your turn
How many dimension features can you identify in this diagram?
Answers on the next slide.

## Slide 12: Dimension features
How many of features did you spot?

## Slide 13
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.