## Slide 1: PowerPoint 8: Limits and fits
PowerPoint presentation
3. Engineering representations
3.2 Dimensions and tolerancing on engineering drawings

## Slide 2
Objectives
By the end of this session, learners should be able to:
understand limits and fits as related to dimensions and tolerancing
calculate limit and fit sizes.
PowerPoint presentation

## Slide 3: What are limits and fits?
Limits and fits are a set of rules relating to the dimensions and tolerances of machined parts. Manufactured components for assembly usually have specified fits. This means the way in which the parts interact with each other.
The easiest way to conceptualise this is to imagine a shaft and a hole.
The size of the shaft and hole are determined by the required fit.
Some components must slip or press against each other to function correctly.
There are three main fit types which are explained on the following slides.

## Slide 4: Clearance fit
The maximum size of the shaft is always smaller than the minimum size of the hole.

## Slide 5: Types of clearance fit
Loose running fits: clearance fits with the largest clearance used in places where accuracy is not important.
Free running fits: for situations that require the movement of components with little consideration of accuracy.
Close running fits: for situations that require a small clearance with regard to accuracy.
Sliding fits: for situations that require high accuracy and small clearance.
Locational clearance fits: have high accuracy but can only provide minimal clearance.

## Slide 6: Interference fits
For interference fits, the maximum size of the shaft is always bigger than the minimum size of the hole.

## Slide 7: Types of interference fit
There are three:
press fit: minimal interference because assembly is by cold pressing
driving fit: more prominent interference than press fit, requiring greater assembly force
forced fit: assembling components requires heating the parts with a hole and freezing the shaft, hence disassembly can lead to broken parts.

## Slide 8: Transition fit
The maximum size of the shaft is somewhat equal to the minimum size of the hole.

## Slide 9: Types of transition fit
There are two:
similar fits leave a small clearance or create a small interference, and assembly can be achieved using a rubber mallet
fixed fits leave a small clearance or create a small interference, and assembly is possible using light force.

## Slide 10: Standards for limits and fits
BS4500 (also now known as ISO limits and fits) was the standard for limits and fits, based on holes and shafts. This is now included as an appendix in BS8888.
Each range of hole size is allocated a capital letter and a number.
Each range of shaft size is allocated a lower case letter and a number.
It is theoretically possible to have very large range of fits, but in practice certain combinations fulfil most requirements.
Table 1 on Slide 12 shows how the tolerance system works in practice for clearance fit (see yellow highlight). In this case, the selection is such that the fit provides a precision running fit suitable for a plain bearing and a shaft. The nominal size of the shaft hole is 25mm diameter.

## Slide 11: Limits and fits: common abbreviations
Here are some common abbreviations you will come across in the following tables:
ES (ecart superior) = upper deviation for holes
EI (ecart inferior) = lower deviation for holes
es = upper deviation for shafts
ei = lower deviation for shafts.

## Slide 12: Table 1: Shaft fits
Type of fit |  | Clearance |  |  |  |  |  | Transition |  | Interference | 
Shaft tolerance |  | c11 | d10 | e9 | f7 | g6 | h6 | k6 | n6 | p6 | s6
Hole tolerances | H7 |  |  |  |  |  |  |  |  |  | 
 | H8 |  |  |  |  |  |  |  |  |  | 
 | H9 |  |  |  |  |  |  |  |  |  | 
 | H11 |  |  |  |  |  |  |  |  |  | 
Refer to Table 2 (next slide) to calculate the tolerance for the hole.
In this case, the nominal size of the shaft is 25mm diameter using an H8f7 fit.

## Slide 13: Table 2: Tolerance limits for bores/holes
Basic sizes |  | Tolerance unit = 0.001mm |  |  |  |  |  |  | 
Over | Up to and incl. | H7 |  | H8 |  | H9 |  | H11 | 
 |  | ES+ | EI | ES+ | EI | ES+ | EI | ES+ | EI
mm 3 | mm 6 | 12 | 0 | 18 | 0 | 30 | 0 | 75 | 0
6 | 10 | 15 | 0 | 22 | 0 | 36 | 0 | 90 | 0
10 | 18 | 18 | 0 | 27 | 0 | 43 | 0 | 110 | 0
18 | 30 | 21 | 0 | 33 | 0 | 52 | 0 | 130 | 0
30 | 50 | 25 | 0 | 39 | 0 | 62 | 0 | 160 | 0
50 | 80 | 30 | 0 | 46 | 0 | 74 | 0 | 190 | 0
80 | 120 | 35 | 0 | 54 | 0 | 87 | 0 | 220 | 0
120 | 180 | 40 | 0 | 63 | 0 | 100 | 0 | 250 | 0
180 | 250 | 46 | 0 | 72 | 0 | 115 | 0 | 290 | 0
Hole size 25mm upper limit + 0.033mm, lower limit + 0.0mm
Refer to Table 3 (Slide 14) to calculate the tolerance for the shaft.

## Slide 14: Table 3: Tolerance limits for shafts
Basic sizes |  | Tolerance unit = 0.001mm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Over | Up to and incl. | c11 |  | d10 |  | e9 |  | f7 |  | g6 |  | h6 |  | k6 |  | n6 |  | p6 |  | s6 | 
 |  | es – | ei – | es – | ei – | es – | ei – | es – | ei – | es – | ei – | es – | ei – | es + | ei + | es + | ei + | es + | ei + | es + | ei +
mm 3 | mm 6 | 70 | 145 | 30 | 78 | 20 | 50 | 10 | 22 | 4 | 12 | 0 | 8 | 9 | 1 | 16 | 8 | 20 | 12 | 27 | 19
6 | 10 | 80 | 170 | 40 | 98 | 25 | 61 | 13 | 28 | 5 | 14 | 0 | 9 | 10 | 1 | 19 | 10 | 24 | 15 | 32 | 33
10 | 18 | 95 | 205 | 50 | 120 | 32 | 75 | 16 | 34 | 6 | 17 | 0 | 11 | 12 | 1 | 23 | 12 | 29 | 18 | 39 | 28
18 | 30 | 110 | 240 | 65 | 149 | 40 | 92 | 20 | 41 | 7 | 20 | 0 | 13 | 15 | 2 | 28 | 15 | 35 | 22 | 48 | 35
30 | 40 | 120 | 280 | 80 | 180 | 50 | 112 | 25 | 50 | 9 | 25 | 0 | 16 | 18 | 2 | 33 | 17 | 42 | 26 | 59 | 43
40 | 50 | 130 | 290 | 80 | 180 | 50 | 112 | 25 | 50 | 9 | 25 | 0 | 16 | 18 | 2 | 33 | 17 | 42 | 26 | 59 | 43
50 | 65 | 140 | 330 | 100 | 220 | 60 | 134 | 30 | 60 | 10 | 29 | 0 | 19 | 21 | 2 | 39 | 20 | 51 | 32 | 72 | 53
65 | 80 | 150 | 340 | 100 | 220 | 60 | 134 | 30 | 60 | 10 | 29 | 0 | 19 | 21 | 2 | 39 | 20 | 51 | 32 | 78 | 59
80 | 100 | 170 | 390 | 120 | 260 | 72 | 159 | 36 | 71 | 12 | 34 | 0 | 22 | 25 | 3 | 45 | 23 | 59 | 37 | 93 | 71
100 | 120 | 180 | 400 | 120 | 260 | 72 | 159 | 36 | 71 | 12 | 34 | 0 | 22 | 25 | 3 | 45 | 23 | 59 | 37 | 101 | 79
120 | 140 | 200 | 450 | 145 | 305 | 85 | 185 | 43 | 83 | 14 | 39 | 0 | 25 | 28 | 3 | 52 | 27 | 68 | 43 | 117 | 92
140 | 160 | 210 | 460 | 145 | 305 | 85 | 185 | 43 | 83 | 14 | 39 | 0 | 25 | 28 | 3 | 52 | 27 | 68 | 43 | 125 | 100
160 | 180 | 230 | 480 | 145 | 305 | 85 | 185 | 43 | 83 | 14 | 39 | 0 | 25 | 28 | 3 | 52 | 27 | 68 | 43 | 133 | 108
180 | 200 | 240 | 530 | 170 | 355 | 100 | 215 | 50 | 96 | 15 | 44 | 0 | 29 | 33 | 4 | 60 | 31 | 79 | 50 | 151 | 122
200 | 225 | 260 | 550 | 170 | 355 | 100 | 215 | 50 | 96 | 15 | 44 | 0 | 29 | 33 | 4 | 60 | 31 | 79 | 50 | 159 | 130
225 | 250 | 280 | 570 | 170 | 355 | 100 | 215 | 50 | 96 | 15 | 44 | 0 | 29 | 33 | 4 | 60 | 31 | 79 | 50 | 169 | 140
Shaft size 25mm has an upper limit of 0.020mm.
The lower limit is 0.041mm.

## Slide 15: Calculating fits
The nominal size of the shaft and hole is 25 mm diameter, which is greater than 18 mm and less than 30 mm. H8 and f7 clearance fit is suitable for a precision running fit.
From the relevant tables an H8 is +33, +0 and an f7 is –20, –41.
*MMC means ‘maximum material condition’. Thus, when both the shaft and the hole are on MMC there will be 25.00 – 24.980 = 0.020 mm clearance.
 | Bore of component (H8) in mm | Diameter of shaft (f7) in mm
MMC* | 25.000 | 24.980
 | 25.033 | 24.959

## Slide 16
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.