## Slide 1: PowerPoint 1: SI units
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.1 Units of measurement used in engineering

## Slide 2: Objectives
By the end of this session, learners should be able to:
state the units of measurement used in engineering and what they represent
convert between SI units and imperial units
convert between different multiples and submultiples.

## Slide 3: What are SI units ?
The units that scientists use all over the world are standardised in the Système Internationale d’Unités: SI units. (There is one exception – North America uses imperial units.) Working in SI units means measurements are consistent and recognised globally.
There are seven base units:
kilogram (kg)
metre (m)
second (s)
ampere (A)
kelvin (K)
mole (mol)
candela (cd)

## Slide 4: SI units in engineering
Here are some of the base units you are mostly likely to encounter within the engineering sector
Property | SI unit | Abbreviation
mass | kilogram | kg
time | second | s
length (distance) | metre | m
Note that when using SI units there should be a space between the value and the unit. When using the full word it should not be capitalized unless at the start of a sentence. For example, 3 m = 3 metres,

## Slide 5: Mass and weight
Mass is the amount of matter in an object and is measured in kilograms. An object cannot have a mass of zero.
Weight is a force due to the pull of gravity on the mass of the object and is measured in newtons (N). Weight = force × acceleration due to gravity.
We often confuse the terms and weight is often quoted in kilograms.
Pressure is defined as force/area. The SI unit for force is newtons (N) and the SI unit for area is square metres (m²). One newton per square metre (N m−²) equals 1 pascal.
Example: When a liquid or a gas is in contact with a solid surface such as water in a tank it produces a force on that surface. The pressure of the fluid is defined as the force per unit area.

## Slide 6: Using SI units
Area is measured in m2
e.g., for a room 10 m long by 10 m wide, area = 10 ×10 = 100 m2
Volume is measured in m3
e.g., for a room 10 m long by 10 m wide by 10 m high,
volume = 10×10 ×10 = 1000 m3
One litre is a volume of 0.001 m3 or 1000 cm3 .

## Slide 7: SI units in engineering
Derived units come from the seven base units. For example, a newton is a unit of force, which is the same as kg m s−2
Here some of the derived units you are mostly likely to encounter within the engineering sector.
Property | SI unit | Abbreviation | Equivalent to
density |  |  | kg/m3 or kg m−3
velocity |  |  | m/s or m s−1
acceleration |  |  | m/s2 or m s−2
force | newton | N | kg m/s2 or kg m s−2
pressure | pascal | Pa | N/m2 or N m−2

## Slide 8: Other derived units used in the engineering sector
You will encounter the following in other units in this qualification:
Specific heat capacity is measured in kJ kg−1 ºC−1.
When working with electricity, as well as the base SI unit of amperes (A):
volt (V) is the derived unit for electric potential, electric potential difference (voltage) and electromotive force
ohm (Ω) is the derived unit of electrical resistance
coulomb (C) is the derived unit of electric charge
watt (W) is an SI unit of power used to measure the rate of energy transfer.

## Slide 9: Multiples and sub-multiples
When working with small areas, volumes, distances or power supplies, the units you calculate are comparatively small and therefore not difficult to record.
For example, the UK mains power supply is an alternating current with a frequency of 50 hertz (Hz) and 230 volts (V).
In large engineering projects, the forces, distances, speeds or volumes involved can be much larger, meaning the numbers become inconvenient to record in full. In precision engineering, there will also be very tiny and precise measurements.
In engineering notation or engineering form the exponent of 10 must be divisible by 3 (i.e. powers of a thousand, but written as, for example, 106 instead of 10002).

## Slide 10: Multiples and sub-multiples
Multiples and sub-multiples allow orders of magnitude to be recorded in shortened form.
Multiple size | Power of 10 (×10x) | Prefix | Prefix abbreviation
1 000 000 000 000 | 12 | tera- | T
1 000 000 000 | 9 | giga- | G
1 000 000 | 6 | mega- | M
1000 | 3 | kilo- | k
0.01 | −2 | centi- | c
0.001 | −3 | milli- | m
0.000 001 | −6 | micro- | μ
0.000 000 001 | −9 | nano- | n
0.000 000 000 001 | −12 | pico- | p

## Slide 11: Worked example: Engineering standard form
The distance from the Sun to Pluto is 4 400 000 000 000 m
This can also be written as:
4.4 × 1012 m
It can be shortened again with the prefix tera to:
4.4 terametres
Or abbreviated to:
4.4 Tm

## Slide 12: Which is greater?
Which is greater:
230 kV or 2.3 MV?
230 kV is equivalent to 230 kV = 230 × 1000 = 230 000 V
2.3 MV is equivalent to 2.3 MV = 2.3 × 1 000 000 = 2 300 000 V
So, 2.3 MV is the greater amount.

## Slide 13: Metric and imperial units
Within engineering you might encounter units that follow the imperial system rather than the SI system, for example when using American equipment. The table below shows how to convert between metric (SI) and imperial measurements.
Property | SI unit | Imperial unit | Conversion
length | metre | inch (in) | 1 in = 0.0254 m = 25.4 mm
length | metre | foot (ft) | 1 ft = 0.3048 m = 304.8 mm
length | metre | yard (yd) | 1 yd = 0.9144 m = 914.4 mm
mass | kilogram | ounce (oz) | 1 oz = 0.02835 kg = 28.35 g
volume | litre | gallon (gal) | 1 gal = 4.546 litres

## Slide 14: Other SI units used in the engineering sector
SI unit | Abbreviation | Measures
watt | W | power
bar | bar | pressure
joule | J | energy
candela | cd | luminous intensity
Illuminance | lux | illumination
kelvin | K | temperature
Here are some of the other units you might encounter within the engineering sector.

## Slide 15
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.