## Slide 1: PowerPoint 10: Hydrostatic pressure
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.7 Fluid dynamics in engineering

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain what is meant by hydrostatic pressure and centre of pressure
calculate hydrostatic pressure
calculate hydrostatic thrust on an immersed plane surface.

## Slide 3
Hydrostatic pressure is defined as
‘The pressure exerted by a fluid at equilibrium at any point of time due to the force of gravity.’
Hydrostatic pressure is proportional to the depth in the fluid, measured from the surface, as the weight of the fluid increases when a downward force is applied.
Hydrostatic pressure
The fluid pressure can be caused by gravity, acceleration or forces when in a closed container.

## Slide 4
Consider a layer of water near the top of the bottle. There is pressure exerted by the layer of water on the sides of the bottle.
As you move down from the top of the bottle to the bottom, the pressure exerted by the layers above builds up.
Hydrostatic pressure example

## Slide 5
Hydrostatic pressure formula
The formula used to calculate hydrostatic pressure is
P = ρ g h
where,
  P is the pressure exerted by the liquid in N m−2 or Pa
  ρ is the density of the liquid in kg m−3
  g is the acceleration due to gravity taken as 9.81 m s −2
  h is the height of the fluid column in m

## Slide 6
Depth of water |  | Pressure | 
feet | metres | pascal | bar
1 | 0.30 | 2943 | 0.03
5 | 1.52 | 14911.2 | 0.15
10 | 3.05 | 29920.5 | 0.30
15 | 4.57 | 44831.7 | 0.45
Hydrostatic pressure vs depth of water

## Slide 7
The pressure in a fluid does not depend on factors such as the surface area of the container, the mass of the liquid or its volume.
Liquids in an open container always have the same height in every part of the container – regardless of its shape.
A communicating vessel – the height of fluid is the same in each part of the vessel.
The behaviour of a fluid

## Slide 8
Centre of pressure
Hydrostatic force is the resultant force acting on a submerged surface due to the pressure loading of the fluid into which the surface is submerged.
Centre of pressure
The location of the point of action of the hydrostatic force is the centre of pressure. The centre of pressure is always below the centre of gravity of the surface in contact.

## Slide 9
Hydrostatic thrust acting on an immersed surface
The thrust force acting on a surface submerged in a liquid can be calculated using
F = Pa A = ρ g A x
where
F = thrust force (N)
Pa = ρ g ha = average pressure on the surface (Pa)
A = area of submerged surface (m2)
x = average depth (m)
ρ = density (kg m−3) (water 1000 kg m−3)
g = acceleration of gravity (9.81 m s−2)

## Slide 10
Example – the thrust force acting on the side of a container
The trust force acting on the submerged vertical side of a container can be calculated using
F = PaA
= A = A
where
Pt = pressure at the top of the submerged surface (Pa)
Pb = pressure at the bottom of the submerged surface (Pa)
ht = depth at the top of the submerged surface (m)
hb = depth at the bottom of the submerged surface (m)

## Slide 11
The thrust on a surface with width 1 m and height from 0 m to 2 m in a water-filled container can be calculated as
F = A
=
= 19 620 N
= 19.6 kN
Example (continued)

## Slide 12
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.