## Slide 1: PowerPoint 11: Bernoulli’s principle
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.7 Fluid dynamics in engineering

## Slide 2: Objectives
By the end of this session, learners should be able to:
state Bernoulli’s principle and apply it to calculations.

## Slide 3: Definitions
One aspect of fluid dynamics is the movement of fluids, for example flows in pipes. Here are some useful definitions.
Flow is a measure of the volume of fluid that flows per unit of time. Units are, for example, litres per minute.
Mass flow rate is the mass of fluid passing a point in a system per unit of time. Units are, for example, kg s−1.
Flow velocity refers to how quickly the fluid is moving. This can be measured in, for example, m s−1.
Pressure is a measure of force applied on an area. Units are, for example, N mm-2 or Pa.

## Slide 4: Viscosity
Most materials (and gases) occupy a smaller volume when they are squeezed – which means they become denser.
The viscosity of a fluid is a measure of its resistance to deformation at a given rate – different fluids have different levels of viscosity.
For example, oil, glycerin and tar are highly viscous.
Volume at lower pressure
Volume at higher pressure

## Slide 5: Incompressible fluids
An ideal hydraulic system uses incompressible fluid.
This is a fluid whose density does not change when the pressure changes. This means that when the pressure is increased its volume stays the same.
Volume at lower pressure
Volume at higher pressure
Incompressible fluid –
volume stays same under pressure

## Slide 6: Bernoulli’s principle
In fluid dynamics, Bernoulli's principle states that an increase in the speed of a fluid occurs simultaneously with a decrease in pressure or a decrease in the fluid's potential energy.
Notes: The principle is named after Daniel Bernoulli, a Swiss mathematician, who published it in 1738 in his book Hydrodynamics.

## Slide 7: Understanding Bernoulli’s principle
The Bernoulli equation can be considered to be a statement of the conservation of energy principle applied to flowing fluids.
The qualitative behaviour that is usually labelled with the term ‘Bernoulli effect’ is the lowering of fluid pressure in regions where the flow velocity is increased.
This lowering of pressure in a constriction of a flow path may seem counterintuitive, but seems less so when you consider pressure to be energy density.
In the high velocity flow through the constriction, kinetic energy must increase at the expense of pressure energy.

## Slide 8: Pressure and Bernoulli equation
Pressure, P = force × area = F A
For a hydraulic system where two points (1 and 2) lie on a streamline, Bernoulli’s equation states that
= constant, where:
  P = pressure
  ρ = density
  v = flow velocity
  h = elevation
  g = gravity
  This assumes that:
  the fluid has constant density/is incompressible
  the flow is steady
  there is no friction.

## Slide 9: Mass flow rate
The volume flowing through a hydraulic system in a certain time can be found by multiplying the cross sectional area by the flow velocity.
V = A × v.
Note that V is the volume and v is the flow velocity.
Mass = density × volume = ρ V = ρ v A
Mass flow rate =
=
=
(which, for t =1, = ρ v A)

## Slide 10: Mass flow rate example
  In a hydraulic system, a pipe has an area of cross section of 120 mm2.
  A fluid of density 1000 kg m−3 flows through the pipe at a velocity of 1.5 m s−1.
  Calculate the mass flow rate.
  Answer:
  Taking t = 1:
  mass flow rate = ρ v A = 1000 × 1.5 × 1.2 × 10−4
  mass flow rate = 0.18 kg s-1

## Slide 11: Changes in pipe diameter
If the diameter of a pipe changes (such as in a tapered pipe), its cross sectional area changes.
When an incompressible fluid flows at a constant rate in a pipe, the mass flow rate must be the same at all points along the pipe.
As the mass flow rate and pressure are constant, a change in the cross sectional area changes the flow velocity.
i.e. v1A1 = v2A2
Using Bernoulli’s equation, the change in pressure between two points in the system where there is a difference in diameter (such as in a tapered pipe) can be expressed as:
Note: this assumes that the difference in the value of g is negligible.

## Slide 12: Example calculation
In a hydraulic system, an incompressible fluid is pumped at a constant mass flow rate through a tapered pipe.
The fluid is pumped into a pipe of area 1.6 × 10−3 m2, where the flow velocity is measured at 0.2 m s−1 and the pressure is 80 bar. The density of the fluid is 900 kg m−3.
Calculate the pressure where the area of the pipe has reduced to 0.8 × 10−3 m2.
Answer:
Rearranging gives m s−1
Rearranging gives
bar

## Slide 13: Bernoulli’s principle in flight
Bernoulli's principle can also be used to calculate the lift force on an aerofoil, if the behaviour of the fluid flow in the vicinity of the foil is known.
For example, if the air flowing past the top surface of an aircraft wing is moving faster than the air flowing past the bottom surface, then Bernoulli's principle implies that the pressure on the upper surface of the wing will be lower above the pressure below the wing.

## Slide 14: Bernoulli’s principle in flight
This pressure difference results in an upwards lifting force (lift).
Whenever the distribution of speed past the top and bottom surfaces of a wing is known, the lift forces can be calculated (to a good approximation) using Bernoulli's equations.

## Slide 15
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.