## Slide 1: PowerPoint 16: Gas laws
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.8 Thermodynamics in engineering

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the difference between pressure and absolute pressure
state Boyle’s law and apply it to calculations of practical examples
state Charles’ law and apply it to calculations of practical examples
state the general gas equation and apply it to calculations of practical examples
state the characteristic gas equation and apply it to calculations of practical examples.

## Slide 3: Pressure
Pascal’s law states:
‘The pressure on a confined fluid is transmitted equally to the whole surface of its container.’
In the example to the right, the gas exerts an equal pressure on the cylinder walls and the piston in all directions.
Regular gauge
Pressure
L
W
Force
Pressure is a measure of the amount of force that is applied to a specific area.

## Slide 4: Pressure calculation
Pressure,
The units of pressure are Pa, N mm−2 or N m−2.
  Example
  A cylinder of surface area 40 mm2 transmits force from a pneumatic system. If the gas pressure in the pneumatic system is 240 N mm−2, calculate the force exerted by the cylinder.
  Answer:
  Rearranging gives F = P × A = 240 × 40 = 1440 N

## Slide 5: Absolute pressure
An absolute pressure is one that is compared with the pressure of an ideal vacuum.
In comparison, pressure at sea level in the atmosphere we breathe is approximately 1.01325 millibars – this reduces as altitude increases.

## Slide 6: Charles’ law
The volume of an ideal gas at constant pressure is directly proportional to the absolute temperature.
Volume at higher temperature
Volume of same gas at lower temperature

## Slide 7: Charles’ law example
  A pneumatic system contains 0.6 m3 of air at 450 K. If the temperature of the air is decreased to 300 K, calculate the change in volume of the gas.
  Assume that there is no pressure change in the system.
  Answer
  Rearranging
  gives V2 = V1 ×
  V2 = 0.6 × = 0.4 m3
  Change in volume = 0.6 − 0.4 = 0.2 m3

## Slide 8: Boyle’s law
For a fixed mass of gas at constant temperature, the volume is inversely proportional to the pressure
P1 V1 = P2 V2
Volume at lower pressure
Volume of same gas at higher pressure

## Slide 9: Boyle’s law example
A gas cylinder contains 18 m3 of gas at a pressure of 90 bar. Calculate the pressure in the cylinder after the gas is compressed to 12 m3.
Answer
Rearranging gives P1 V1 P2 V2
135 bar

## Slide 10: Mass and density
It should be noted that when applying both Boyle’s law and Charles’ law, the quantity of the gas remains the same – this means that the mass is constant.
When the volume of a gas changes, the density changes.
Density can be calculated using the formula
density =
Common units of density are kg/m3.

## Slide 11: General gas equation
If one or more of these properties change, it will result in changes to the other properties. These now become P2, V2 and T2.
The equations now become:
or just
In this example let us suppose that a fixed mass of gas has the properties P1, V1 and T1.
where n is the number of moles of gas and R is the gas constant

## Slide 12: Example (general gas equation)
A sealed box containing a sample of gas at a pressure of 1  105 Pa is heated from 270 K to 300 K. What is the pressure exerted by the gas on the wall the box now?
Step 1: All quantities are in the correct units so there is no need to convert any.
Step 2: Rearrange the gas equation so that the unknown is on its own. Since the volume remains constant, V can be eliminated.

## Slide 13
Step 3: Substitute the numbers into the equation.
The new pressure is 1.11  105 Pa.
Example (general gas equation)
P2 Pa
P2 1.11  105 Pa

## Slide 14: Characteristic gas equation
The characteristic gas equation is pV = mRT
where:
pressure (P), in kilopascals (kPa)
volume (V), in litres (L)
temperature (T), in kelvin (K)
mass of the gas (m)
the value of R is a constant that depends on the molar mass of the gas.
Note that, here, R is NOT the universal gas constant 8.31 J K−1 mol−1 used in the ideal gas laws in physics.

## Slide 15
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.