## Slide 1: PowerPoint 2: Vectors and coordinates
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.2 Vector and coordinate measuring systems

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the difference between scalar and vector quantities
state examples of scalar and vector quantities
convert between Cartesian and polar coordinates.

## Slide 3: Scalars and vectors
A quantity that has only magnitude is called a scalar quantity.
Examples of scalar quantities include distance, speed and mass.
Other scalar quantities include time and temperature.
A quantity that has magnitude and direction is called a vector quantity and can be represented by vectors.
Examples of vector quantities include displacement and velocity.

## Slide 4: Scalars and vectors: speed and velocity example
Speed is a scalar quantity as it has magnitude only.
Velocity is a vector quantity as it has both magnitude and direction.

## Slide 5: Coordinates
Coordinates specify positions – for example, GPS systems use them to determine where you are.
One common use in engineering is to instruct the tool where to move in CAM machines.
Types of coordinates include Cartesian (x, y) and polar (r, θ).

## Slide 6: Cartesian coordinates
Cartesian coordinates indicate the location of a point relative to a fixed reference point (the origin).
They are read across first, then up (or down).
The coordinates plotted are:

## Slide 7: Polar representation
Polar coordinates may be written in the form
Using polar coordinates, we identify a point by how far away from the origin it is along a straight line, r, and the angle this line makes with the positive x-axis, θ , e.g. (14, 36⁰).
The value of r is called the modulus.
This is denoted by mod z or | z|.
To find the modulus from Cartesian coordinates, use Pythagoras’ theorem:
(r, θ) or r θ

## Slide 8: Polar argument
The angle θ is called the argument (or amplitude) of the polar coordinates.
It is denoted by arg z or amp z
Hence arg z = θ
To find the argument of a polar coordinate from Cartesian coordinates, use trigonometry:

## Slide 9: Converting between Cartesian and polar coordinates
Convert the Cartesian coordinates (2, 4) into polar form.
Using Pythagoras’ theorem and trigonometry:
r = = 4.47
θ = tan−1 = tan−1 2 = 63.4o so the coordinates are (4.47, 63.4o)
Convert the polar coordinates (4.47, 63.4o) into Cartesian form.
Using trigonometry:
x = r cos θ = 4.47 cos 63.4o = 2
y = r sin θ = 4.47 sin 63.4o = 4 so the coordinates are (2, 4)
Notes: Note: all calculations shown to 3 significant figures.

## Slide 10: Conversion from Cartesian to polar coordinates
To convert from Cartesian to polar coordinates:
When we know a point in Cartesian coordinates (x, y) and we want to write it in polar coordinates (r, θ), we solve a right-angled triangle with two known sides.
Example A: What is (12, 5) in polar coordinates?

## Slide 11
Use Pythagoras’ theorem to find the longest side of the triangle (the hypotenuse (r)):
r2 = 122 + 52
r =
r =
r = = 13
Use the tan function to find the angle:
tan θ =
θ = tan−1 = 22.6° (to one decimal place)
Answer: (12, 5) is equal to (13, 22.6o) in polar coordinates.

## Slide 12: Conversion from polar to Cartesian coordinates
To convert from polar to Cartesian coordinates:
When we know a point in polar coordinates (r, θ), and we want to write it in Cartesian coordinates (x, y), we solve a right-angled triangle with a known longest side and angle.
Example B: What is (13, 22.6o) in Cartesian coordinates?

## Slide 13
Use the cosine function for x: cos 22.6 =
Rearranging and solving gives: x = 13 × cos 22.6°
x = 13 × 0.923
x = 12.0 to one decimal place
Use the sine function for y: sin 22.6 =
Rearranging and solving gives: y = 13 × sin 22.6°
y = 13 × 0.391
y = 5.0 to one decimal place
Hence (13, 22.6o) is (12, 5) in Cartesian coordinates.

## Slide 14: Example: Velocity of an aircraft
Velocity can be represented by a vector.
Imagine an aircraft flying north at a speed of 60 m s−1.
The arrow represents the velocity of the aircraft; the length of the arrow represents the speed, and the direction represents the direction of travel.
60 m s−1 north

## Slide 15: Velocity example (continued)
Imagine the same aircraft flying north at a speed of 60 m s−1, but, in this case, there is a wind blowing that has a velocity of 20 m s−1 to the east.
An additional vector can be drawn to represent the actual velocity of the aircraft after taking the wind speed and direction into account .
60 m s−1 north
20 m s−1 east

## Slide 16: Velocity example (continued)
The actual velocity of the aircraft, resulting from its northward motion and effect of the easterly wind, is represented by another vector, shown here with a dashed arrow.
60 m s−1 north
20 m s−1 east
?

## Slide 17: Velocity example (continued)
The actual velocity of the aircraft can be found by adding the two vectors together.
If the two vectors are at right angles to each other, you can use Pythagoras’ theorem.
Magnitude
c2 = a2 + b2
c2 = (60 × 60) + (20 × 20) = 4000
c = 63.24 m s−1

## Slide 18: Velocity example (continued)
The resultant direction of the aircraft can be found using trigonometry.
Direction
Angle = tan−1
= tan−1
= 18.4°
60 m s−1 north
20 m s−1 east
Solution: Therefore the velocity can be represented as either (20, 60) in Cartesian coordinates or (63.24, 18.4o) in polar coordinates.

## Slide 19
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.