## Slide 1: PowerPoint 10: Surface treatments
PowerPoint presentation
6. Materials and their properties
6.4 Heat treatments and surface treatments

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand how surface treatment processes affect the properties of materials.
Notes: The picture shows the galvanizing process.

## Slide 3: Painting
Applications of paint to a material surface can alter the manner in which the material reacts to external forces and can protect the material from oxidation and corrosion.
It should be noted that the content of the paint can have an adverse effect on the base material (eg solvent-based paints can break down the polymer chains in thermoplastics).

## Slide 4: Plastic coating
Plastic coating is a process that involves immersing a preheated part into liquid plastisol to form a plastic coating that can add protection and aesthetic value to most metal parts.
The procedure can enhance the appearance of the part, provide a soft grip and/or protect the part from chemicals and abrasion.
Special purpose additives can be used in the coating to provide specific characteristics such as fungal resistance, dielectric strength and flame retardancy.

## Slide 5: Galvanising
In its simplest form, galvanising refers to the application of a zinc coating to the surface of a metal (usually steel or iron).
It is mainly used as a protective measure to prevent corrosion and, by extension, increase the serviceable life of the protected metal component.
When properly applied to a steel surface, zinc coatings offer two main types of protection: barrier protection and galvanic protection.

## Slide 6: Barrier protection
When the zinc coating is applied to the surface, it dries and hardens to form a protective zinc oxide layer or barrier that is impervious to air and moisture, thus eliminating one of the components needed for corrosion to occur – the electrolyte.
Because the underlying steel substrate is unable to come into contact with external air or moisture, corrosion is prevented.

## Slide 7: Galvanic protection
Galvanic protection, also known as cathodic protection, protects the underlying steel substrate by corroding preferentially, thus sacrificing itself in the process.
Because zinc is a highly reactive and electronegative metal, it will assume the role of the anode, therefore corroding first in the event that the adjacent steel is unprotected. Zinc will continue to offer galvanic protection until the coating is entirely consumed.

## Slide 8
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.