## Slide 1: PowerPoint 11: Causes and prevention of material failure
PowerPoint presentation
6. Materials and their properties
6.5 Causes of material failure and their prevention

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand the causes of material failure and methods used to prevent this.

## Slide 3: Corrosion
Corrosion is when a refined metal is naturally converted to a more stable form such as its oxide, hydroxide or sulphide state. This leads to deterioration of the material.
Metal corrodes when it reacts with another substance such as oxygen, hydrogen, an electrical current or even dirt and bacteria.
Corrosion can also also occur when metals like steel are placed under too much stress, causing the material to crack.
The most common type of iron corrosion occurs when it is exposed to oxygen and the presence of water, which creates a red iron oxide commonly known as rust.

## Slide 4: Uniform and pitting corrosion
Uniform corrosion is the most common form of corrosion and usually takes place evenly and over large areas of a material’s surface.
One of the most aggressive forms of corrosion, pitting corrosion, can be hard to predict, detect or characterise. This localised type of corrosion happens when a local anodic or cathodic point forms a corrosion cell in the surrounding surface. This pit can create a hole or cavity which typically penetrates the material vertically, down from the surface.
Pitting corrosion can be caused by damage or a break in the oxide film or protective coating, and can also be due to non-uniformities in the structure of the metal.

## Slide 5: Crevice corrosion
Crevice corrosion occurs in areas where oxygen is restricted, such as under washers or bolt heads. This localised corrosion usually results from a difference in the ion concentration between two areas of metal.
The imbalance between the crevice and the rest of the material contributes to a high rate of corrosion.
Crevice corrosion can take place at lower temperatures than pitting corrosion, but can be minimised by proper joint design.

## Slide 6: Galvanic corrosion
Galvanic corrosion occurs when two different metals with physical or electrical contact are immersed in a common electrolyte (such as salt water), or when a metal is exposed to different concentrations of electrolyte.
Where two metals are immersed together, known as a galvanic couple, the more active metal (the anode) corrodes faster than the more noble metal (the cathode).

## Slide 7: Intergranular corrosion and SCC
Intergranular corrosion occurs when impurities are present at the grain boundaries, formed during the solidification of an alloy. Intergranular corrosion can also be caused by the enrichment or depletion of an alloying element at the grain boundaries. This type of corrosion occurs along or adjacent to the grain, affecting the mechanical properties of the metal despite the bulk of the material being unaffected.
Stress corrosion cracking (SCC) refers to the growth of cracks due to a corrosive environment which can lead to the failure of ductile metals when subjected to tensile stress, particularly at high temperatures.

## Slide 8: Chemical corrosion
Chemical corrosion refers to the gradual destruction of a metal’s surface due to the reaction of the surface with substances in its external environment. It is often characterised by the oxidation of a metal with an acid to form oxides.
Notes: The photo shows corrosion on a car battery.

## Slide 9: Stress corrosion
Stress corrosion occurs when a material exists in a relatively inert environment but corrodes due to an applied stress. The stress may be externally applied or residual. This form of corrosion is particularly dangerous because it may not occur under a particular set of conditions until there is an applied stress.

## Slide 10: Erosion corrosion
Erosion corrosion is the combined effect that occurs due to corrosion and erosion and is caused by the rapid flow of any turbulent fluid on a metal surface. Pitting, which is often found on the inner surfaces of pipes, is the main cause of turbulence.
When fluid is flowing through a pipe, the velocity of the fluid and the physical effect of the fluid moving against the surface is combined with the corrosive action of the moving fluid. This in turn causes an accelerated loss of metal.

## Slide 11: Corrosion prevention
Corrosion prevention refers to the measures taken to prevent corrosion.
Prevention measures are designed to protect materials, substrates and metallic structures from the deterioration that results from a substance’s chemical or electrochemical interaction with its immediate surroundings.
Notes: The photo to the left shows sacrificial anodes on the waterjet of a boat. Sacrificial anodes are easily corroded materials which are installed on submerged metal. The anodes corrode, leaving the rest of the system relatively corrosion free. A sacrificial anode is also known as a galvanic anode.

## Slide 12: Methods of corrosion prevention
  Corrosion prevention begins by determining the galvanic effect of the material by studying its position in the galvanic series. Alongside this, an analysis of the surrounding environmental conditions will reveal anything that may accelerate corrosion. From this information, the material can be treated to prevent corrosion, using the following techniques:
  protective coating: isolation of the substrate by application of layers (galvanising, electroplating, powder coating, painting)
  metal alloy: by choosing from from a selection of corrosion resistant materials
  corrosion inhibitors (anticorrosive chemical compounds)
  electrochemical control measures (eg use of a sacrificial anode).

## Slide 13: Deformation
In materials engineering, deformation also refers to material failure as a result of modifications of the shape or size of an object due to applied forces or a change in temperature.
Deformation is usually caused by forces such as:
tensile (pulling)
compressive (pushing)
shear
bending
torsion (twisting).

## Slide 14: Deformation
As deformation occurs, internal intermolecular forces arise that oppose the applied force. If the applied force is not too strong, these forces resist the it and allow the material to resume its original state once the load is removed.
A larger applied force may cause a permanent deformation of the material, or even structural failure.
Different types of deformation may result from variations in type of material, size and the forces applied.

## Slide 15: Types of deformation
Elastic deformation: can be reversible. Elastomers and type memory metals like nitinol exhibit huge elastic deformation ranges, as does rubber.
Plastic deformation: may be irreversible. Soft thermoplastics have a rather large plastic deformation variance, as do ductile metals such as copper, silver and gold.
Metal fatigue: occurs primarily in ductile metals. Metal fatigue has been a common cause of failure, especially before the process was well understood.
Compressive failure: is applied to bars and columns, leading to shortening. Loading a structural object or specimen can increase the compressive stress until it reaches its compressive strength.

## Slide 16: Fracture
Fracture is a cause of failure due to the separation of a material into two or more pieces under the action of an applied stress. A material may undergo one of two major types of fracture depending on its mechanical properties:
  ductile fracture
  brittle fracture.
Materials undergoing ductile fracture first experience plastic deformation, ie, the material resists the fracture by stretching itself. This plastic deformation, which is not limited to polymers, is also seen in metal alloys.
Materials that undergo brittle fracture will fracture with negligible plastic deformation (ie break without warning).

## Slide 17: Fracture
Regardless of the type of fracture, during failure a material will experience:
  crack formation, where all fractures start
  propagation of the crack, in response to the applied stress.
In ductile fractures, this crack is stable, meaning it will undergo continuous deformation, only propagating when more stress is applied. As such, ductile materials will typically deflect by a significant amount before they fail, thus giving warning before they fracture entirely.
On the other hand, when cracks form under brittle fracture, they propagate across the material instantaneously, meaning failure can occur with little or no warning. This is one of the characteristics that makes brittle failure so undesirable, especially in applications such as building construction.

## Slide 18: Brittle fracture
In brittle fracture, no noticeable deformation is observed since crack propagation is instantaneous. This propagation is almost purely perpendicular to the direction of the tensile stress.
While brittle fracture has a distinctive shape, different materials may exhibit unique characteristics. For example, in brittle steel, V-shaped markings are usually found in the centre of the fractured cross section. On the other hand, for amorphous materials like ceramic glass, the surface of the fractured cross section may have a smooth, shiny appearance.

## Slide 19: Necking
Necking is a type of plastic deformation observed in ductile materials subjected to tensile stress. This deformation is characterised by a localised reduction in the cross-sectional area of the material, giving it a V or ‘neck’ shape.
During necking, a large amount of local strain is concentrated in a small region of the material. Therefore, necking is often closely associated with yielding.

## Slide 20: Cup-and-cone formation
One of the main characteristics of ductile fracture is known as a cup-and-cone formation. The stages in cup-and-cone formation are:
  the ductile material undergoes necking
  micro-voids start to form perpendicular to the stress direction
  the micro-voids coalesce to form a crack
  the crack propagates
  the material eventually fractures (a cup and a cone form at the top and bottom respectively).

## Slide 21: Fatigue
In engineering material science, fatigue is the weakening of a material.
It is a cumulative effect causing a material to fail after repeated applications of stress, none of which exceeds the ultimate tensile strength.
The term fatigue is based on the concept that a material becomes ‘tired’ and fails at a stress level below the nominal strength of the material.
Fatigue is caused by cyclic stresses, residual stresses, material properties, internal defects, grain size, temperature, design geometry, surface quality, oxidation and corrosion.

## Slide 22: Stages of fatigue
Fatigue occurs when a material is subjected to repeat loading and unloading. If the loads are above a certain threshold, microscopic cracks begin to form at the stress concentrators such as the surface, persistent slip bands (PSBs) and grain interfaces. Eventually, when a crack reaches a critical size, the crack propagates suddenly, and the structure fractures.
Fatigue failure occurs in three stages:
  crack initiation
  slow, stable crack growth
  rapid fracture.

## Slide 23: Creep
Creep failure is the time-dependent and permanent deformation of a material when subjected to a constant load or stress. This deformation typically occurs at elevated temperatures, although it may occur under ambient temperatures as well. For metals, the creep curve consists of three periods.
    The first is the primary or transient creep region, where the material experiences an increase in creep resistance or strain hardening. At this point, as the material is strained, deformation becomes more difficult.
    The second period is secondary or steady-state creep. Here, the creep rate is constant and usually has the longest duration. This is due to the competing processes between strain hardening and recovery.
    Lastly is tertiary creep, where the creep occurs at an accelerated rate as the material approaches ultimate failure.

## Slide 24: Creep curve

## Slide 25
Any questions?