## Slide 1: PowerPoint 12: Testing methods
PowerPoint presentation
6. Materials and their properties
6.6 Materials testing methods and interpretations of results

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand material testing methods and how these are used.

## Slide 3: Material testing
There are many tests that can be carried out on materials to determine their properties or qualities. The tests can be either destructive or non-destructive.
Destructive tests are often conducted to determine a specific property of the material/component being tested. They usually require a specifically shaped test piece to be made and this is damaged/destroyed during testing. Such tests include:
  tensile tests
  impact tests
  fatigue tests
  hardness tests.

## Slide 4: Visual testing (VT)
Visual testing (VT) is an inspection for flaws that are visible to the naked eye. Visual tests (VTs) are the most commonly used non-destructive testing method across all industries.
VT is used to detect flaws such as deformation, welding defects and corrosion.
The tools used for this type of inspection include steel rules, gauges, cameras and magnifying lenses.

## Slide 5: Destructive tensile testing
Tensile testing is a form of tension testing and is a destructive engineering and materials test. In the test, controlled tension is applied to a sample until it fully fails.
This is one of the most common mechanical testing techniques. It is used to find out how strong a material is and how much it can be stretched before it breaks.

## Slide 6: Tensile test process and outcome
Process
  The test is performed by gripping the ends of a suitably prepared standardised test piece in a tensile test machine, then applying a continually increasing load until such time as failure occurs.
  Test pieces are standardised in order that results are reproducible and comparable.
Outcome
  To provide information that will be used in design calculations or to demonstrate that a material complies with the requirements of the appropriate specification.

## Slide 7: Test properties
Yield strength
The yield strength is the point at which plastic deformation occurs under stress. This is determined during testing over a measured gauge length via the use of devices known as extensometers. The devices may be either mechanical clip-on or video, where non-contact is a limitation (eg elevated temperature testing).
Ultimate tensile strength (UTS)
The UTS is the maximum stress that a specimen is exposed to during testing. This may differ from the specimen’s strength when breaking, depending on whether it is brittle, ductile or has properties of both. These material properties can change depending on environment, for example in extreme hot or cold conditions.

## Slide 8: Test properties
Ductility
Ductility relates to the elongation of a tensile test. The percentage of elongation is calculated by the maximum gauge length divided by the original gauge length.
Strain hardening
How much the material hardens with plastic deformation when it is strained beyond the yield point.
Modulus of elasticity
The modulus of elasticity, also known as Young’s modulus, measures the stiffness of a specimen whereby the material will return to its original condition once the load has been removed.

## Slide 9: Charpy test (toughness test)
The Charpy impact test, also known as the Charpy V-notch test, is a high strain-rate test that involves striking a standard notched specimen with a controlled weight pendulum swung from a set height.
The impact test helps measure the amount of energy absorbed by the specimen during fracture.

## Slide 10: Charpy test
The standard Charpy V-notch specimen is 55mm long, 10mm square and has a 2mm deep notch with a tip radius of 0.25mm machined on one face.
The specimen is supported at its two ends on an anvil and struck on the opposite face to the notch by the pendulum. The amount of energy absorbed in fracturing the test piece is measured and this gives an indication of the notch toughness of the test material.
The pendulum swings through during the test, the height of the swing being a measure of the amount of energy absorbed in fracturing the specimen. Conventionally, three specimens are tested at any one temperature and the results averaged.

## Slide 11: Hardness testing (Brinell test)
The Brinell test was devised by a Swedish researcher at the beginning of the twentieth century.
The test comprises forcing a hardened steel ball ‘indenter’ into the surface of the sample using a standard load.
The diameter/load ratio is selected to provide an impression of an acceptable diameter.

## Slide 12: Hardness testing (Vickers test)
The Vickers hardness test is similar to the Brinell test, the major difference being the use of a square-based pyramidal diamond indenter rather than a hardened steel ball.
Also, unlike the Brinell test, the depth of the impression does not affect the accuracy of the reading.
The diamond does not deform at high loads so the results on very hard materials are more reliable.
The load may range from 1 to 120kgf and is applied for between 10 and 15 seconds.

## Slide 13: Hardness testing (Rockwell test)
The Rockwell test uses a direct reading instrument based on the principle of differential depth measurement.
Rockwell testing differs from Brinell testing in that the Rockwell hardness number is based on an inverse relationship to the measurement of the additional depth to which an indenter is forced by a heavy (major) load beyond the depth resulting from a previously applied (minor) load.
Initially a minor load is applied, and a zero datum position is established. The major load is then applied for a specified period and removed, leaving the minor load applied.
The resulting Rockwell number represents the difference in depth from zero datum position as a result of the application of the major load.

## Slide 14: Fatigue testing (Wohler test)
The determination of the fatigue resistance or fatigue life of the desired metals can be carried out using the Wohler test. Standard test devices apply compressive and tensile stresses on the metal to simulate a fatigue cycle.
The simulation of the fatigue cycle is maintained by the repeated utilisation of the tensile and compressive loads. To obtain a reliable result from the test, test conditions should have similarities to the service conditions of the material that is tested.

## Slide 15: Wohler test

## Slide 16: Corrosion testing
Corrosion testing refers to the processes conducted by laboratories in order to solve, prevent or mitigate problems related to corrosion. These processes can be applied to industrial materials and infrastructure products, and are often used in failure analysis.
Corrosion laboratories can conduct a broad range of laboratory tests that are typically focused on areas such as:
  electrochemical
  corrosivity
  heat transfer
  immersion.

## Slide 17: Corrosion test processes
Immersion testing
Immersion testing is considered the most popular and simplest type of corrosion test. This test is used to assess different materials that are subjected to particular conditions. It is a very versatile process which can be personalised to meet specific needs regardless of application.
In this test, the testing apparatus can expose the specimen to test solutions and then subject it to different physical or metallurgical situations, such as crevices and heat treatment.

## Slide 18: Corrosion test processes
Hot wall test
This test is utilised to evaluate situations where metal vessels are hotter than bulk solutions. These are common in external heated vessels where corrosion is typically impacted by temperature. In this test, elevated temperatures signify high levels of corrosion activity.
Salt spray test
This technique is used to evaluate a coated sample’s resistance to corrosion. This test produces an attack to coated specimens to measure the suitability of the protective coating.

## Slide 19: Taber test (wear resistance testing)
Taber abrasion is a method used to determine the ability of a material to withstand wear.
The material being evaluated is rotated beneath two abrasive wheels for a given time and under a given load.
The Taber abrasion test is performed on coated materials because, if a coating is allowed to wear away, then the base material will be exposed to the environment and lead to premature failure due to corrosion.

## Slide 20: Testing for electrical conductivity
Electrical conductivity is a physical property that indicates how well a given material conducts electricity.
A current originates when electrical charges flow in response to a difference in electrical potential.
The conductivity is defined as the ratio of the density of this current to the strength of the electric field.
Electrical conductivity can be calculated measuring the resistance, area and length of the test material.

## Slide 21: Testing for electrical conductivity
The resistivity of a material is given as p = RA/l where
  p is the resistivity
  R is the resistance
  A is the area
  l is the length.
The conductivity is s = 1/p where s is the conductivity.
The conductivity is therefore s = l/AR and will be measured in ohm-1 metres-1, also known as siemens (S).

## Slide 22
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.