## Slide 1: PowerPoint 13: Analysis, calculations and results
PowerPoint presentation
6. Materials and their properties
6.6 Materials testing methods and interpretations of results

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand how material testing results are interpreted.

## Slide 3: Loading
A material in service or during manufacturing is subjected to different forces. Depending on the magnitude of these forces, the material may or may not change its shape.
The act of applying a force is known as loading. The five forms of loading are:
  compression
  tension
  shear
  torsion
  bending.

## Slide 4: Visualisation of loading forces
1: compression; 2: tension; 3: shear; 4: torsion; 5: bending

## Slide 5: Hooke’s law
Hooke’s law, also referred to as the law of elasticity, was discovered by the English scientist Robert Hooke in 1660.
It states that, for relatively small deformations of an object, the size or displacement of the deformation is directly proportional to the deforming force or load.
Under these conditions the object returns to its original shape and size upon removal of the load.

## Slide 6: Hooke’s law
Hooke’s law can be expressed mathematically as:
            F= -kX
Where:
F is the force applied to the spring (either in the form of strain or stress)
X is the elongation of the spring (a negative value)
k is the spring constant (stiffness).

## Slide 7: Young’s modulus
Young’s modulus is a numerical constant, named for the eighteenth-century English physician and physicist Thomas Young. It describes the elastic properties of a solid undergoing tension or compression in only one direction, as in the case of a metal rod which, after being stretched or compressed lengthwise, returns to its original length.

## Slide 8: Young’s modulus
Young’s modulus is therefore a measure of the ability of a material to withstand changes in length when under lengthwise tension or compression. Young’s modulus is equal to the longitudinal stress divided by the strain. Stress and strain can be described as follows, in the case of a metal bar under tension.
If a metal bar of cross-sectional area A is pulled by a force F at each end, the bar stretches from its original length Lo to a new length Ln. (simultaneously, the cross section decreases.)
The stress is the quotient of the tensile force divided by the cross-sectional area, or F/A. The strain or relative deformation is the change in length, Ln − Lo, divided by the original length, or (Ln − Lo)/Lo.

## Slide 9: Young’s modulus
Young’s modulus = stress/strain =
This is a specific form of Hooke’s law of elasticity.
The units of Young’s modulus in the English system are pounds per square inch (psi), and in the metric system newtons per square metre (N/m2).
The value of Young’s modulus for aluminum is about 1.0 × 107psi, or 7.0 × 1010N/m2. The value for steel is about three times greater, which means that it takes three times as much force to stretch a steel bar the same amount as a similarly shaped aluminum bar.

## Slide 10: Stress
Stress is defined as the ratio of the applied force to the cross-sectional area of the material it is applied to.
σ=F/A
      F = force (N) A= area (m2) σ = stress (N/m2 or Pa)
Stress can be understood as an internal force induced in the metal in response to an externally applied force. It will try to resist any change in dimension caused by the external force.
When the cross-sectional area changes, the same force will induce greater or smaller stresses in the metal. A smaller cross-sectional area will result in a larger stress value and vice versa.

## Slide 11: Strain
Strain is defined as the ratio of the change in dimension to the initial dimension of the metal. It does not have a unit. There are three types of strain: normal, volumetric and shear. Normal strain (or longitudinal strain) concerns itself with the change in only one dimension – length, for example.
The formula for calculating strain is:
ε=(l-lo)/lo
where
  lo = starting or initial length (mm)
  l = stretched length (mm)

## Slide 12: Stress–strain curves
Stress–strain curves are obtained by observing and measuring the deformation in a material when a load is applied gradually to it. For ductile materials, the resulting curve shows three stages.
A linear elastic region where the material undergoes elastic deformation (characterised by a linear graph).
A strain hardening region that occurs when the specimen is subjected to the maximum stress it can sustain (also called the ultimate tensile strength or UTS).
The necking region where the neck forms. At this point, the ability of the material to sustain stress decreases rapidly as it approaches fracture.

## Slide 13: Plotting a stress–strain curve
The most common method for plotting a stress–strain curve is to subject a rod of the test piece to a tensile test.
This is done using a universal testing machine. It has two claws which hold the two extremes of the rod and pull it at a uniform rate.
The force applied and the strain produced is recorded until a fracture occurs. The two parameters are then plotted on an X–Y graph.

## Slide 14: Stress–strain curve: steel

## Slide 15: Interpreting the steel stress–strain curve
The material exhibits elastic behaviour up to the yield strength point, after which the material loses elasticity and exhibits plasticity. From the origin until the proportional limit nearing yield strength, the straight line on the graph implies that the material follows Hooke’s law.
Beyond the elastic limit between proportional limit and yield strength, the material loses its elasticity and exhibits plasticity. The area under the curve from origin to the proportional limit falls under the elastic range. The area under the curve from the proportional limit to the rupture/fracture point falls under the plastic range.
The material’s ultimate strength is defined based on the maximum ordinate value given by the stress–strain curve (from origin to rupture). The value provides the rupture with strength at the point of rupture.

## Slide 16: Stress–strain curve example

## Slide 17: Interpreting stress–strain curve colours
Green = a brittle material: this material is also strong because there is little strain for a high stress. The fracture of a brittle material is sudden with little or no plastic deformation.
Black = a strong material which is not ductile: steel wires stretch very little, and break suddenly.
Orange = a ductile material: after the elastic region there is a section where necking occurs; permanent deformation occurs in this plastic region.
Purple = a plastic material: very small elastic region.

## Slide 18
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.