## Slide 1: PowerPoint 1: Physical properties
PowerPoint presentation
6. Materials and their properties
6.1 Physical and mechanical properties of materials

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
explain different physical properties of materials.

## Slide 3: Physical properties
All materials have physical and mechanical properties.
Physical properties are things that are measurable. For example:
Density
Melting point
Conductivity
Coefficient of expansion.

## Slide 4: Conductivity
Thermal conductivity is a measure of the quantity of heat that flows through a material. It is measured as 1 degree per unit of time, per unit of cross-sectioned area, per unit of length.
Materials with low thermal conductivity may be used as insulators, those with high thermal conductivity may used as a heat sink. Metals that exhibit high thermal conductivity are candidates for use in applications such as heat exchangers or refrigeration.
Low thermal conductivity materials are used in high temperature applications, but often high temperature components require high thermal conductivity, so it is important to understand the environment. Electrical conductivity is similar, measuring the quantity of electricity that is transferred through a material of known cross section and length.

## Slide 5: Corrosion resistance
Corrosion resistance describes a material’s ability to prevent natural chemical or electrochemical attack by atmosphere, moisture or other agents. Corrosion takes many forms, including pitting, galvanic reaction, stress corrosion, parting, intergranular corrosion and others.
Corrosion resistance may be expressed as the maximum depth in millimetres to which corrosion would penetrate in one year. It is based on a linear extrapolation of penetration occurring during the lifetime of a given test or service.

## Slide 6: Corrosion resistance
Some materials are intrinsically corrosion resistant, while others benefit from the addition of plating or coating.
Many metals that belong to families that resist corrosion are not totally safe from it, and are still subject to the specific environmental conditions where they operate.
Metal components are powder coated to enhance corrosion resistance.

## Slide 7: Density
Density, often expressed as pounds per cubic inch, or grams per cubic centimetre, describes the mass of the material per unit volume.
The density will determine how much a component of a certain size will weigh. This factor is important in applications like aerospace or automotive, where weight is important.
Engineers looking for lower weight components may seek materials that are less dense, but must then consider the strength to weight ratio.
A higher density material like steel might be chosen, for example, if it provides higher strength than a lower density material. Such a part could be made thinner so that less material helps to compensate for the higher density.

## Slide 8: Calculating density: formula
The density calculation formula for solids, liquids and gas molecules is the measurement of mass per unit volume at a given temperature and pressure.
In chemistry or physics, density is expressed by the symbol ρ or D.
Mathematically, density is expressed by the formula:
where
m = mass of the substance
V = volume

## Slide 9: Calculating density: the density triangle
We can also use the density triangle to calculate the other variables. In the triangle, density is represented by d.

## Slide 10: Calculating density: example
An object has a mass of 570g and a volume of 2,280cm3
Using the formula:
​
we can calculate: Density = = 0.25g/cm3

## Slide 11: Calculating density: finding a volume
To find a volume from given values, calculate as follows.
A liquid has a density of 1,000kg/m3 and mass of 0.5kg.
To calculate the volume of the liquid (answer in litres):
Volume = = = 0.0005m3
To convert to litres we need to multiply by 1,000:
= 0.0005 x 1,000 = 0.5 litres

## Slide 12: Melting point
In general, ‘melting’ is a phase change of a substance from the solid to the liquid phase.
The melting point of a substance is the temperature at which this phase change occurs. The melting point also defines a condition in which the solid and liquid can exist in equilibrium.
Notes: shutterstock_1964543551

## Slide 13: Melting point
Adding heat will convert the solid into a liquid with no temperature change.
At the melting point, the two phases of a substance, liquid and vapour, have identical free energies and therefore are equally likely to exist.
Below the melting point, the solid is the more stable state of the two, whereas above the melting point the liquid form is preferred. The melting point of a substance depends on pressure and is usually specified at standard pressure.

## Slide 14: Specific heat capacity
Specific heat capacity is the amount of heat energy required to raise the temperature of a substance per unit of mass.
It is also an example of an extensive property since its value is proportional to the size of the system being examined.
It is defined as the ratio of the amount of energy transferred to a material and the change in temperature that is produced:
C = Q / ΔT
where C is heat capacity, Q is energy, usually expressed in joules (J), and ΔT is the change in temperature, usually expressed in degrees Celsius (C) or kelvins (K).

## Slide 15: Hardenability
Hardenability is the ability of a steel to partially or completely transform from austenite (a solid solution of carbon stable at high temperatures) to some fraction of martensite (a hard, brittle solid solution of carbon in iron, the main constituent of hardened steel), at a given depth below the surface, when cooled under a given condition.
For example, a steel of a high hardenability can transform to a high fraction of martensite to depths of several millimetres under relatively slow cooling, such as an oil quench, whereas a steel of low hardenability may only form a high fraction of martensite to a depth of less than a millimetre, even under rapid cooling such as a water quench.
Hardenability therefore describes the capacity of the steel to harden in depth under a given set of conditions.

## Slide 16: Weldability
Weldability is the ability of any material (usually metals and their alloys) to weld with similar materials.
Many metals and thermoplastics can be welded together to fabricate a final material that is required in the fabrication process or any other industrial process.
Weldability is also known as joinability.
Notes: shutterstock_1813353151

## Slide 17: Permittivity
Permittivity defines the ability of a material to store electrical potential energy under the influence of an electric field.
It is measured by the ratio of the capacitance of a capacitor with the material as a dielectric (an electrical insulator that can be polarised by an applied electrical field) to its capacitance with a vacuum as dielectric.
Permittivity can also be referred to as the dielectric constant.

## Slide 18: Recyclability
This refers to the ability of a material to be recycled into a similar or other form.
Recyclability, also known as capability of being reusable at the end of a product’s useful life, helps to minimise waste, pollution and resource usage.

## Slide 19: Thermal expansion
Thermal expansion refers to a fractional change in the size of a material in response to a change in temperature.
This includes:
changes in length compared to original length (∆ℓ/ℓ0), called linear expansion
changes in area compared to original area (∆A/A0), called areal expansion or superficial expansion
changes in volume compared to original volume (∆V/V0), called volumetric expansion or cubical expansion.

## Slide 20: Thermal expansion of a solid

## Slide 21: Permeability
In electromagnetism, permeability is the measure of magnetisation that a material obtains in response to an applied magnetic field.
Permeability is typically represented by the (italicised) Greek letter μ.
In SI units, permeability is measured in henries per metre (H/m), or equivalently in newtons per ampere squared (N/A2).
The permeability constant μ0, also known as the magnetic constant or the permeability of free space, is the proportionality between magnetic induction and magnetising force when forming a magnetic field in a classical vacuum.

## Slide 22
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.