## Slide 1: PowerPoint 2: Mechanical properties
PowerPoint presentation
6. Materials and their properties
6.1 Physical and mechanical properties of materials

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
explain different mechanical properties of materials.

## Slide 3: Mechanical properties
All materials have mechanical and physical properties and there is a difference between the two.
As you have already learned, physical properties are things that are measurable.
Mechanical properties relate to how a material performs when different forces are applied to it. Such properties include strength, ductility and wear resistance.

## Slide 4: Fatigue strength
Fatigue can lead to fracture under repeated or fluctuating stresses (eg loading or unloading) that have a maximum value less than the tensile strength of the material.
Fatigue strength, then, refers to the maximum stress the material can withstand (the variable) in a given number of cycles.
Fatigue strength is an important consideration when designing components that will be subjected to repetitive load conditions.

## Slide 5: Shear strength
Shear strength is a consideration in applications like bolts or beams where the direction as well as the magnitude of the stress is important.
Shear occurs when directional forces cause the internal structure of the material to slide against itself, at the granular level.
Notes: Shutterstock_1930515758

## Slide 6: Tensile strength
Tensile strength refers to the amount of load a section of a material can withstand before it breaks.
At the tensile point, the load causes the material to fracture.
Tensile or ultimate tensile strength is measured in newtons (N) per square millimetre (megapascals or MPa), or pounds per square inch.
Testing the tensile strength of materials.

## Slide 7: Yield strength
Similar in concept and measure to tensile strength, yield strength describes the point (yield point) after which a material under load will no longer return to its original position or shape.
This deformation moves from elastic to plastic.
Design calculations include the yield point to establish the limits of a material’s dimensional integrity under load.
Yield strength is measured in newtons (N) per square millimetre (megapascals or MPa), or pounds per square inch.

## Slide 8: Toughness
Measured using the Charpy impact test and similar to impact resistance, toughness represents a material’s ability to absorb impact without fracturing at a given temperature.
Since impact resistance is often lower at low temperatures, materials may become more brittle.
Charpy values are commonly prescribed in ferrous alloys where the possibilities of low temperatures exist in the application (eg offshore oil platforms, oil pipelines etc) or where instantaneous loading is a consideration (eg ballistic containment in military or aircraft applications).
Notes: shutterstock_451549891

## Slide 9: Hardness
Hardness is defined as a material’s ability to resist permanent indentation (ie plastic deformation).
Typically, the harder the material, the better it resists wear or deformation.
The term hardness also refers to the local surface stiffness of a material or its resistance to scratching, abrasion or cutting.
Hardness is measured by employing such methods as the Brinell, Rockwell and Vickers tests, which measure the depth and area of a depression made by a harder material.
Notes: shutterstock_1879072513

## Slide 10: Ductility
Ductility is the ability of a material to deform (that is, stretch) without fracturing, and retain the new shape when the load is removed. Think of it as the ability to stretch a given metal into a wire.
Ductility is often measured using a tensile test as a percentage of elongation, or the reduction in the cross-sectional area of the sample before failure.
A tensile test can also be used to determine the Young’s modulus of elasticity, an important stress/strain ratio used in many design calculations.

## Slide 11: Malleability
Malleability, a physical property, describes a material’s ability to be formed without breaking.
Pressure, or compressive stress, is used to press or roll the material into thinner sheets.
A material with high malleability will be able to withstand higher pressure without breaking.
Aluminum is a malleable material.

## Slide 12: Elasticity
Elasticity describes a material’s tendency to return to its original size and shape when a distorting force is removed.
As opposed to materials that exhibit plasticity (where the change in shape is not reversible), an elastic material will return to its previous configuration when the stress is removed.
The stiffness of a material is often measured by Young’s modulus, which compares the relationship between stress (the force applied) and strain (the resulting deformation).

## Slide 13: Plasticity
Plasticity, the converse of elasticity, describes the tendency of a solid material to hold its new shape when subjected to forming forces. It is the quality that allows materials to be bent or worked into a permanent new shape.
Materials transition from elastic behaviour to plastic behaviour at the yield point.

## Slide 14: Brittleness
Brittleness is a mechanical property of a material manifested by failure without undergoing any deformation on application of stress.
Materials with this property have elastic proportionality in stress and strain. Examples of brittle materials are ceramics, glass and cold metals.
Brittleness in metals helps in determining the critical cooling temperature that transforms a ductile material into a brittle material.

## Slide 15
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.