## Slide 1: PowerPoint 3: Ferrous metals
PowerPoint presentation
6. Materials and their properties
6.2 Types of material and their structures

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand the structure and classification of ferrous metals.

## Slide 3: The three groups of metals
When metals occur naturally they are called ‘ore’ and in industry are normally mixed with other metal ores (alloying) to give the desired properties and qualities. Metals are divided into three groups.
Ferrous
Non-ferrous
Alloys
Metals must be extracted from their ore before they can be used. This is done by mining the ore and removing rocks and other compounds. The ore then goes through a process of reduction, which removes oxygen by heating and changes the chemical bonding.

## Slide 4: Ferrous metals
The term ferrous relates to any material that contains iron in its composition.
The main ores of iron (Fe) are oxides and carbonates, and these ores are typically melted in blast furnaces.
Commonly used terms in iron and steel making include pig, cast, acid, basic, wrought and ingot or Swedish iron, along with steel.
Notes: The photo shows untreated iron ore.

## Slide 5: The blast furnace

## Slide 6: Types of iron
Pig iron is the impure product of the blast furnace when cast into small ingots or ‘pigs’.
Cast iron is selected grades of pig iron re-melted in a cupola and cast into shapes using sand moulds.
Acid iron is a pig iron of low phosphorous content, which may be refined to steel by an acid process.
Basic iron is a pig iron containing up to 2% of phosphorous, and this may only be refined into steel using a basic process.

## Slide 7: Types of iron
Wrought iron is a refined iron containing a certain amount of slag.
Ingot iron is the purest commercial form of iron, and is made by giving iron from the blast furnace the maximum possible refining in a steel-making furnace.
Steel is essentially an alloy of iron and carbon, containing between 1 and 5% carbon. Steel is made by oxidising away the impurities which are present in the iron produced in the blast furnace.

## Slide 8: Forms of supply
Metals can be supplied in many forms depending on the application and use of the material.
Square bar Round bar
Powdered steel Slotted beam
Sheet steel Steel plate
Round billet I-beam
C-beam Hollow round
Hollow square

## Slide 9: Carbon content
When we refer to steel there is often a reference to the carbon content of the material such as:
mild steel which contains up to 0.3% carbon
medium carbon steel which contains between 0.3% and 0.6% carbon
high carbon steels or tool steels which contain more than 0.6% carbon; these steels are always used in the hardened and tempered condition.
The varied levels of carbon affect the properties of the metal. Technically, these are ‘alloys’ of iron and carbon.

## Slide 10: Impurities
Carbon steels may also contain other substances in addition to the Iron and carbon which are typically either sulphur or phosphorus. These are regarded as impurities.
These impurities have an impact on the material properties and can weaken the steel if their effect is not countered. This is often done with the addition of manganese as a counter-solution.

## Slide 11: Properties of iron and steel
Type | Alloy composition | Properties
Mild steel | Carbon 0.1–0.3% Iron 99.7–99.9% | Tough, high tensile strength, can be hardened, rusts easily
Carbon steel | Carbon 0.6–1.4% Iron 98.6–99.4% | Tough, can be hardened and tempered
Stainless steel | Iron, nickel and chromium (% differs by grade) | Tough, resistant to rust, subject to stains
Cast iron | Carbon 2–6% Iron 94–98% | Strong but brittle, high compressive strength
Wrought iron | 100% Iron | Fibrous, tough, ductile, resistant to rusting

## Slide 12
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.