## Slide 1: PowerPoint 4 : Non-ferrous metals
PowerPoint presentation
6. Materials and their properties
6.2 Types of material and their structures

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand the structure and classification of non-ferrous metals.

## Slide 3: Non-ferrous metals
The term ‘non-ferrous metals’ relates to materials which are alloys or metals that do not contain any appreciable amounts of iron.
All pure metals are non-ferrous elements, except for iron.

## Slide 4: Aluminium
malleable
corrosion resistant
a conductor of heat and electricity.
In its purest form, aluminium has low tensile strength in comparison to steel, but when alloyed with copper, silicon, iron or manganese this property can be greatly improved.
Aluminium is widely used in the aerospace and automotive sectors due to its low weight and high corrosion resistance.
Aluminium is probably one of the most widely used non-ferrous materials and is also one of the lightest. It is:

## Slide 5: Copper
Copper is widely used in applications such as household pipes, electrical wiring and cooking utensils. It is:
malleable
corrosion resistant
a conductor of heat and electricity.
Copper does not have the same strength as steel but has a reasonable level of tensile strength which again can be improved by alloying with tin to form bronze or with zinc to form brass.

## Slide 6: Zinc
Zinc is an element which is typically soft but also brittle. Similar to other non-ferrous metals it has a high level of corrosion resistance and is often used as a protective coating for mild steel components (galvanising). It is:
ductile
conductive.
Zinc’s conductivity is moderate for a metal. Its strong electrochemical properties, however, serve well in alkaline batteries and during the galvanising process.

## Slide 7: Brass
Brass and bronze are both metal alloys, which means they are a combination of two or more different metals. Brass is composed of copper and zinc.
Brass has a higher malleability than zinc or copper.
It has a low melting point (900 degrees centigrade).
It flows when melted.
Combinations of iron, aluminium, silicon and manganese make brass corrosion resistant.

## Slide 8: Bronze
Bronze is made up of copper and tin. Bronze:
is hard and brittle
melts at 950 degrees centigrade depending on the amount of tin present
resists corrosion (especially seawater corrosion) and metal fatigue more than steel
is a better conductor of heat and electricity than most steels.

## Slide 9: Other alloys
Phosphor bronze is an 8% tin bronze which contains about 0.3% phosphorus. This alloy has high tensile strength, hardness and resistance to wear and corrosion by seawater.
Gunmetal is a tin/bronze/zinc alloy, and has excellent resistance to corrosion and moderately high strength.
The tensile strength, ductility and hardness of copper-nickel alloy increase with nickel content. Cupro-nickels are suitable for both hot and cold working. British ‘silver’ coins contain 75% copper and 25% nickel.

## Slide 10: Nickel silvers and silver bronzes
Nickel silvers and silver bronzes are neither silvers nor true bronzes, but contain elements of copper, nickel and zinc.
Nickel silvers are hard and ductile but only the purer alloys can be hot worked.
Silver bronzes have a higher zinc content and are suitable for hot working.

## Slide 11: Copper-silicon and copper-aluminium alloys
Silicon ‘bronze’ alloys have good corrosion resistance, particularly in sulphurous atmospheres and are used as access fittings for chimneys.
Copper-aluminium alloys (‘bronzes’) are bright golden-yellow in colour, very strong and resistant to corrosion. They can be annealed to make them soft and ductile.
Delta bronze is an example of a wrought alloy. It contains about 1% aluminium, iron, nickel and manganese.

## Slide 12: Properties chart
Name | Colour | Alloy composition | Properties
Aluminium | Light grey | Aluminium 95% Copper 4% Manganese 1% | Ductile Malleable Light
Copper | Reddish brown | Not an alloy | Ductile Malleable Conductive
Brass | Yellow | Copper 65% Zinc 35% | Hard Conductive
Silver | Whitish grey | Not an alloy | Ductile Malleable Corrosion resistance
Lead | Bluish grey | Not an alloy | Ductile

## Slide 13
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.