## Slide 1: PowerPoint 5: Plastics, polymers and composites
PowerPoint presentation
6. Materials and their properties
6.2 Types of material and their structures

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand the definition of thermoplastics, thermosets, elastomers and composites
be able to give examples of each.

## Slide 3: Thermoplastics vs thermosets
These two types of material sound similar but have different mechanical and physical properties.
Thermosets and thermoplastics are both polymers, but they behave differently when exposed to heat.
Thermoplastics can melt under heat after curing while thermosets retain their form and stay solid under heat once cured.

## Slide 4: Polymer structure

## Slide 5: Thermoplastics
A thermoplastic is a resin that is solid at room temperature but becomes plastic and soft upon heating, flowing due to crystal melting or by virtue of crossing the glass transition temperature (Tg).
Upon processing, usually via injection-moulding or blow-moulding, thermoplastics take the shape of the mould within which they are poured as they melt, and cool to solidify into the desired shape.

## Slide 6: Examples of thermoplastics
One significant aspect of thermoplastics is their reversibility – the ability to undergo reheating, melt again, and change shape. This allows for additional processing of the same material, even after being prepared as a solid.
Processes such as extrusion, thermoforming and injection moulding rely on such resin behaviour.
Some common thermoplastic materials include:
polyethylene (PE)
polycarbonate (PC)
polyvinyl chloride (PVC).

## Slide 7: Thermosets
These are generally harder and more rigid than thermoplastics and cannot be softened by reheating.
During the initial process a chemical change occurs when heat and pressure are applied as the polymers become crosslinked together. Once formed these cannot be broken.

## Slide 8: Thermoset examples
Polyester resin fiberglass systems, sheet moulding compounds and bulk moulding compounds, filament winding, wet lay-up lamination, repair compounds and protective coatings.
Polyurethanes: insulating foams, mattresses, coatings, adhesives, car parts, print rollers, shoe soles, flooring, synthetic fibres.
Polyurea/polyurethane hybrids used for abrasion-resistant waterproof coatings.
Bakelite, a phenol-formaldehyde resin used in electrical insulators and plasticware.

## Slide 9: More thermoset examples
Urea-formaldehyde foam, used in plywood, particleboard and medium-density fibreboard (MDF).
Melamine resin used on worktop surfaces.
Diallyl-phthalate (DAP), used in high temperature electrical connectors and other components. Usually glass filled.
Epoxy resin, used as the matrix component in many fibre-reinforced plastics such as glass-reinforced plastic and graphite-reinforced plastic.
Silicone resins used for thermoset polymer matrix composites and as a ceramic matrix composite precursor.

## Slide 10: Thermoplastics vs thermosets
Feature | Thermoplastics | Thermosets
Molecular structure | Linear polymer: weak molecular bonds in a straight-chain formation | Network polymer: high level of crosslinking with strong chemical molecular bonds
Melting point | Melting point lower than the degradation temperature | Melting point higher than the degradation temperature
Mechanical | Flexible and elastic. High resistance to impact (10x more than thermosets). Strength comes from crystallinity | Inelastic and brittle. Strong and rigid. Strength comes from crosslinking

## Slide 11: Thermoplastics vs thermosets
Feature | Thermoplastics | Thermosets
Polymerisation | Addition polymerisation: repolymerised during manufacture (before processing) | Polycondensation polymerisation: polymerised during processing
Microstructure | Comprised of hard crystalline and elastic amorphous regions in solid state | Comprised of thermosetting resin and reinforcing fibre in solid state
Recyclability | Recyclable and reusable by the application of heat and/or pressure | Non-recyclable
Solubility | Can dissolve in organic solvents | Cannot dissolve in organic solvents

## Slide 12: Elastomers
Elastomers have loosely crosslinked polymers. Examples are materials such as rubber and neoprene.
Elastomers have the characteristics of rubber in terms of flexibility and elasticity.
The long, randomly coiled, loosely crosslinked materials can be stretched easily, but return to their original shape when the force or stress is removed.
Notes: The picture shows the material neoprene.

## Slide 13: Composites
Composites, also known as fibre-reinforced polymers (FRPs), are made from a polymer matrix that is reinforced with an engineered, man-made or natural fibre or other reinforcing material.
The matrix protects the fibres from environmental and external damage. The fibres, in turn, provide strength and stiffness to reinforce the matrix and help it resist cracks and fractures.

## Slide 14: Composites
By combining specific resins and reinforcements to set formulae, a composite can be designed to meet the specific strength requirements of an application.
For example, you can alter the ratio of the resin and reinforcement, or orient the fibres in one direction or various directions.
Composites are anisotropic, meaning the material properties change depending on the placement and number of layers of reinforcement material – the fibres. This provides engineering flexibility and designers can tailor the properties of the final product. When it comes to strength, tensile, shear and compressive strength all have an effect on use and design.

## Slide 15: Composite properties
Tensile strength
Tensile strength refers to the amount of stress a material can handle before it breaks, cracks, becomes deformed or otherwise fails. One measure of tensile strength is flexural strength – a material or structure’s ability to withstand bending.
Tensile strength varies by material and is measured in megapascals (MPa). For example, the ultimate tensile strength of steel ranges from 400 to 690MPa, while the ultimate strength of carbon fibre reinforced polymer composites ranges from 1,200 to 2,410MPa, depending on fibre orientation and other design factors.

## Slide 16: Composite properties
Shear strength
Shear strength describes how well a material can resist strain when layers shift or slide. It’s important to know the maximum amount of shear stress (or force per unit area) a material can handle prior to failure.
Shear strength in composites varies based on the formulation and design. Composites can be designed so that shear stresses are oriented within a plane, transverse to the plane or throughout the layers (interlaminar). There are several ways to control shear properties, including fibre orientation, the sequencing of layers, the type and volume of fibres used, the type and density of core materials, and more.

## Slide 17: Composite properties
Compressive strength
Compressive strength indicates how a material performs when it is compressed or flattened by pressure. Some materials fracture or break when they hit their compressive strength limit, while others deform permanently.
Composites typically have higher tensile strengths than compressive strengths. Composites loaded in compression may buckle, kink or crush.

## Slide 18: Examples of composites
MDF, which is manufactured from different wood fibres compressed together.
Plywood, which consists of thin layers of wood bonded together with their grain directions set at right angles to one another.
Glass reinforced plastic (GRP), which consists of either an epoxy or polyester resin reinforced with glass fibre matting.
Carbon fibre reinforced plastic (CRP), which consists of either an epoxy or polyester resin reinforced with carbon fibres.
Notes: The picture shows the material MDF.

## Slide 19
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.