## Slide 1: PowerPoint 6: Ceramic, natural and smart materials
PowerPoint presentation
6. Materials and their properties
6.2 Types of material and their structures

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
discuss the form and role of ceramics, natural materials and smart materials in engineering.

## Slide 3: Ceramics
Ceramic products can be categorised as whiteware, refractory or engineering products.
Whiteware (eg dinner plates) is familiar to the vast majority of us. Refractory products are used in applications such as furnace linings and crucibles. Engineering ceramics are used in ‘high-tech’ applications such as aerospace, electronics and biomedical. Ceramics are good electrical insulators.

## Slide 4: Engineering ceramics
All ceramics are made from the same basic ingredients, ie carbon, nitrogen, oxygen or boron in combination with a metal (eg aluminum or silicon). In nature, these materials are found in abundance, but they usually contain impurities.
Engineering ceramics – also referred to as advanced, structural or fine ceramics – have been processed to be very pure and, in general, have superior properties to unrefined ceramics.
Notes: Images show ceramic bearings and a ceramic insulator in a high voltage electrical connector.

## Slide 5: Ceramics: types and uses
Ceramic materials
Glasses
Clay products
Refractories
Abrasives
Cements
Advanced
Optical
Whiteware
Composite
Structural
Bricks
Sandpaper
Cutting
Polishing
Composites
Structural
Engine rotors
Bearings
Sensors

## Slide 6: Wood
Wood, a natural material, can be classified into one of three categories: softwoods, hardwoods and engineered woods.
Softwoods
Softwoods are the wood and lumber which are milled from conifer trees. Scientifically known as gymnosperms, conifer trees are any trees that have needles and produce cones. Examples of popular softwood trees used in woodworking, construction and furniture are pine, cedar, fir, spruce and redwood.

## Slide 7: Wood
Hardwoods
Hardwoods come from any trees which do not produce needles or cones. These trees are most commonly known as deciduous trees, scientifically known as angiosperms. Hardwoods are trees that produce leaves and seeds.

## Slide 8: Wood
Engineered woods
The third type of wood you may encounter are engineered woods. Engineered woods do not occur naturally in the environment but instead are manufactured from other wooden material.
Engineered woods are boards made from wood which is manipulated to have certain qualities or features. Also known as composite woods, these products are often made from the waste wood of sawmills.

## Slide 9: Smart materials
Smart materials are materials that are manipulated to respond in a controllable and reversible way, modifying some of their properties as a result of external stimuli such as a certain mechanical stress or a certain temperature, among others.
Because of their responsiveness, smart materials are also known as responsive materials.
Notes: Image shows smart textile material.

## Slide 10: Smart materials
Shape memory alloy (SMA)
This material is an alloy containing a combination of copper, zinc, nickel, aluminium and titanium. SMAs which have been deformed as a result of heat or external forces return to their original or permanent shape when reheated.
Quantum tunnelling composite (QTC)
This is a material that acts as an insulator in its normal state but under compression it becomes an electrical conductor.

## Slide 11: Smart materials
Piezoelectric crystals
With certain crystals such as quartz, when a force or pressure is applied this causes a voltage to be set up across the faces at right angles. This can be used in reverse with an applied voltage, causing stress in the material which in turn causes it to twist or bend in a controlled manner.

## Slide 12
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.