## Slide 1: PowerPoint 9: Heat treatments
PowerPoint presentation
6. Materials and their properties
6.4 Heat treatments and surface treatments

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand how heat treatment processes affect the structure and properties of materials.

## Slide 3: Metal hardening
The use of metal hardening will result in an improvement of the mechanical properties, as well as an increase in the level of hardness of a material, producing a tougher, more durable item.
Alloys are heated above the critical transformation temperature for the material, then cooled rapidly enough to cause the soft initial material to transform to a much harder, stronger structure.
Hardened materials are usually tempered or stress relieved to improve their dimensional stability and toughness.

## Slide 4: Case hardening
Case hardening is a simple method of hardening steel involving the use of a metal that has low carbon content, and combining it with a metal that has a higher carbon content.
The combination of metals produces a product that is much harder. The addition of the low-carbon metal creates a material that can be moulded easily into desired shapes.
The surface improvement not only increases the product strength, but also assists in avoiding weakening of the iron.
Case hardening is usually performed after the formation of the component into its final form. Components that will be subjected to severe impacts and high pressures are generally case hardened.

## Slide 5: Precipitation hardening
Precipitation hardening is a heat treatment technique that takes place at low temperatures and makes use of alloying materials, such as aluminum and titanium.
This causes increased yield strength as well as improved corrosion resistance, depending on the alloying metals.
This process takes place in three stages:
solution annealing
quenching
ageing.

## Slide 6: Solution annealing
The first step of precipitation hardening is called solution annealing. Its goal is to precipitate (or withdraw) metastable phases of alloys. In this process, inhomogeneities are transformed into homogeneities.
The metal is treated with a solution at high temperatures, slightly below the eutectic point of the material. Too low and the solution annealing is ineffective; too high and metals reach their melting point.

## Slide 7: Quenching
Once the alloying materials are dissolved into the surface of the part, rapid cooling takes place until the solubility limit is exceeded. This prevents alloys from discharging.
The solid solution after quenching is metastable, oversaturated and single-phased.
Typical quenching agents in precipitation hardening are water, oil and gas.

## Slide 8: Quenching
The material is heated to the suitable temperature for hardening, then cooled rapidly by immersing the hot part in water, oil or another suitable liquid to transform the material to a fully hardened structure.
Quenched parts must usually be aged, tempered or stress relieved to achieve the proper toughness, final hardness and dimensional stability.

## Slide 9: Ageing
Ageing is the last and most time consuming step of precipitation hardening.
The solution is heated to an intermediate temperature. At temperatures between 150 and 190 degrees centigrade (400–500 for stainless steels), the part is held in a constant heat.
The exact ageing temperature depends on the composition of the material. The oversaturated solid solution transforms into two-phase alloys.

## Slide 10: Tempering
Tempering develops the required combination of hardness, strength and toughness or relieves the brittleness of fully hardened steels. The treatment follows a quenching or air cooling operation. Tempering is generally considered effective in relieving stresses induced by quenching in addition to lowering hardness to within a specified range, or meeting certain mechanical property requirements.
Tempering is the process of reheating the steel at a relatively low temperature, leading to precipitation and spheroidisation of the carbides present in the microstructure.
The result is a component with the appropriate combination of hardness, strength and toughness for the intended application. Tempering is also effective in relieving the stresses induced by quenching.

## Slide 11: Annealing
The primary purpose of annealing is to alter the metal’s mechanical properties, making it softer and more workable, because annealing reduces the risk of material fracture, cracking and distortion.
Hard, brittle metals are also more likely to cause excessive wear or damage to tools and machinery, and annealing reduces this impact.
Annealing is often used after cold working processes such as drawing, grinding, roll forming or bending to allow the metal to be worked further.
It is also commonly used to remove stresses that appear after welding. In some circumstances, annealing can be used to improve the electrical properties of a metal by making it more conductive.

## Slide 12
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.