## Slide 1: PowerPoint 1: Newton’s laws of motion
PowerPoint presentation
7. Mechanical principles
7.1 Principles of motion and mechanics in engineering and manufacturing systems

## Slide 2: Objectives
By the end of this session, learners should be able to describe Isaac Newton’s three laws of motion:
law of inertia (Newton’s first law)
law of mass and acceleration (equation of motion) (Newton’s second law)
law of action and reaction (Newton’s third law).

## Slide 3: Newton’s first law: inertia
Newton’s first law of motion states that an object will not change its speed or direction unless an unbalanced force (a force which is distant from the reference point) affects it.
Another name for the first law of motion is the law of inertia. If balanced forces act on an object, it doesn’t accelerate or change direction. This means it doesn’t change its velocity or momentum.
Objects continue in their state of rest, or move with uniform velocity, as long as no net force acts. For rotating objects, the moment of inertia (I) is related to the mass (m) and the distance from the axis of rotation (r):
I = mr²

## Slide 4: Examples of Newton’s first law
If you kick a football on a football field, eventually it will stop, because of friction between the ball and the grass. It will also stop if it hits something, like a player’s foot or a goalpost.
If you are driving in your car at speed and hit a brick wall, the car will come to an instant stop, but you (and anything else in the vehicle) will keep moving forward. This is why cars have seatbelts and airbags, to protect you from smashing into the steering wheel or windscreen.
If you kicked a ball in space, it would keep going forever, because there is no gravity, friction or air resistance acting on it. It will only stop moving in one direction if it hits something or reaches the gravitational field of another planet.

## Slide 5: Newton’s second law: mass and acceleration
The second law of motion states that acceleration is produced when an unbalanced force acts on an object (mass: m). The more mass the object has, the more net force has to be used to move it.
As a result, we can state that
force = mass × acceleration
F = ma
where F is the resultant of all the forces (or net force) acting on the object.
The acceleration of an object is proportional to the size of the resultant applied force and takes place in the direction of that force.

## Slide 6: Examples of Newton’s second law
If you use the same force to push a lorry and push a car, the car will have a greater acceleration than the lorry, because the car has a lower mass.
It is easier to push an empty shopping trolley than a full one, because the full shopping trolley has a greater mass than the empty one. This means that more force is required to push the full shopping trolley.
This is Newton’s cradle. If you lift one ball and let go, the force will only push one ball on the other side of the cradle.

## Slide 7: Calculating force
F = ma
Force is measured in newtons (N). A newton is defined as the force required to give a mass of 1kg an acceleration of 1m/s², where m/s stands for metres per second.
The mass of an object refers to the amount of matter that is contained in the object. The weight of an object is the force of gravity acting on that object:
W = mg
where the acceleration due to gravity, g, is approximately 9.81m/s².

## Slide 8: Calculating force: examples
Remember: force = mass × acceleration or F = ma
Calculate the force acting on an object of mass 2kg accelerating at 5m/s2
F = 2(kg)×5(m/s2)
F = 10N
Calculate the acceleration if F = 10N and m = 30kg
10(N) = 30(kg)×a
a =
a = 0.333m/s2 (to 3sf)

## Slide 9: Your turn
If F = 20N, and a = 5m/s2 what is the mass (m) in kg?
Hint:
m =
Notes: The answer is 4kg.

## Slide 10
The third law of motion states that for every action force there is an equal and opposite reaction that produces the same change in momentum in the opposite direction.
Newton’s third law: motion
What is happening to the balloon?

## Slide 11: Examples of Newton’s third law
When air rushes out of a balloon, the opposite reaction causes the balloon to fly up and around until all the air is displaced.
Similarly, when you jump off a small rowing boat into water, you will push yourself forward towards the water. The same size force you used to push yourself forward will make the boat move backwards.
When you dive off a diving board, you push down on the board. The board springs back and forces you into the air.

## Slide 12: Reaction forces
A reaction force is a force that acts in the opposite direction to an applied action force. Imagine you are skateboarding.
Action–reaction force properties | Examples
Both forces are there whenever any force occurs. | Your foot pushes (action) and the ground pushes back (reaction).
They always have the same magnitude. | The force arrows are the same length.
They always act in opposite directions. | The force arrows point in opposite directions.
They always act on different objects. | Your foot and the ground.
Both are real forces and can cause a change in motion. | You move forward on your skateboard.

## Slide 13: Newton’s three laws of motion: summary

## Slide 14
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.