## Slide 1: PowerPoint 2: Types of force
PowerPoint presentation
7. Mechanical principles
7.1 Principles of motion and mechanics in engineering and manufacturing systems

## Slide 2: Objectives
By the end of this session, learners should be able to understand and explain the following types of force:
concurrent
non-concurrent
coplanar
non-contact.

## Slide 3: What is force?
When discussing mechanical principles it is important to understand some key definitions.
A force (F) is a push or a pull that acts on an object due to interaction with another object. Force is measured in newtons (N).
Energy is expressed as the amount of work done by a force. Energy cannot be created or destroyed, only converted from one form to another. The units of energy are joules (J).
Work done is the force × distance moved and is expressed in joules (J).
Power is defined as the amount of energy transferred per second, measured in watts (W).

## Slide 4: System of forces
In engineering, we are often dealing with complex machines or structures. In these settings, there is often more than one force in action at any one time.
When a number of forces act on a body (ie an object), they are called a force system or a system of forces.

## Slide 5: Types of force
You need to be aware of the following types of force:
non-contact
concurrent
non-concurrent
coplanar.

## Slide 6: Contact and non-contact forces
Contact forces act between two objects that are physically touching. Examples include:
  tension, friction, air resistance, normal reaction force.
Non-contact forces act between two objects that are not physically touching – they are forces acting at a distance. Examples include:
  magnetic force, electrostatic force, gravitational force, nuclear force.

## Slide 7: Contact and non-contact forces

## Slide 8: Concurrent forces
In a concurrent force system, all forces pass through one general point. If all the forces on an object act at one point, the resultant of these forces might or might not be zero. The forces could be tensile (pulling) or compressive (pushing).
If all the forces have the same line of action, then they are known as collinear whereas if the lines of action of the forces intersect at a single point, then they are known as concurrent.

## Slide 9: Non-concurrent forces
In a non-concurrent system, the lines of action of all the forces do not meet at one point.
This is shown here, where the lines of action of the forces on the object do not intersect at the same point.

## Slide 10: Coplanar forces
If a body (object) is acted on by several forces which all lie in the same plane, then the forces are said to be coplanar.
You may find it helpful to imagine the plane as a surface, such as a tabletop.
A system in which all the forces lie in the same plane is known as a coplanar force system. The forces in a coplanar force system can be collinear, concurrent, parallel, or non-concurrent and non-parallel.

## Slide 11: Example of non-concurrent coplanar forces
This picture shows coplanar forces, because all the forces in the system are in the same plane.
They are also non-concurrent as the lines of action of all of the forces do not meet at one point.
Points A, B, C and D are collinear (in the same line).

## Slide 12
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.