## Slide 1: PowerPoint 3: Simply supported beams
PowerPoint presentation
7. Mechanical principles
7.1 Principles of motion and mechanics in engineering and manufacturing systems

## Slide 2: Objectives
By the end of this session, learners should be able to explain the following principles in relation to simply supported beams:
  loading
  reaction forces
  loaded components
  shear force
  load distribution
  bending moments.

## Slide 3: What are beams?
A beam is a structural element that supports a load.
The simplest beam is rectangle in cross section, like a long plank of wood, supported at both ends.
The ends of a simply supported beam are held up by supports but are not connected to the supports.
The load is divided between the two supports – the load at each support is called the reaction force.

## Slide 4: Examples of simply supported beams
Typical practical applications of simply supported beams with point loadings include bridge girders, vehicle chassis, beams in buildings, post and lintel structures, beds of machinery and shelves.

## Slide 5: Force (action) and reaction
The downward force (action) is balanced by the left and right reactions.
On this beam the load is applied in just one place – this is called point loading.

## Slide 6: Reaction forces in simply supported beams
Total length of beam between supports, L = L1 + L2
R1 x L = F x L1, ie R1 = (F x L1) / L
R2 x L = F x L2, ie R2 = (F x L2) / L
R1 + R2 = F

## Slide 7: Example calculation
Calculate the reaction forces for the beam shown.
Answer
R1 x 2.0 = 200 x 1.5 = 300N; hence R1 = 300 / 2 = 150N
R2 x 2.0 = 200 x 0.5 = 100N; hence R2 = 100 / 2 = 500N

## Slide 8: Loaded components: point loading
Compression occurs at the top of the beam
Bending occurs along the beam depending on the distance of the force from the ends
Shearing occurs at the ends of the beam
Tension occurs at the bottom of the beam

## Slide 9: Shear force
Shear force is the force in the beam acting perpendicular to its longitudinal x-axis.
Shear force can be calculated and illustrated on a shear force diagram.

## Slide 10: Bending moments
The bending moment acting at a point on a beam is the resultant turning moment due to all the forces acting on one side of the point.
There are two types of bending moment:
sagging bending moments (positive)
hogging bending moments (negative).
Bending moments in the beam can be calculated and illustrated on a bending moment diagram.

## Slide 11: Uniformly distributed loading (UDL)
A beam loaded with concentrated point loads alone cannot exist, because the beam itself has mass and weight. In a beam of uniform cross-section, this represents a uniform load throughout the length of the beam. Here is a uniformly loaded beam of length (l) and weight per metre (W). The only point loads are the reactions at the supports RA and RB. Since the loading is symmetrical, RA and RB are equal:
RA

## Slide 12: UDL
Take a section XX at a distance from the left-hand support where RA acts.
The shearing force at XX = () ()

## Slide 13: Shear force diagram
The shear force diagram shows maximum values at the points of support and zero shear at the midpoint.
The line joining the shearing force is a sloping line passing through the midpoint.

## Slide 14: Bending moment
The bending moment diagram is a continuous curve with a maximum value at the midpoint.
The bending moment, , at XX =
Therefore: (l– 2)

## Slide 15: Combination of point and uniformly distributed loading
What tends to happen is a combination of point loads and uniform loading, as shown in the loading diagram (a).
Calculate the reactions and by taking moments about A:
(45×2) + (12×9) ×4.5 + (24×12) = 9
Thus, = 96kN and = 81kN
RC

## Slide 16: Combination of point and uniformly distributed loading
Shearing forces
(Let x be any distance from A):
For 0 ≤ x ≤ 2, shear force = (81 – 12x)kN
For 2 ≤ x ≤ 9, shear force = (81 – 12x – 45) = (36 –12x)kN
For 9 ≤ x ≤12, shear force = (81 – 12×9 – 45 + 96) = +24kN

## Slide 17: Combination of point and uniformly distributed loading
These results are shown by straight lines in the diagram.

## Slide 18
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.