## Slide 1: PowerPoint 5 : Work, energy and power
7. Mechanical principles
7.2 Principles of forces and energy

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the difference between mechanical work, energy and power
outline D’Alembert's principle.

## Slide 3: Work and mechanical energy
When a force acts on an object to cause a displacement of the object, it is said that work is done on the object.
work done = force ×distance moved in the direction of the force
Mechanical energy is the energy that is possessed by an object due to its motion or its position. Mechanical energy is the sum of the KE (energy of motion) and PE (stored energy of position) of an object. Energy is required to do work.
It should be noted that in practical applications energy can also be dynamically stored in flywheels, springs, objects raised to a height and pressurised fluids.

## Slide 4: Power
Power is the rate at which work is done or the rate at which energy is transferred. It is calculated using the equation:
power =
or
P =
The standard SI unit of power is the watt (W) which is equivalent to 1J/s.

## Slide 5: D’Alembert’s principle
D’Alembert’s principle, also known as the Lagrange–d’Alembert principle, is a statement of the fundamental classical laws of motion.
It is based on Newton’s second law:
It states that the sum of the differences between the forces exerted on a system of particles and the time derivatives of the momenta of the system is zero when the system is projected into virtual displacement. For a dynamic system, no work is done by the difference between exerted and inertial forces.
Alternatively, the reaction caused by the inertia of an accelerated body is equal and opposite to the force causing the acceleration.
Notes: You may wish to show the video here: https://youtu.be/WOHRp3V-QA0?t=363

## Slide 6: Example 1
Consider two teams playing tug-of-war. A box of mass m is attached to a rope at two opposite places. Team A pulls the box with force FA and Team B pulls it with force FB. The force of team A is greater, so the box is accelerated towards team A.
By D’Alembert’s principle: (FA − FB) − ma = 0

## Slide 7: Example 2
A box of mass m is placed on an inclined surface with a coefficient of friction µ, and it accelerates downwards.
By D’Alembert’s principle (along x-axis, ie parallel to the slope): (− F + mg sinθ) − ma = 0 − μ(mg cosθ) + mg sinθ − ma = 0

## Slide 8
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.